## Slide 1: CS 540 Computer Networks II
Sandy Wang
chwang_98@yahoo.com
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2
6. Routing Protocols – ISIS
Notes: In this chapter, we look at the underlying technology and protocol architecture
of LANs. Chapters 12 and 13 are devoted to a discussion of specific
LAN systems.

## Slide 3: Topics
  Overview
  LAN Switching
  IPv4
  IPv6
  Tunnels
  Routing Protocols -- RIP, RIPng, OSPF
  Routing Protocols -- ISIS, BGP
  Midterm Exam
  MPLS
  Transport Layer -- TCP/UDP
  Congestion Control & Quality of Service (QoS)
  Access Control List (ACL)
  Application Layer Protocols
  Application Layer Protocols continue
  Final Exam

## Slide 4: Reference Books
Cisco CCNA Routing and Switching ICND2 200-101 Official Cert Guide, Academic Edition by Wendel Odom -- July 10, 2013. ISBN-13: 978-1587144882
The TCP/IP Guide: A Comprehensive, Illustrated Internet Protocols Reference by Charles M. Kozierok – October 1, 2005. ISBN-13: 978-1593270476
Data and Computer Communications (10th Edition) (William Stallings Books on Computer and Data Communications) by Williams Stallings – September 23, 2013. ISBN-13: 978-0133506488
http://class.svuca.edu/~sandy/class/CS540/

## Slide 5: Interior and Exterior Gateway Protocols
Note: IGRP and EIGRP are Cisco proprietary protocols. They are meant as an alternative between the limited RIP routing protocol and the more complicated and resource intensive OSPF and IS-IS routing protocols. IGRP was discontinued with IOS 12.2 in 2005.
The dates shown are when the RFC or other document was finalized. The protocol may have been implemented earlier than this date.
 | Interior Gateway Protocols |  |  |  | Exterior Gateway Protocols
 | Distance Vector Routing Protocols |  | Link State Routing Protocols |  | Path Vector
Classful | RIPv1 (1982/1988) | IGRP (1985) |  |  | EGP (1982)
Classless | RIPv2 (1994) | EIGRP (1992) | OSPFv2 (1991) | IS-IS (1990) | BGPv4 (1995)
IPv6 | RIPng (1997) | EIGRP for IPv6 (not yet released) | OSPFv3 (1999) | IS-IS for IPv6 (2000) | BGPv4 for IPv6 (1999)

## Slide 6: History
IS-IS: Intermediate System to Intermediate System
Described in ISO 10589, 1992
First production developed by Digital Equipment Corporation
Integrated IS-IS was proposed RFC 1195. Routing both ISO’s Connectionless-Mode Network Service (CLNS) and IP.

## Slide 7: Similarities between OSPF & IS-IS
Link-state routing protocol and use a Dijkstra-based SPF algorithm to calculate shortest-path tree
Hellos to maintain adjacencies
Hierarchical
Provide address summarization
Classless
Elect Designated Router for broadcast networks
Authentication Capabilities

## Slide 8: IS-IS versus OSPF - Terminology
IS-IS | OSPF | Comments
ES (End System) | Host | 
IS (Intermediate System) | Router | 
Circuit | Link | 
SNPA (Subnetwork Point of Attachment) | Datalink Address | 
PDU (Protocol Data Unit) | Packet | 
DIS (Designated Intermediate System) | DR (Designated Router) | 
N/A | BDR | 
IIH (IS-to-IS Hello Packet) | Hello packet | 

## Slide 9: IS-IS versus OSPF - Terminology
IS-IS | OSPF | Comments
LSP (Link-State Packet) | LSA (Link -State Advertisement) | LSAs are actually comparable to TLVs used in LSPs.
CSNP (Complete Sequence Number PDU or Packet) | DBD (Data Base Description Packet) | 
PSNP (Partial Sequence Number PDU or Packet) | LSAck or LSR (Link State Request) | 
Routing Domain | AS | The term routing domain is also used with OSPF.
Level 1 Area | Area (non-backbone) | 
Level 2 Area | Backbone area (Area 0) | IS-IS uses a backbone path connected by contiguous L2 routers. There is no backbone area in IS-IS

## Slide 10: IS-IS versus OSPF – ISs (Routers)
IS-IS | OSPF | Comments
Level 1 IS (router) | Internal Non-backbone Router | Internal, non-backbone router in a Totally Stubby Area
Level 2 IS (router) | Internal Backbone Router or ASBR | Any Level 2 router can distribute externals into the domain. No special name. (Cisco IOS allows Level 1 routers to distribute externals.)
Level 1-2 IS (router) | ABR | 
System ID | Router ID | The System ID is the key for SPF calculations. Sometimes the NET address is thought of as the Router ID.
AFI = 49 | RFC 1918 Addresses | AFI is part of the NSAP.

## Slide 11: IS-IS versus OSPF - Timers
Interface | IS-IS | OSPF
Point-to-Point | Hello – 10 sec Holdtime – 30 sec | Hello – 10 sec Dead – 40 sec
Broadcast | Hello – 10 sec Holdtime – 30 sec | Hello – 10 sec Dead – 40 sec
NBMA | N/A | Hello – 30 sec Dead – 120 sec
Other | IS-IS | OSPF
LS Aging | 1,200 sec or 20 min (counts down) | 3,600 sec or 60 min (counts up)
LS Refresh | Every 15 min | Every 30 min
NBMA | N/A | Hello – 30 sec Dead – 120 sec
SPF Delay/Holdtime | 5.5 sec / 10 sec | 5 sec / 10 sec

## Slide 12: Level 1 Router
Level 1 IS (L1 IS, router)
  Analogous to OSPF Internal non-backbone router (Totally Stubby)
  Responsible for only routing to ESs inside an area.
Level 1 routers maintain the Level 1 database for the area and exit points to neighboring areas.
Notes: Level 1 IS (L1 IS, router)
  Analogous to OSPF Internal non-backbone router (Totally Stubby)
  Responsible for routing to ESs inside an area.
A contiguous group of Level 1 routers define an area.
Level 1 routers maintain the Level 1 database for the area and exit points to neighboring areas.

## Slide 13: Level 2 Router
Level 2 IS (L2 IS, router)
  Analogous to OSPF Internal Backbone router
  Responsible for routing between areas
Also referred to as area routers.
Interconnects the Level 1 areas
Store separate database of only inter-area topology
Notes: Level 2 IS (L2 IS, router)
  Analogous to OSPF Internal Backbone router
  Responsible for routing between areas
Also referred to as area routers.
Interconnect the Level 1 areas
Store separate database of only inter-area topology
All interfaces in the same area

## Slide 14: Level 1 – Level 2 Router
Level 1 and Level 2 IS (L1-L2 IS, router)
  Analogous to OSPF ABR router
  Participate in both L1 intra-area routing and L2 inter-area routing.
Maintain both Level 1 and Level 2 LSDB
Support Level 1 function communicating with other Level 1 routers in their area
  Inform other Level 1 routers that they are the exit point (default route) from the area.
Support Level 2 function communicating with the rest of the backbone path.
Notes: Level 1 and Level 2 IS (L1-L2 IS, router)
  Analogous to OSPF ABR router
  Participate in both L1 intra-area routing and L2 inter-area routing.
Maintain both Level and Level 2 LSDB
Support Level 1 function communicating with other Level 1 routers in their area
  Inform other Level 1 routers that they are the exit point (default route) from the area.
Support Level 2 function communicating with the rest of the backbone path.
All interfaces in the same area

## Slide 15: IS-IS Backbone
IS-IS does not share the concept of a backbone area 0 with OSPF.
IS-IS backbone a set of distinct areas interconnected by a chain of Level 2 routers, weaving their way through and between the Level 1 Areas.
The IS-IS backbone (path) consists of a contiguous set of Level 1-2 and Level 2 routers.
Where is the backbone (path)?
Notes: IS-IS does not share the concept of a backbone area 0 with OSPF.
An IS-IS backbone can appear as a set of distinct areas interconnected by a chain of Level 2 routers, weaving their way through and between the Level 1 Areas.
The IS-IS backbone (path) consists of a contiguous set of Level 1-2 and Level 2 routers.
Where is the backbone (path)?

## Slide 16: ISO Addressing
NSAP (Area, System ID, NSEL)
SNAP

## Slide 17: ISO Address
IS-IS uses OSI network layer addressing: 8 to 20 bytes
Network Entity Title (NET) Described in ISO 8348
A variety of NSAP formats exist, which we will not go into.
Represented in hexadecimal (up to 40 hex digits)
Cisco format: Area – System ID – NSEL (always 00 on ISs)
49.0001.2222.2222.2222.00
NSAP
Notes: OSI network layer addressing is done through the NSAP (Network Service Access Point) consisting of:
  OSI Address of the device
  OSI network services provided to the transport layer
  Conceptual boundary between network and transport layers
A variety of NSAP formats exist, which we will not go into.
Represented in hexadecimal (up to 40 hex digits)
Cisco format: Area – System ID – NSEL (always 00 on ISs)
49.0001.2222.2222.2222.00

## Slide 18: OSI Addressing
(a) Simple Area ID/System ID Format
(b) An OSI NSAP Format
(c) a GOSIP NSAP Format (Government Open System Interconnection Profile)
  AFI – Authority and Format identifier
  ICD – International Code Designator
  DFI – Domain Specific Part (DSP) Format identifier
  AAI – Administrative Authority identifier
  RDI – Routing Domain Identifier (Autonomous system number)
  SEL: Network Service Access Point (NSAP) Selector
NSAP
Notes: OSI network layer addressing is done through the NSAP (Network Service Access Point) consisting of:
  OSI Address of the device
  OSI network services provided to the transport layer
  Conceptual boundary between network and transport layers
A variety of NSAP formats exist, which we will not go into.
Represented in hexadecimal (up to 40 hex digits)
Cisco format: Area – System ID – NSEL (always 00 on ISs)
49.0001.2222.2222.2222.00

## Slide 19: OSI Addressing
Must begin with single octet (47.xxxx….)
Must end with single octet
NSAP
Notes: OSI network layer addressing is done through the NSAP (Network Service Access Point) consisting of:
  OSI Address of the device
  OSI network services provided to the transport layer
  Conceptual boundary between network and transport layers
A variety of NSAP formats exist, which we will not go into.
Represented in hexadecimal (up to 40 hex digits)
Cisco format: Area – System ID – NSEL (always 00 on ISs)
49.0001.2222.2222.2222.00

## Slide 20: NSAPs
Format of the Cisco NSAP address consists of three parts.
  Area address
  System ID
  NSAP selector byte
Area address is a variable length field
The system ID is the ES or IS identifier in an area, similar to the OSPF router ID.
  The system ID has a fixed length of six bytes as engineered in the Cisco IOS.
The NSAP selector byte is a service identifier.
  Analogous to that of a port or socket in TCP/IP.
Notes: Format of the Cisco NSAP address consists of three parts.
  Area address
  System ID
  NSAP selector byte
Area address is a variable length field
The system ID is the ES or IS identifier in an area, similar to the OSPF router ID.
  The system ID has a fixed length of six bytes as engineered in the Cisco IOS.
The NSAP selector byte is a service identifier.
  Analogous to that of a port or socket in TCP/IP.

## Slide 21: NSAPs – Cisco Format
Area
Addresses starting with 49 (AFI=49) are considered private IP address, analogous to RFC 1918.
  Routed by IS-IS
  Should not be advertised to other CLNS networks (outside this IS-IS domain)
Additional 2 bytes (0001) added for the area ID
All routers in the same are must have the same area address
Area – System ID – NSEL 49.0001.2222.2222.2222.00
Notes: Area
Addresses starting with 49 (AFI=49) are considered private IP address, analogous to RFC 1918.
  Routed by IS-IS
  Should not be advertised to other CLNS networks (outside this IS-IS domain)
Additional 2 bytes (HODSP) added for the area ID
All routers in the same are must have the same area address

## Slide 22: NSAPs – Cisco Format
System ID
Cisco fixes the System ID at 6 bytes.
Customary to use one of the following:
  MAC address from the router
  IP address of loopback interface
    192.168.111.3 -> 192.168.111.003 -> 1921.6811.1003
Each device (IS and ES) must have a unique System ID within the area. (Recommended to make them unique within the domain.)
Area – System ID – NSEL 49.0001.2222.2222.2222.00
Notes: System ID
OSI requires it must be the same number of bytes throughout the domain.
Cisco fixes the System ID at 6 bytes.
Customary to use one of the following:
  MAC address from the router
  IP address of loopback interface
    192.168.111.3 -> 192.168.111.003 -> 1921.6811.1003
Each device (IS and ES) must have a unique System ID within the area. (Recommended to make them unique within the domain.)

## Slide 23: NSAPs – Cisco Format
NSEL (NSAP Selector)
NSEL is a service identifier.
Loosely equivalent to that of a port or socket in TCP/IP.
Not used in routing decisions.
NET (Network Entity Title)
When NSEL = 00, it identifies the device itself, the network level address.
The NSAP with a NSEL = 00 is known as a Network Entity Title (NET)
  A NET is an NSAP with the NSEL set to (00)
Area – System ID – NSEL 49.0001.2222.2222.2222.00
Notes: NSEL (NSAP Selector)
NSEL is a service identifier.
Loosely equivalent to that of a port or socket in TCP/IP.
Must be specified by a single byte preceded by a period (.)
Not used in routing decisions.
NET
When NSEL = 00, it identifies the device itself, the network level address.
The NSAP with a NSEL = 00 is known as a Network Entity Title (NET)
A NET is an NSAP with the NSEL set to (00)

## Slide 24: NSAP (NETs)
Example 1: NSAP 47.0001.aaaa.bbbb.cccc.00
Area ID is:
  47.0001
System ID is:
  aaaa.bbbb.cccc
NSAP selector byte is:
  00
Example 2: NSAP 39.0f01.0002.0000.0c00.1111.00
Area ID is:
  39.0f01.0002
System ID is:
  0000.0c00.1111
NSAP selector byte is:
  00
Other Examples
Area – System ID – NSEL 49.0001.2222.2222.2222.00
Notes: Example 1: NSAP 47.0001.aaaa.bbbb.cccc.00
Area ID is 47.0001
System ID is aaaa.bbbb.cccc
NSAP selector byte is 00
Example 2: NSAP 39.0f01.0002.0000.0c00.1111.00
Area ID is 39.0f01.0002
System ID is 0000.0c00.1111
NSAP selector byte is 00

## Slide 25: Configuring IS-IS (so far)
ip router isis: IS-IS must be enabled on the interface
Note: IS-IS routing cannot be enabled on an interface until an IP address has been configured on the interface.
IOS: Cisco IOS 12.2(12) with Enterprise Plus (16 MB Flash/48 MB RAM) or Enter Plus IPSec56 (16 MB Flash/64 MB RAM)
SanJose1
interface FastEthernet0/0
ip address 172.16.0.1 255.255.255.0
ip router isis
isis priority 100
router isis
net 49.0001.1111.1111.1111.00
SanJose2
interface FastEthernet0/0
ip address 172.16.0.2 255.255.255.0
ip router isis
router isis
net 49.0001.2222.2222.2222.00
Area . System ID . NSEL
SanJose3
interface FastEthernet0/0
ip address 172.16.0.3 255.255.255.0
ip router isis
router isis
net 49.0001.3333.3333.3333.00
Area 49.0001
Notes: ip router isis: IS-IS must be enabled on the interface
IOS: Cisco IOS 12.2(12) with Enterprise Plus (16 MB Flash/48 MB RAM) or Enter Plus IPSec56 (16 MB Flash/64 MB RAM)
Note: IS-IS routing cannot be enabled on an interface until an IP address has been configured on the interface.

## Slide 26: Configuring IS-IS (so far)
To display both ES and IS neighbors.
SNPA (Subnetwork Point of Attachment) address is the interface circuit ID.
  Ethernet: MAC address of the remote router.
  Serial, would show encapsulation, I.e. HDLC
Type: Cisco routers default to L1-L2 type routers.
  We will see how to change this in a moment.
Area 49.0001
Notes: To display both ES and IS neighbors.
SNPA is the MAC address of the remote router.
  If serial, would show encapsulation, I.e. HDLC
Cisco routers default to L1-L2 type routers.
We will see how to change this in a moment.

## Slide 27: Hello Messages
IS-IS uses Hello PDUs to establish adjacencies with other routers
L1-only routers and L1/L2 routers  L1 adjacency
L2-only routers and L1/L2 routers  L2 adjacency
L1-only and L2-only routers  No adjacency
Rules:
  Two L1-only routers form an L1 adjacency only if their AIDs match
  Two L2-only routers from an L2 adjacency, even if their AIDs are different
  An L1-only router forms an L1 adjacency with an L1/L2 router only if their AIDs match
  An L2-only router forms an L2 adjacency with an L1/L2 router even if their AIDs are different
  Two L1/L2 routers form both L1 and L2 adjacencies if their AIDs match
  Two L1/L2 routers form only and L2 adjacency if their AIDs do not match
Notes: IS-IS uses Hello PDUs to establish adjacencies with other routers (ISs) and ESs.
IS-IS has three types of Hello PDUs:
  ESH, sent by ES to an IS
  ISH, sent by IS to an ES
  IIH, used between two ISs (CCNP 1)
    Hello Level 1 LAN
    Hello Level 2 LAN
    Hello Point-to-Point
In OSI there are only two main types of physical links:
  Broadcast: Multiaccess media types, usually LANs
  Nonbroadcast: Point-to-Point, Multipoint, and dynamically established links (WAN links)
Thus, IS-IS supports only two media representations:
  Broadcast for LANs
  Point-to-Point for all other media
IS-IS has no concept of an NBMA network.
  Recommended that point-to-point links be used for native ATM, Frame Relay, or X.25

## Slide 28: Adjacencies
L1 routers form L1 adjacencies with L1 and L1-L2 routers in their area.
L2 routers form L2 adjacencies with L2 and L1-L2 routers in their area or another area.
L1 router does not form an adjacency with an L2 router
LAN Adjacencies
Notes: L1 routers form L1 adjacencies with L1 and L1-L2 routers in their area.
L2 routers form L2 adjacencies with L2 and L1-L2 routers in their area or another area.
L1L2 routers form L1 and L2 adjacencies with each other in their area or another area.
L1 router does not form an adjacency with an L2 router

## Slide 29: Level 1 and Level 2 Adjacencies
L1/L2
L1
L1
L1/L2
L2
L1/L2
L1
L1
L1/L2
L2
Level 1 Adjacencies
L1/L2
L1
L1
L1/L2
L2
Level 2 Adjacencies

## Slide 30: Neighbors and Adjacencies
IS-IS discover neighbors and forms adjacencies using IS-IS Hello PDUs.
  Transmitted every 10 seconds
  Can be changed using the interface command, is hello-interval
Hold time defaults to 3 times the Hello time (30 seconds), before declaring a neighbor dead.
  Changed using the interface command is hello-multiplier
  Default is 3
Notes: IS-IS discover neighbors and forms adjacencies using IS-IS Hello PDUs.
Transmitted every 10 seconds
Can be changed using the interface command, is hello-interval
Hold time defaults to 3 times the Hello time (30 seconds), before declaring a neighbor dead.
  Changed using the interface command is hello-multiplier
  Default is 3

## Slide 31: LAN Representation and Adjacencies
Similar to the DR in OSPF…
DIS (Designated IS) is elected to generate the LSP (Link State Packet, ie. LSA) representing the virtual router connecting all attached routers to a star-shaped topology
LAN uses a virtual node called pseudo node.
  Represents the LAN
  Sent by the DIS
DIS
Notes: Similar to the DR in OSPF…
DIS (Designated IS) is elected to generate the LSP (Link State Packet, ie. LSA) representing the virtual router connecting all attached routers to a star-shaped topology
For SPF, the whole network must look like a collection of nodes and point-to-point links
  Multi-access networks are different
LAN uses a virtual node called pseudonode.
  Represents the LAN
  Sent by the DIS

## Slide 32: LAN Representation and Adjacencies
Election of DIS:
  Router with highest priority (in the range of 0-127, Cisco default is 64)
  Router with highest MAC address
No Backup DIS
No way to make a router ineligible from being DIS (no OSPF priority 0)
New router (IS) can cause a new election, unlike OSPF
Periodically broadcasts CSNPs (OSPF DBD) every 10 seconds
Elect both L1 and L2 DISs
DIS
Notes: Election of DIS:
  Router with highest priority (Cisco default is 64)
  Router with highest MAC address
No “BDR”
No way to make a router ineligible from being DIS (no OSPF priority 0)
New router (IS) can cause a new election, unlike OSPF
Periodically broadcasts CSNPs (OSPF DBD) every 10 seconds
Frame Relay: DIS is highest local DLCI if priorities are equal

## Slide 33: Configuring IS-IS (so far)
isis priority: Sets DIS priority on a LAN interface, default 64
SanJose1
interface FastEthernet0/0
ip address 172.16.0.1 255.255.255.0
ip router isis
isis priority 100
router isis
net 49.0001.1111.1111.1111.00
SanJose2
interface FastEthernet0/0
ip address 172.16.0.2 255.255.255.0
ip router isis
router isis
net 49.0001.2222.2222.2222.00
Area . System ID . NSEL
SanJose3
interface FastEthernet0/0
ip address 172.16.0.3 255.255.255.0
ip router isis
router isis
net 49.0001.3333.3333.3333.00
Area 49.0001
DIS
Notes: isis priority: Sets DIS priority on a LAN interface, default 64

## Slide 34: IS-IS Routing Process
IS-IS Routing Process is divided into four stages:
  Update
  Decision
  Forwarding
  Receive
Notes: IS-IS Routing Process is divided into four stages:
  Update
  Decision
  Forwarding
  Receive

## Slide 35: IS-IS Routing Process: Update
The Update Process
Routers can only forward data packets if they have an understanding of the network topology.
LSPs are generated and flooded throughout the network whenever:
  An adjacency comes up or down (example: a new router comes online).
  An interface on a router changes state or is assigned a new metric.
  An IP route changes (example: because of redistribution)
Notes: The Update Process
Routers can only forward data packets if they have an understanding of the network topology.
LSPs are generated and flooded throughout the network whenever:
  An adjacency comes up or down (example: a new router comes online).
  An interface on a router changes state or is assigned a new metric.
  An IP route changes (example: because of redistribution)

## Slide 36: IS-IS Routing Process: Update
Sending and Receiving an LSP
Receiving an LSP
  If the LSP is already present in the database (LSDB), the router (IS) acknowledges (PSNP) and ignores it.
    The router sends the duplicated LSP it its neighbors.
    Level 1 LSPs are flooded throughout the area
    Level 2 LSPs are sent across all L2 adjacencies.
Notes: Sending and Receiving an LSP
Receiving an LSP
  If the LSP is already present in the database (LSDB), the router (IS) acknowledges (PSNP) and ignores it.
    The router sends the duplicated LSP it its neighbors.
    Level 1 LSPs are flooded throughout the area
    Level 2 LSPs are sent across all L2 adjacencies.

## Slide 37: LSDB Synchronization and Update Process
IS-IS LSDB is accomplished by using special PDUs, known as SNPs (Sequence Number PDUs):
  CSNP (Complete Sequence Number PDU) – (OSPF: DBD)
    List of LSPs held by the router
  PSNP (Partial Sequence Number PDU) – (OSPF: LSAck/LSR)
    Acknowledge the receipt of a LSP
    Request a complete LSP for a missing entry
X
LSP (LSA)
PSNP (LSAck)
LSP (LSA)
LSP (LSA)
PSNP (LSAck)
PSNP (LSAck)
Notes: IS-IS LSDB is accomplished by using special PDUs, known as SNPs (Sequence Number PDUs):
  CSNP (Complete Sequence Number PDU) – (OSPF: DBD)
    List of LSPs held by the router
  PSNP (Partial Sequence Number PDU) – (OSPF: LSAck/LSR)
    Acknowledge the receipt of a LSP
    Request a complete LSP for a missing entry

## Slide 38: Update Process
Point-to-Point networks:
  Once an LSP is sent, router sets a timer (minimumLSPTransmissionInterval) of 5 seconds
  If PSNP (ACK) not received, resends LSP.
Notes: Point-to-Point networks:
  Once an LSP is sent, router sets a timer (minimumLSPTransmissionInterval) of 5 seconds
  If PSNP (ACK) not received, resends LSP.

## Slide 39: IS-IS Routing Process: Update
Sending and Receiving an LSP:
Propagating (sending) LSPs on a Point-to-Point Interface
  When an adjacency is established both routers send a CSNP (OSPF DBD) summary of their LSDB.
  If the receiving router has any LSPs that were not present in the CSNP it received, it sends a copy of the missing LSP to the other router.
CSNP
CSNP
You are missing LSP 3
LSP 3
PSNP (Ack)
Notes: Sending and Receiving an LSP:
Propagating (sending) LSPs on a Point-to-Point Interface
  When an adjacency is established both routers send a CSNP (OSPF DBD) summary of their LSDB.
  If the receiving router has any LSPs that were not present in the CSNP it received, it sends a copy of the missing LSP to the other router.

## Slide 40: IS-IS Routing Process: Update
Sending and Receiving an LSP:
Propagating (sending) LSPs on a Point-to-Point Interface
  Likewise, if the receiving router is missing any LSPs received in the CSNP, the receiving router sends a PSNP (OSPF LSR) requesting the full LSP to be sent.
  LSPs are acknowledges with a PSNP (OSPF LSAck)
  When the LSP is sent, the router sets a timer.
    If the acknolwedgement (PSNP) is not received within 5 seconds (Cisco default), the LSP is resent.
CSNP
CSNP
I am missing LSP 3
LSP 3
PSNP (Ack)
PSNP 3
Notes: Sending and Receiving an LSP:
Propagating (sending) LSPs on a Point-to-Point Interface
  Likewise, if the receiving router is missing any LSPs received in the CSNP, the receiving router sends a PSNP (OSPF LSR) requesting the full LSP to be sent.
  LSPs are acknowledges with a PSNP (OSPF LSAck)
  When the LSP is sent, the router sets a timer.
    If the acknolwedgement (PSNP) is not received within 5 seconds (Cisco default), the LSP is resent.

## Slide 41: IS-IS Routing Process: Update
Sending and Receiving an LSP:
Propagating (sending) LSPs on a Broadcast Interface
  The DIS (OSPF DR) takes on much of the responsibility for synchronizing the databases on behalf of the pseudo node.
  LSPs are not acknowledged by each receving router
  DIS periodically multicast a CSNP that describes every LSP in the LSDB
  DIS has three tasks:
    Creating and maintaining adjacencies
    Creating and updating the pseudonode LSP
    Flooding the LSPs over the LAN.
Notes: Sending and Receiving an LSP:
Propagating (sending) LSPs on a Broadcast Interface
  The DIS (OSPF DR) takes on much of the responsibility for synchronizing the databases on behalf of the pseudonode.
  DIS has three tasks:
    Creating and maintaining adjacencies
    Creating and updating the pseudonode LSP
    Flooding the LSPs over the LAN.

## Slide 42: Update Process
On Broadcast networks:
  LSPs are not acknowledged by each receiving router.
  DIS periodically multicasts a CSNP (OSPF DBD) that describes every LSP in LSDB.
    Default is every10 seconds
  L1 CSNPs are multicast to AllL1ISs
  L2 CSNPs are multicast to AllL2ISs
PSNP (OSPF LSR) goes to DIS.
III. LSP 77 is sent by DIS to R1
CSNP (DBD)
PSNP (LSR)
LSP 77 (LSA)
PSNP (LSAck)
Notes: On Broadcast networks:
  LSPs are not acknowledged by each receiving router.
  DIS periodically multicasts a CSNP (OSPF DBD) that describes every LSP in LSDB.
    Default is every10 seconds
  L1 CSNPs are multicast to AllL1ISs
  L2 CSNPs are multicast to AllL2ISs

## Slide 43: IS-IS Routing Process: Update
CSNP (DBD)
LSP 88
Sending and Receiving an LSP:
Propagating (sending) LSPs on a Broadcast Interface
  On receiving a CSNP the router compares it with its LSDB…
  If the receiving router has a newer version of the LSP then what was sent in the CSNP, or if the CSNP did not contain one of its LSPs, the router multicasts the LSP to all routers on the LAN.
I have a newer version of LSP 88
Receipt of LSP 88 is acknowledged by all routers with a PSNP.
Notes: Sending and Receiving an LSP:
Propagating (sending) LSPs on a Broadcast Interface
  On receiving a CSNP the router compares it with its LSDB…
  If the receiving router has a newer version of the LSP then what was sent in the CSNP, or if the CSNP did not contain one of its LSPs, the router multicasts the LSP to all routers on the LAN

## Slide 44: IS-IS Routing Process: Update
CSNP (DBD)
PSNP (LSR)
LSP 77 (LSA)
PSNP (LSAck)
Sending and Receiving an LSP:
Propagating (sending) LSPs on a Broadcast Interface
  On receiving a CSNP the router compares it with its LSDB…
  If the database is missing an LSP that was in the CSNP, it sends a PSNP requesting the full LSP.
  The DIS sends the LSP.
Notes: Sending and Receiving an LSP:
Propagating (sending) LSPs on a Broadcast Interface
  On receiving a CSNP the router compares it with its LSDB…
  If the database is missing an LSP that was in the CSNP, it sends a PSNP requesting the full LSP.
  The DIS sends the LSP.

## Slide 45: IS-IS Routing Process: Update
Determining if an LSP is valid:
  Receiving router uses three fields to help determine if the received LSP is more recent than the one in its LSDB.
  Remaining Lifetime
    Used to age-out or delete LSPs
    Lifetime is set to 0 and flooded
    Receiving routers recognize this means the route is bad and deletes the LSP from their LSDB, rerunning SPF algorithm, new SPT, new routing table.
    Note: LSPs have a maximum age of 20 minutes in an IS-IS LSDB (can be increased to 65535 seconds, ~18.2 hours), and are re-flooded (refreshed) every 15 minutes.
    Expired LSP will be kept in the LSDB for 60 seconds (ZeroAgeLifetime)
  Sequence Number
    First LSP starts with a sequence number of 1, with following LSPs incremented by 1.
    When sequence number reaches maximum (0xffffffff), the IS-IS process shuts down for 21 minutes (MaxAge + ZeroAgeLifetime) to allow old LSPs to age out
  Checksum
    If received LSP’s checksum does not computer correctly, the LSP is flushed and the lifetime set to 0.
    The receiving router floods the LSP with the lifetime set to 0.
    When the originating router gets this LSP (lifetime = 0) it retransmits a new LSP.
Notes: Determining if an LSP is valid:
  Receiving router uses three fields to help determine if the received LSP is more recent than the one in its LSDB.
  Remaining Lifetime
    Used to age-out or delete LSPs
    Lifetime is set to 0 and flooded
    Receiving routers recognize this means the route is bad and deletes the LSP from their LSDB, rerunning SPF algorithm, new SPT, new routing table.
    Note: LSPs have a maximum age of 20 minutes in an IS-IS LSDB, and are re-flooded (refreshed) every 15 minutes.
  Sequence Number
    First LSP starts with a sequence number of 1, with following LSPs incremented by 1.
  Checksum
    If received LSP’s checksum does not computer correctly, the LSP is flushed and the lifetime set to 0.
    The receiving router floods the LSP with the lifetime set to 0.
    When the originating router gets this LSP (lifetime = 0) it retransmits a new LSP.

## Slide 46: IS-IS Routing Process: Decision
IS-IS Routing Process is divided into four stages:
  Update
  Decision
  Forwarding
  Receive
Notes: IS-IS Routing Process is divided into four stages:
  Update
  Decision
  Forwarding
  Receive

## Slide 47: IS-IS Routing Process: Decision
The Decision Process
  Uses Dijkstra’s algorithm to build a SPT (Shortest Path Tree)
  The SPT is used to create the forwarding table, also known as the routing table.
  Several tables are used during this process:
    PATH table
      PATH table is the SPT during the construction of the LSDB
      Each candidate route is placed in the PATH table while the metric is examined to determine if it is the shortest path to the destination.
    TENT is the tentative database (a scratchpad) during this process
Notes: The Decision Process
  Uses Dijkstra’s algorithm to build a SPT (Shortest Path Tree)
  The SPT is used to create the forwarding table, also known as the routing table.
  Several tables are used during this process:
    PATH table
      PATH table is the SPT during the construction of the LSDB
      Each candidate route is placed in the PATH table while the metric is examined to determine if it is the shortest path to the destination.
    TENT is the tentative database (a scratchpad) during this process

## Slide 48: IS-IS Metrics
Specified in ISO 10589
  Default – Must be supported
  Delay – Optional. Reflect the transit delay of a subnetwork
  Expense – Optional. Reflect the monetary cost of using the subnetwork
  Error – Optional. Reflect the residual error probability of the subnetwork.
  Cisco only supports the default metric

## Slide 49: IS-IS Routing Process: Decision
Determining the best route
Criteria by which the lowest cost paths are selected and placed in the forwarding database are:
  Internal paths are chosen before external paths outside the routing domain, to prevent sub-optimal routes and routing loops.
  Level 1 paths within the area are “more attractive” than Level 2 paths outside the area, to prevent sub-optimal routes and routing loops.
  If there is no path, the forwarding database sends the packet to the nearest Level 2 router, which is the default router.
Notes: Determining the best route
Criteria by which the lowest cost paths are selected and placed in the forwarding database are:
  Cisco allows up to six equal-cost paths, four by default.
  Cisco only supports the default metric
  Internal paths are chosen before external paths outside the routing domain, to prevent sub-optimal routes and routing loops.
  Level 1 paths within the area are “more attractive” than Level 2 paths outside the area, to prevent sub-optimal routes and routing loops.
  Longest match or most specific address in IP ensures that the closest router is chosen.
  ToS (Type of Service) in IP header is used, if configured.
  If there is no path, the forwarding database sends the packet to the nearest Level 2 router, which is the default router.

## Slide 50: IS-IS Routing Process: Forwarding
IS-IS Routing Process is divided into four stages:
  Update
  Decision
  Forwarding
  Receive
Notes: IS-IS Routing Process is divided into four stages:
  Update
  Decision
  Forwarding
  Receive

## Slide 51: IS-IS Routing Process: Forwarding and Receiving
Forwarding process
  After the SPT has been built the forwarding database can be created.
  The forwarding table is the lookup table for the longest match.
Receive process
  If the frame is valid, the receive process passes user data and error reports to the forwarding process.
  Whereas routing information: Hellos, LSPs, and SNPs are sent to the update process.

## Slide 52: Odds and Ends
L1L2 routers run two IS-IS processes, one for its L1 LSDB and another for its L2 LSDB.

## Slide 53: IS-IS Packet Format
MAC Hdr
IS-IS Hdr
IS-IS type-specific Data
MAC Header
  Src – MAC addr of sending interface
  Dst – 01-80-C2-00-00-14 for Level-1 ISs
  01-80-C2-00-00-15 for Level-2 ISs
  IEEE 802.2 LLC Frame format
IS-IS Header
  Intra-domain Routing Protocol Discriminator: 0x83
  Length – length of the header in bytes
  Version/Protocol ID: 1
  ID Length: length of the system ID
  PDU Type
  Version: always set to 1
  Max Area Addresses: # of area addresses permitted for this IS Area
Notes: 01:00:5E:00:00:00 - 01:00:5E:7F:FF:FF 0x0800 IPv4 Multicast (RFC 1112), insert the low 23 Bits of the multicast IPv4 Address into the Ethernet Address (RFC 7042 2.1.1.)
33:33:xx:xx:xx:xx 0x86DD IPv6 Multicast (RFC 2464), insert the low 32 Bits of the multicast IPv6 Address into the Ethernet Address (RFC 7042 2.3.1.)
224.0.0.5 The Open Shortest Path First (OSPF) All OSPF Routers address is used to send Hello packets to all OSPF routers on a network segment.
224.0.0.6 The OSPF All Designated Routers ""(DR)"" address is used to send OSPF routin`g information to designated routers on a network segment.

## Slide 54
0xFE
0xFE -- ISO Network Layer Protocol
0X03
0xFE

## Slide 55: IS-IS Header Format
Intradomain Routing Proto Discrminator
Length
Version/Protocol ID
Rsvd
PDU Type
Length – the length of the fixed header in octets
ID Length – the length of the System ID field. 0: 6 octets, 255: zero octet
Max Area addresses – the number of area address permitted for this IS area. In the range of 1-254, 0: 3 addresses
ID Length
Version
Reserved
Max Area Addresses
0X83
1
1-8, 255: Null System ID
1

## Slide 56: IS-IS PDU Types
IS-IS PDU Type | Value
Hello PDUs | 
Level 1 LAN Hellos | 15
Level 2 LAN Hello | 16
Point-to-point Hello | 17
Link State PDUs | 
Level 1 LSP | 18
Level 2 LSP | 20
Sequence Number PDUs | 
Level 1 CSNP | 24
Level 2 CSNP | 25
Level 1 PSNP | 26
Level 2 PSNP | 27

## Slide 57: Terminology
CLV (Code/Length/Value) and TLV (Type/Length/Value)
  Same thing, CLV is more of the OSI term.
  There are variable length fields in a PDU.
    Code or Type specifies the type of information.
    Length specifies the size of the Value field.
    Value is the information itself.
      Example CLV or TLV 128 defines the capability to carry IP routes in IS-IS packets, in essence TLV 128 is Integrated IS-IS.
Notes: CLV (Code/Length/Value) and TLV (Type/Length/Value)
  Same thing, CLV is more of the OSI term.
  There are variable length fields in a PDU.
    Code or Type specifies the type of information.
    Length specifies the size of the Value field.
    Value is the information itself.
      Example CLV or TLV 128 defines the capability to carry IP routes in IS-IS packets, in essence TLV 128 is Integrated IS-IS.

## Slide 58: IS-IS TLV Codes – Specified in ISO 10589
Type | TLV | Description
1 | Area Addresses | Area address of the originating IS
2 | IS Neighbors | List the originator’s IS-IS neighbors and the metrics
3 | ES Neighbors | Not relevant to IP routing
4 | Partition Designated Level 2 IS | Not supported
5 | Prefix Neighbors | Reachable address prefix neighbors
6 | IS Neighbors (Hellos) | System IDs of all neighbors whose Hellos have been heard within the last Hold time.
8 | Padding | Pad a Hello PDU to minimum 1492 bytes or the MTU
9 | LSP Entries | Summarize LSPs
10 | Authentication Information | Authentication type and information
14 | LSP Buffer size | The LSP buffer size of the originator
Value
Type
Length
1 byte
1 byte
length

## Slide 59: IS-IS TLV Codes – Specified in RFC 1195
Type | TLV | Description
128 | IP Internal Reachability Information | List IP addr/mask within the routing domain
129 | Protocols Supported | Protocols supported by the originator (v4, v6…)
130 | IP External Reachability Information | List IP addr/mask external to the routing domain
131 | Inter-Domain Routing Protocol Information | Carry information from external routing protocols transparently through the IS-IS domain
132 | IP Interface Address | IP address of the interface out which the PDU was sent
133 | Authentication Information | Authentication type and information
Value
Type
Length
1 byte
1 byte
length

## Slide 60: IS-IS TLV used in each PDU
Type | TLV | 15 | 16 | 17 | 18 | 20 | 24 | 25 | 26 | 27
 |  | Hello |  |  | LSP |  | Sequence # |  |  | 
1 | Area Addresses | X | X | X | X | X |  |  |  | 
2 | IS Neighbors |  |  |  | X | X |  |  |  | 
3 | ES Neighbors |  |  |  | X |  |  |  |  | 
4 | Partition Designated Level 2 IS |  |  |  |  | X |  |  |  | 
5 | Prefix Neighbors |  |  |  |  | X |  |  |  | 
6 | IS Neighbors (Hellos) | X | X |  |  |  |  |  |  | 
8 | Padding | X | X | X |  |  |  |  |  | 
9 | LSP Entries |  |  |  |  |  | X | X | X | X
10 | Authentication Information | X | X | X | X | X | X | X | X | X
128 | IP Internal Reachability Information |  |  |  | X | X |  |  |  | 
129 | Protocols Supported | X | X | X | X | X |  |  |  | 
130 | IP External Reachability Information |  |  |  | X | X |  |  |  | 
131 | Inter-Domain Routing Protocol Information |  |  |  |  | X |  |  |  | 
132 | IP Interface Address | X | X | X | X | X |  |  |  | 

## Slide 61: IS-IS TLV Codes – Extending Capabilities
Type | TLV | RFC | Description
12 | Optional Checksum | 3358 | Add checksum capability to SNPs
22 | Extended IS Reachability | 3784 | Add traffic engineering capabilities, replace type 2 TLV
134 | Traffic Engineering Router ID | 3784 | traffic engineering capabilities
135 | Extended IP Reachability | 3784 | traffic engineering capabilities, replace type 128 and 130 TLVs
137 | Dynamic Hostname | 2763 | Identified by hostname instead system ID
211 | Restart | 3847 | Graceful Restart
222 | MT Intermediate Systems | Draft | Multi-topology support
229 | Multi-Topology | Draft | Multi-topology support
232 | IPv6 Internet Address | Draft | Type 132 TLV equivalent
235 | MT Reachable IPv4 Prefixes | Draft | Multi-topology support
236 | IPv6 Reachability | Draft | Type 128, 130 TLV equivalent
237 | MT Reachable IPv6 Prefixes | Draft | Multi-topology support
240 | Point-to-point Three-way Adjacency | 3373 | 
250 | Experimental | Draft | 

## Slide 62: IS-IS Hello PDU Format
ID Length
Intra-domain Routing Proto Discriminator
Length
Version/Protocol ID
Rsvd
PDU Type
ID Length
Version
Reserved
Max Area Addresses
Rsvd
Circuit Type
Source ID
Holding Time
PDU Length
Priority
LAN ID
Rsvd
ID Length + 1
2
2
2
1
1
1
1
1
1
1
1
1

## Slide 63: Hello PDU Fields
Source ID – System ID of the router that originated the Hello
Holding Time – time should wait before declaring the originating router dead
PDU length – Length of the entire PDU
Priority – Used for electing DR. Range 0 – 127 with higher number means higher priority
LAN ID – System ID of the DR plus one more octet (the pseudo node ID)

## Slide 64: IS-IS Hello PDU Format – Point-to-point
ID Length
Intra-domain Routing Proto Discriminator
Length
Version/Protocol ID
Rsvd
PDU Type
ID Length
Version
Reserved
Max Area Addresses
Rsvd
Circuit Type
Source ID
Holding Time
PDU Length
Local Circuit ID
1
2
2
1
1
1
1
1
1
1
1
1
Local Circuit ID – Assigned by the originating router and is unique among the router’s interfaces

## Slide 65: IS-IS LSP PDU Format
2
Intra-domain Routing Proto Discriminator
Length
Version/Protocol ID
Rsvd
PDU Type
ID Length
Version
Reserved
Max Area Addresses
PDU Length
Remaining Life Time
LSP ID
Sequence number
4
2
ID Length + 2
1
1
1
1
1
1
1
1
Checksum
2
P
ATT
1
OL
IS Type
Notes: P – Partition bit : Partition repair capability. Not supported.
ATT – Attached bit : Used by L2 and L1/L2 routers to indicate they have route to another area.
OL – Overload bit : the originating router is experiencing a memory overload and has incomplete Link-State Database. Other routers still route packets to the overloaded router’s directly connected networks, but do not use the router for transit traffic.
LSP ID – the system ID, the pseudo node ID and the LSP number of the LSP

## Slide 66: IS-IS CSNP Format
2
Intra-domain Routing Proto Discriminator
Length
Version/Protocol ID
Rsvd
PDU Type
ID Length
Version
Reserved
Max Area Addresses
PDU Length
Source ID
Start LSP ID
End LSP ID
ID Length + 2
ID Length + 1
ID Length + 2
1
1
1
1
1
1
1
1

## Slide 67: IS-IS PSNP Format
2
Intra-domain Routing Proto Discriminator
Length
Version/Protocol ID
Rsvd
PDU Type
ID Length
Version
Reserved
Max Area Addresses
PDU Length
Source ID
ID Length + 1
1
1
1
1
1
1
1
1