## Slide 1: CS 540 Computer Networks II
Sandy Wang
chwang_98@yahoo.com
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2
MPLS
Notes: In this chapter, we look at the underlying technology and protocol architecture
of LANs. Chapters 12 and 13 are devoted to a discussion of specific
LAN systems.

## Slide 3: Topics
  Overview
  LAN Switching
  IPv4
  IPv6
  Tunnels
  Routing Protocols -- RIP, RIPng
  Routing Protocols -- OSPF
  IS-IS
  Midterm Exam
  BGP
  MPLS
  Transport Layer -- TCP/UDP
  Congestion Control & Quality of Service (QoS)
  Access Control List (ACL)
  Final Exam

## Slide 4: Reference Books
Cisco CCNA Routing and Switching ICND2 200-101 Official Cert Guide, Academic Edition by Wendel Odom -- July 10, 2013. ISBN-13: 978-1587144882
The TCP/IP Guide: A Comprehensive, Illustrated Internet Protocols Reference by Charles M. Kozierok – October 1, 2005. ISBN-13: 978-1593270476
Data and Computer Communications (10th Edition) (William Stallings Books on Computer and Data Communications) by Williams Stallings – September 23, 2013. ISBN-13: 978-0133506488
http://class.svuca.edu/~sandy/class/CS540/

## Slide 5: Agenda
Introduction to MPLS
LDP
MPLS VPN

## Slide 6: MPLS Concept
In Core:
  Forward using labels (as opposed to IP addr)
  Label indicates service class and destination
Label Switch Router (LSR)
Label Distribution Protocol (LDP)
Edge Label Switch Router
At Edge:
  Classify packets
  Label them
Notes: We’ve given you broad definitions of what MPLS does in the network. Now let’s discuss the essential concept of how MPLS actually works. Let’s start with terminology.
At the edge of the network, traffic is processed, classified, and given an MPLS label that determines how it will travel through the core to its final destination.
The core devices look at the label, make a switching decision, and sends the packet to the next stop. This is how ATM switches can act as routers, because all the decisions are made beforehand and stored in switching tables.

## Slide 7: Major RFCs
RFC 3031 -- Multiprotocol Label Switching Architecture
RFC 5036 -- LDP Specification

## Slide 8: MPLS concept
MPLS: Multi Protocol Label Switching
Packet forwarding is done based on Labels.
Labels are assigned when the packet enters into the network.
Labels are on top of the packet.
MPLS nodes forward packets/cells based on the label value (not on the IP information).

## Slide 9: MPLS concept
MPLS allows:
  Packet classification only where the packet enters the network.
  The packet classification is encoded as a label.
  In the core, packets are forwarded without having to re-classify them.
    No further packet analysis
    Label swapping

## Slide 10: Terminology
LDP – Label Distribution Protocol
LSP – Label-Switched Path
LSR – Label Switch Router
LIB -- Label Information Base
FEC -- Forwarding Equivalence Class
  A group of IP packets which are forwarded in the same manner
NHLFE -- Next Hop Label Forwarding Entry
  Contains the forwarding information
  the packet's next hop
  the operation to perform on the packet's label stack
    Swap, push. pop
Notes:   2. the operation to perform on the packet's label stack; this is one of the following operations:
  replace the label at the top of the label stack with a specified new label
  pop the label stack
  replace the label at the top of the label stack with a specified new label, and then push one or more specified new labels onto the label stack.
  It may also contain:
  the data link encapsulation to use when transmitting the packet
  the way to encode the label stack when transmitting the packet
  any other information needed in order to properly dispose of the packet.

## Slide 11: MPLS Operation
1a. Existing routing protocols (e.g. OSPF, IS-IS) establish reachability to destination networks.
1b. Label Distribution Protocol (LDP)
establishes label to destination network mappings.
2. Ingress Edge LSR receives packet, performs Layer 3 value-added services, and labels(PUSH) packets.
3. LSR switches packets using label swapping(SWAP) .
4. Edge LSR at egress removes(POP) label and delivers packet.
Notes: Here is how MPLS actually works.
Step 1A: a routing protocol such as OSPF, EIGRP, or IS-IS determines the layer 3 topology. A router builds a routing table as it “listens” to the network. A Cisco router or IP+ATM switch can have a routing function inside that does this. All devices in the network are building the layer 3 topology.
Step 1B: The Label Distribution Protocol establishes label values for each device according to the routing topology, to pre-configure maps to destination points. Unlike ATM PVCs where the VPI/VCIs are manually assigned, labels are assigned automatically by LDP.
Step 2: An ingress packet enters the Edge LSR. The LSR labels it, does all the layer 3 value-added services, including QoS, Bandwidth management, and so forth. It then applies a label to it based on the information in the forwarding tables. (This also reflects QoS, which we’ll discuss in detail in the next section).
Step 3: the core LSR read the labels on each packet on the ingress interface, and based on what the label says, sends the packet out the appropriate egress interface with a new label.
Step 4: the egress Edge LSR strips the label and sends the packet to its destination.

## Slide 12: Label Switch Path (LSP)
LSPs are derived from IGP routing information
LSPs may diverge from IGP shortest path
LSPs are unidirectional
    Return traffic takes another LSP
LSP follows IGP shortest path
LSP diverges from IGP shortest path
IGP domain with a label distribution protocol
IGP domain with a label distribution protocol

## Slide 13: Encapsulations
Label Header
MAC Header
Layer 3 Header
LAN MAC Label Header

## Slide 14: Label Header
Header= 4 bytes, Label = 20 bits.
Can be used over Ethernet, 802.3, or PPP links
Contains everything needed at forwarding time
Label = 20 bits EXP = Class of Service, 3 bits
S = Bottom of Stack, 1 bit TTL = Time to Live, 8 bits
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
Label
EXP
S
TTL
Notes: The tag frame encapsulation uses what’s called a shim header. It’s a header that sits between the MAC layer header and the layer 3 header in the packet. It consists of one or more entries that look like this.
Its a 32-bit word per entry which contains:
the tag your forwarding on
a 3-bit class of service field
an 8-bit time to live field, and
a 1-bit end of stack.
The end of stack is what allows you to determine when you’re popping a tag, whether this is the last tag on the packet, or whether there are further tags.

## Slide 15: Loops and TTL
TTL is decremented prior to enter the non-TTL capable LSP
    If TTL is 0 the packet is discarded at the ingress point
TTL is examined at the LSP exit
IGP domain with a label distribution protocol
LSR-1
LSR-2
LSR-4
LSR-5
LSR-3
LSR-6
Egress
IP packet TTL = 6
Label = 25
IP packet TTL = 6
IP packet TTL = 10
LSR-6 --> 25 Hops=4
IP packet TTL = 6
Label = 39
IP packet TTL = 6
Label = 21

## Slide 16: Label Assignment and Distribution
Labels have link-local significance:
    Each LSR binds his own label mappings
Each LSR assign labels to his FECs
Labels are assigned and exchanged between adjacent LSR

## Slide 17: Label Assignment and Distribution
Rtr-C is the downstream neighbor of Rtr-B for destination 171.68.10.0/24
Rtr-B is the downstream neighbor of Rtr-A for destination 171.68.10.0/24
LSRs know their downstream neighbors through the IP routing protocol
  Next-hop address is the downstream neighbor
171.68.10.0/24
Rtr-B
Rtr-A
Rtr-C
171.68.40.0/24
Upstream and Downstream LSRs

## Slide 18: Unsolicited Downstream Distribution
LSRs distribute labels to the upstream neighbors
171.68.10/24
Rtr-B
Rtr-A
Rtr-C
171.68.40/24
Next-Hop
In
Lab
-
...
Address
Prefix
171.68.10
...
Out
I/F
1
...
Out
Lab
30
...
In
I/F
0
...
Next-Hop
In
Lab
30
...
Address
Prefix
171.68.10
...
Out
I/F
1
...
Out
Lab
40
...
In
I/F
0
...
Next-Hop
In
Lab
40
...
Address
Prefix
171.68.10
...
Out
I/F
1
...
Out
Lab
-
...
In
I/F
0
...
Use label 40 for destination 171.68.10/24
Use label 30 for destination 171.68.10/24
IGP derived routes

## Slide 19: On-Demand Downstream Distribution
Upstream LSRs request labels to downstream neighbors
Downstream LSRs distribute labels upon request
171.68.10.0/24
Rtr-B
Rtr-A
Rtr-C
171.68.40.0/24
Use label 30 for destination 171.68.10/24
Use label 40 for destination 171.68.10/24
Request label for destination 171.68.10/24
Request label for destination 171.68.10/24

## Slide 20: Label Retention Modes
Label retention mode refers to the way in which an LSR treats label mappings it is not currently using.
Liberal retention mode
  LSR retains labels from all neighbors
    should a topology change occur, the labels to use in the new topology are usually already in place
    Require more memory and label space
Conservative retention mode
  LSR retains labels only from next-hops neighbors
    Any label mapping received from a peer LSR that is not used in an active NHLFE (Next Hop Label Forwarding Entry) is released
    Delay in obtaining new labels when a topology change occurs.
    Free memory and label space

## Slide 21: Label Distribution Control Modes
Independent LSP control
  LSR binds a Label to a FEC independently, whether or not the LSR has received a Label the next-hop for the FEC
  The LSR then advertises the Label to its neighbor
Ordered LSP control
  LSR only binds and advertise a label for a particular FEC if:
    it is the egress LSR for that FEC or
    it has already received a label binding from its next-hop

## Slide 22: Router Example: Forwarding Packets
0
171.69
Packets Forwarded Based on IP Address
Data
Address
Prefix
128.89
171.69
1
1
I/F
…
Address
Prefix
128.89
171.69
0
1
…
0
1
I/F
128.89
0
1
128.89.25.4
Data
Address
Prefix
128.89
0
…
…
I/F
Data
Data
128.89.25.4
128.89.25.4
128.89.25.4
Notes: Now when a packet comes into a router a look up is done based on the IP address in the packet, at match is obtained, and the packet is forwarded out the appropriate interface.
The packet follows the same process on a hop-by-hop bases through the network until it reaches its destination.

## Slide 23: MPLS Example: Routing Information
128.89
1
0
1
0
Routing Updates (OSPF, EIGRP, …)
You Can Reach 128.89 and 171.69 Thru Me
You Can Reach 171.69 Thru Me
You Can Reach 128.89 Thru Me
In
Label
Address
Prefix
128.89
171.69
1
1
Out
I’face
Out Label
In
Label
Address
Prefix
128.89
171.69
0
1
Out
I’face
Out Label
In
Label
Address
Prefix
128.89
0
Out
I’face
Out Label
…
…
…
…
…
…
171.69
Notes: Tag edge routers and tag switches use standard IP routing protocols to identify routes through the network. Theses fully interoperate with non-tag switching routers
So what tag switching does is it extends the forwarding table by adding a tag field. One for the incoming tag and one for the outgoing tag. Note the topology of the network is discovered using unmodified layer 3 protocols such as OSPF.

## Slide 24: MPLS Example: Assigning Labels
128.89
1
0
1
0
Label Distribution Protocol (LDP)
(downstream allocation)
Use Label 4 for 128.89 and Use Label 5 for 171.69
Use Label 7 for 171.69
Use Label 9 for 128.89
In
Label
Address
Prefix
128.89
171.69
1
1
Out
I’face
Out Label
In
Label
Address
Prefix
128.89
171.69
0
1
Out
I’face
Out Label
In
Label
Address
Prefix
128.89
0
Out
I’face
Out Label
-
9
…
…
…
…
…
…
…
…
…
…
…
…
9
7
4
5
4
5
-
-
171.69
Notes: Tag routers and switches use the tables generated by the standard routing protocols to assign and distribute tag information via the tag distribution protocol (TDP). Tag routers receive the TDP information and build a forwarding database, which makes use of the tags.
TDP is then used to bind tags to routes and distribute this information to each routers upstream neighbor.

## Slide 25: MPLS Example: Forwarding Packets
In
Label
Address
Prefix
128.89
171.69
1
1
Out
I’face
Out Label
…
…
…
…
4
5
-
-
Label Switch Forwards Based on Label
In
Label
Address
Prefix
128.89
171.69
0
1
Out
I’face
Out Label
…
…
…
…
9
7
4
5
In
Label
Address
Prefix
128.89
0
Out
I’face
Out Label
-
9
…
…
…
…
Data
128.89.25.4
Data
128.89.25.4
Data
128.89.25.4
Data
128.89
1
0
1
0
128.89.25.4
4
9
Notes: When we get to the first router, the one performing the tag imposition, there’s an IP look-up based on the IP prefix. It finds the forwarding table entry and it discovers that to get to the destination it should use tag x. It sticks that tag on the front of the packet and forwards it along to the next hop tag switch.
At this point the router can just do pure tag forwarding, gets in the packet with tag x, figures our that the outgoing interface is y, and the outgoing tag replaces the incoming tag. Note packet is forwarded based solely on the tag without re-analyzing the network layer header. This provides the essential separation of routing and forwarding referred to earlier.
The packet reaches the tag edge router at the egress point of the network ,where the tag is stripped off and the packet delivered.

## Slide 26: Agenda
Introduction to MPLS
LDP
MPLS VPN

## Slide 27: MPLS Unicast IP Routing
MPLS introduces a new field that is used for forwarding decisions.
Although labels are locally significant, they have to be advertised to directly reachable peers.
  One option would be to include this parameter into existing IP routing protocols.
  The other option is to create a new protocol to exchange labels.
The second option has been used because there are too many existing IP routing protocols that would have to be modified to carry labels.

## Slide 28: Label Distribution Protocol
Defined in RFC 3036 and 3037
Used to distribute labels in a MPLS network
Forwarding equivalence class
  How packets are mapped to LSPs (Label Switched Paths)
Advertise labels per FEC
  Reach destination a.b.c.d with label x
Neighbor discovery
  Basic and extended discovery

## Slide 29: MPLS Unicast IP Routing Architecture
LSR
Control plane
Data plane
Routing protocol
Label distribution protocol
Label forwarding table
IP routing table
Exchange of
routing information
Exchange of
labels
Incoming
labeled packets
Outgoing
labeled packets
IP forwarding table
Incoming
IP packets
Outgoing
IP packets

## Slide 30: MPLS Unicast IP Routing: Example
LSR
Control plane
Data plane
OSPF:
RT:
LIB:
FIB:
LFIB:
OSPF: 10.0.0.0/8
10.0.0.0/8  1.2.3.4
10.0.0.0/8  1.2.3.4
10.0.0.0/8  1.2.3.4
L=5 10.1.1.1
10.1.1.1
10.1.1.1

## Slide 31: MPLS Unicast IP Routing: Example
LSR
Control plane
Data plane
OSPF:
RT:
LIB:
FIB:
LFIB:
OSPF: 10.0.0.0/8
10.0.0.0/8  1.2.3.4
10.0.0.0/8  1.2.3.4
10.1.1.1
LDP: 10.0.0.0/8, L=3
10.0.0.0/8  Next-hop L=3,
LDP: 10.0.0.0/8, L=5
L=5 10.1.1.1
L=3 10.1.1.1
L=5  L=3
, L=3
L=3 10.1.1.1
10.0.0.0/8  1.2.3.4
Local = 5

## Slide 32: Label Allocation in Packet-Mode MPLS Environment
Label allocation and distribution in packet-mode MPLS environment follows these steps:
  IP routing protocols build the IP routing table.
  Each LSR assigns a label to every destination in the IP routing table independently.
  LSRs announce their assigned labels to all other LSRs.
  Every LSR builds its LIB, LFIB data structures based on received labels.

## Slide 33: Building the IP Routing Table
IP routing protocols are used to build IP routing tables on all LSRs.
Forwarding tables (FIB) are built based on IP routing tables with no labeling information.

## Slide 34: Allocating Labels
Every LSR allocates a label for every destination in the IP routing table.
Labels have local significance.
Label allocations are asynchronous.
Router B assigns label 25 to destination X.

## Slide 35: LIB and LFIB Set-up
LIB and LFIB structures have to be initialized on the LSR allocating the label.
Router B assigns label 25 to destination X.
Outgoing action is POP as B has received no label for X from C.
Local label is stored in LIB.

## Slide 36: Label Distribution
The allocated label is advertised to all neighbor LSRs, regardless of whether the neighbors are upstream or downstream LSRs for the destination.
X = 25
X = 25
X = 25

## Slide 37: Receiving Label Advertisement
Every LSR stores the received label in its LIB.
Edge LSRs that receive the label from their next-hop also store the label information in the FIB.
X = 25
X = 25
X = 25

## Slide 38: Interim Packet Propagation
Forwarded IP packets are labeled only on the path segments where the labels have already been assigned.
A
B
C
E
IP: X
Lab: 25
IP: X
IP lookup is performed in FIB, packet is labeled.
Label lookup is performed in LFIB, label is removed.

## Slide 39: Further Label Allocation
A
B
C
D
E
Network X
Every LSR will eventually assign a label for every destination.
Router C assigns label 47 to destination X.
X = 47
X = 47

## Slide 40: Receiving Label Advertisement
Every LSR stores received information in its LIB.
LSRs that receive their label from their next-hop LSR will also populate the IP forwarding table (FIB).
X = 47
X = 47

## Slide 41: Populating LFIB
Router B has already assigned label to X and created an entry in LFIB.
Outgoing label is inserted in LFIB after the label is received from the next-hop LSR.
X = 47
X = 47
Label
Action
Next hop
25
47
C
LFIB on B

## Slide 42: Packet Propagation Across MPLS Network
A
B
C
E
IP: X
Lab: 25
Lab: 47
IP lookup is performed in FIB, packet is labeled.
Label lookup is performed in LFIB, label is switched.
Label lookup is performed in LFIB, label is removed.
IP: X
Ingress LSR
Egress LSR

## Slide 43: Steady State Description
After the LSRs have exchanged the labels, LIB, LFIB and FIB data structures are completely populated.
Convergence in Packet-mode MPLS

## Slide 44: Link Failure Actions
Routing protocol neighbors and LDP neighbors are lost after a link failure.
Entries are removed from various data structures.


## Slide 45: Routing Protocol Convergence
Routing protocols rebuild the IP routing table and the IP forwarding table.


## Slide 46: MPLS Convergence
LFIB and labeling information in FIB are rebuilt immediately after the routing protocol convergence, based on labels stored in LIB.


## Slide 47: MPLS Convergence After a Link Failure
MPLS convergence in packet-mode MPLS does not impact the overall convergence time.
MPLS convergence occurs immediately after the routing protocol convergence, based on labels already stored in LIB.

## Slide 48: Link Recovery Actions
Routing protocol neighbors are discovered after link recovery.

## Slide 49: IP Routing Convergence After Link Recovery
IP routing protocols rebuild the IP routing table.
FIB and LFIB are also rebuilt, but the label information might be lacking.
C
C
—
pop
C

## Slide 50: MPLS Convergence After a Link Recovery
Routing protocol convergence optimizes the forwarding path after a link recovery.
LIB might not contain the label from the new next-hop by the time the IP convergence is complete.
End-to-end MPLS connectivity might be intermittently broken after link recovery.
Use MPLS Traffic Engineering for make-before-break recovery.

## Slide 51: LDP Session Establishment
LDP -- establish a session
  Hello messages are periodically sent on all interfaces enabled for MPLS.
  If there is another router on that interface it will respond by trying to establish a session with the source of the hello messages.
UDP is used for hello messages. It is targeted at “all routers on this subnet” multicast address (224.0.0.2).
TCP is used to establish the session.
Both TCP and UDP use well-known LDP port number 646.

## Slide 52: LDP Neighbor Discovery
1.0.0.1
1.0.0.3
MPLS_A
NO_MPLS_C
1.0.0.4
MPLS_D
1.0.0.2
MPLS_B
TCP (1.0.0.2:1043  1.0.0.1:646)
UDP: Hello
(1.0.0.1:1050  224.0.0.2:646)
UDP: Hello
(1.0.0.4:1033  224.0.0.2:646)
UDP: Hello
(1.0.0.2:1064  224.0.0.2:646)
UDP: Hello
(1.0.0.1:1051  224.0.0.2:646)
UDP: Hello
(1.0.0.4:1034  224.0.0.2:646)
UDP: Hello
(1.0.0.2:1065  224.0.0.2:646)
UDP: Hello
(1.0.0.1:1052  224.0.0.2:646)
UDP: Hello
(1.0.0.4:1035  224.0.0.2:646)
UDP: Hello
(1.0.0.2:1066  224.0.0.2:646)
TCP (1.0.0.4:1065  1.0.0.1:646)
TCP (1.0.0.4:1066  1.0.0.2:646)
LDP Session is established from the router with higher IP address.

## Slide 53: LDP Session Negotiation
Peers first exchange initialization messages.
The session is ready to exchange label mappings after receiving the first keepalive.
1.0.0.1
MPLS_A
1.0.0.2
MPLS_B
Initialization message
Establish TCP session
Initialization message
Keepalive
Keepalive

## Slide 54: Double Lookup Scenario
MPLS Domain
Double lookup is not an optimal way of forwarding labeled packets.
A label can be removed one hop earlier.
10.0.0.0/8
L=19
10.0.0.0/8
L=18
10.0.0.0/8
L=17
LFIB
18  19
FIB
10/8  NH, 19
LFIB
17  18
FIB
10/8  NH, 18
LFIB
35  17
FIB
10/8  NH, 17
LFIB
19  untagged
FIB
10/8  NH
10.1.1.1
17

10.1.1.1
18

10.1.1.1
19

10.1.1.1


Double lookup is needed:
1. LFIB: remove the label.
2. FIB: forward the IP packet based on IP next-hop address.
10.0.0.0/8

## Slide 55: Penultimate Hop Popping
MPLS Domain
A label is removed on the router before the last hop within an MPLS domain.
10.0.0.0/8
L=pop
10.0.0.0/8
L=18
10.0.0.0/8
L=17
LFIB
18  pop
FIB
10/8  NH, 19
LFIB
17  18
FIB
10/8  NH, 18
LFIB
35  17
FIB
10/8  NH, 17
LFIB
FIB
10/8  NH
10.1.1.1
17

10.1.1.1
18

10.1.1.1

10.1.1.1

One single lookup.
10.0.0.0/8
Pop or implicit null label is adveritsed.

## Slide 56: Penultimate Hop Popping
Penultimate hop popping optimizes MPLS performace (one less LFIB lookup).
Pop or implicit null label uses value 3 when being advertised to a neighbor.
Reserved Label values:
  0: explicit NULL. Can be used in signaling protocols as well as label headers.
  3: implicit NULL. Used in signaling protocols only. It should never appear in the label stack. Its use in a signaling protocol indicates that the upstream router should perform penultimate hop popping (PHP; remove the top label on the stack).

## Slide 57: LDP Messages
Discovery messages
  Used to discover and maintain the presence of new peers
  Hello packets (UDP) sent to all-routers multicast address
  Once neighbor is discovered, the LDP session is established over TCP

## Slide 58: LDP Messages
Session messages
  Establish, maintain and terminate LDP sessions
Advertisement messages
  Create, modify, delete label mappings
Notification messages
  Error signalling

## Slide 59: Agenda
Introduction to MPLS
LDP
MPLS VPN

## Slide 60: What Is a VPN?
Virtual Private Network – Provide a private network over a shared infrastructure
Interconnect geographically separate sites, with the same privacy and guarantees as a private network

## Slide 61: IP VPN Taxonomy
Client-
Initiated
NAS-
Initiated
IP Tunnel
Virtual
Circuit
Network- Based VPNs
Security
Appliance
Router
FR
ATM
IP VPNs
DIAL
DEDICATED
RFC 2547
Virtual
Router
Notes: There are two fundamental types of IP VPNs: dial and dedicated.
Dial IP VPNs offer remote Intranet access for mobile users and telecommuters. This is the most common form of IP VPN deployed today. These services are sometimes known as “corporate dial outsourcing” solutions. There are two types of Dial IP VPNs, which are classified by where the tunnel is created: on the subscriber’s PC or by the Service Provider on the NAS (Network Access Server).
While dedicated IP VPNs come in many forms, the common element is the delivery of IP services to the subscriber. This is typically done over an IP network using devices such as a security appliance or router on the customer site. IP VPN services may also be offered by providing an IP interface over a Frame Relay or ATM network. The application of these dedicated services is in connecting remote offices to corporate Intranets and Extranets over the WAN. These services are characterized by multiple users and higher speed connections. To provide complete VPN services, businesses and Service Providers frequently combine these dedicated VPNs with remote access solutions.
In addition to today’s choices, Service Providers will soon be deploying VPN Aware Networks, a new category of products being designed to meet emerging Service Provider IP VPN requirements for scalability and flexibility.

## Slide 62: MPLS-VPN Terminology
Provider Network (P-Network)
  The backbone under control of a Service Provider
Customer Network (C-Network)
  Network under customer control
CE router
  Customer Edge router. Part of the C-network and interfaces to a PE router
Site -- Set of (sub)networks part of the C-network and co-located
  A site is connected to the VPN backbone through one or more PE/CE links
PE router -- Provider Edge router.
  Part of the P-Network and interfaces to CE routers
P router -- Provider (core) router, without knowledge of VPN

## Slide 63
Provider network
PE
PE
PE
site1
CE
site2
CE
site3
CE
P

## Slide 64: Goals
Inter-site connectivity
Privacy – Don’t allow traffic from one VPN to be seen in another VPN
Independent addressing – Private addresses in each VPN

## Slide 65: BGP – MPLS VPNs
Separation of forwarding
Distribution of routing information
New address type
Forwarding with MPLS

## Slide 66: Separation of Forwarding
Goal – control connectivity and ensure privacy by segregating the forwarding information
PE router connected to CEs from several VPNs
With a single forwarding table, it is possible to forward packets from one VPN to another

## Slide 67: Multiple Forwarding Tables
Multiple forwarding tables – each table associated with a site
Packets from the customer are identified based on the incoming port, which identifies the forwarding table
Contents – routes received from the CE and routes received from remote PEs with constrained routing
Called VPN routing and forwarding Table -- VRF

## Slide 68: Constrained Distribution of Routing Information
The Idea:
CE advertised routes to the local PE via some routing protocol
The local PE marks these routes with an extended community and advertise them in BGP
The routes are distributed to all remote PEs by BGP
Remote PE receives BGP routes, filters them based on the community and advertises them to the CE
 The need for unique addresses

## Slide 69
Provider network
PE
PE
PE
site1
CE
site2
CE
site3
CE
P
site4
CE
PE
10.1.0.0/16
10.1.0.0/16
10.2.0.0/16
10.2.0.0/16
10.1.0.0/16 route-target green
10.2.0.0/16 route-target green
10.1.0.0/16 route-target gray
10.2.0.0/16 route-target gray

## Slide 70: Overlapping address space and VPN-IP addresses
Goal
Turn non-unique addresses into unique addresses
An 8-byte unique identifier called the route distinguisher concatenated with IP addresses
Route Distinguisher Format

## Slide 71: VPN-IP addresses
Used only in the provider’s network
Used only in the control plane
The translation happens on the PE

## Slide 72
Provider network
PE
PE
PE
site1
CE
site2
CE
site3
CE
P
site4
CE
PE
10.1.0.0/16
10.1.0.0/16
10.2.0.0/16
10.2.0.0/16
RD1:10.1.0.0/16 route-target green
RD1:10.2.0.0/16 route-target green
RD2:10.1.0.0/16 route-target gray
RD2:10.2.0.0/16 route-target gray
VPN green  RD1
VPN gray  RD2

## Slide 73: Forward VPN packets in Provider Network
VPN-IP addresses do not appear in IP header
Need a way to forward traffic with overlapping addresses in the provider network

## Slide 74
Provider network
PE1
PE3
PE2
site1
CE1
site2
CE2
site3
CE3
P0
site4
CE4
PE4
10.1.0.0/16
10.1.0.0/16
10.2.0.0/16
10.2.0.0/16
RD1:10.1.0.0/16 PE1
RD1:10.2.0.0/16 PE2
RD2:10.1.0.0/16 PE4
RD2:10.2.0.0/16 PE3
P1
10.2.0.3
10.2.0.3

## Slide 75
Provider network
PE1
PE3
PE2
site1
CE1
site2
CE2
site3
CE3
P0
site4
CE4
PE4
10.1.0.0/16
10.1.0.0/16
10.2.0.0/16
10.2.0.0/16
RD1:10.1.0.0/16 PE1
RD1:10.2.0.0/16 PE2
RD2:10.1.0.0/16 PE4
RD2:10.2.0.0/16 PE3
P1
10.2.0.3
10.2.0.3
Label 2
Label 1

## Slide 76: VPN Labels
The Idea:
Use a label to identify the next hop at the remote PE. Also called VPN label
The label is distributed by BGP, along with the VPN-IP address
Traffic will carry two labels – the VPN label and the LSP label
The remote PE makes the forwarding decision based on the VPN label

## Slide 77
Provider network
PE1
PE3
PE2
site1
CE1
site2
CE2
site3
CE3
P0
site4
CE4
PE4
10.1.0.0/16
10.1.0.0/16
10.2.0.0/16
10.2.0.0/16
P1
10.2.0.3
VPN label
LSP label

## Slide 78: VPN Model -- Summary
P routers do not maintain VPN routes. Only maintain routes to other P and PE routers
PE routers maintain VPN routes, but only for VPNs that have sites attached to them
VPNs can have overlapping address spaces

## Slide 79: 1st – LSP Setup
Provider network
PE1
PE2
site1
CE1
site2
CE2
P0
10.1.0.0/16
10.2.0.0/16
P1
[PE2, 3]
[PE2, 100]
[PE2, 200]
PE2-- push 200

## Slide 80: 2nd – Route Distribution
Provider network
PE1
PE2
site1
CE1
site2
CE2
P0
10.1.0.0/16
10.2.0.0/16
P1
PE2-- push 200
site3
CE3
10.2.0.0/16
VPN green  RD1
VPN gray  RD2
[10.2.0.0/16] via CE2
[RD1:10.2.0.0/16, label 1001] via PE2
[10.2.0.0/16] via PE1

## Slide 81: 3rd – The Forwarding Table
Provider network
PE1
PE2
site1
CE1
site2
CE2
P0
10.1.0.0/16
10.2.0.0/16
P1
[PE2, 3]
[PE2, 100]
[PE2, 200]
[10.2.0.0/16] nh CE2
[RD1:10.2.0.0/16, label 1001] nh PE2
[10.2.0.0/16] via PE1
10.2.0.0/16 - push 1001, nh PE2
PE2-- push 200
1001 – pop, vpn green
10.2.0.0/16 – nh CE2

## Slide 82: 4th – Forwarding Traffic
Provider network
PE1
PE2
site1
CE1
site2
CE2
P0
10.1.0.0/16
10.2.0.0/16
P1
[PE2, 3]
[PE2, 100]
[PE2, 200]
10.2.1.1
10.2.0.0/16 - push 1001, nh PE2
PE2-- push 200
1001 – pop, vpn green
10.2.0.0/16 – nh CE2
10.2.0.0/16 - nh PE1
10.2.1.1
1001
200
10.2.1.1
1001
100
10.2.1.1
1001
10.2.1.1

## Slide 83: Route Distinguisher
Distinguish one set of routes (one VRF) from another. It is a unique number prepended to each route within a VRF to identify it as belonging to that particular VRF. An RD is carried along with a route via MP-BGP when exchanging VPN routes with other PE routers.
An RD is 64 bits in length comprising three fields:
  type (two bytes), administrator, and value.
Type 0
ASN (2 bytes)
Value (4 bytes)
Type 1
IP (4 bytes)
Value (2 bytes)
Type 2
ASN (4 bytes)
Value (2 bytes)

## Slide 84: Route Target
A BGP extended community attribute used control route distribution among VRFs. Route targets are applied to a VRF to control the import and export of routes among it and other VRFs.
Route-target Export:
Route-target Import:
ip vrf Customer_A
rd 65000:100
route-target export 65000:100
route-target import 65000:100
BGP update:
Extended community:
Route-taget 65000:100
Prefix 10.2.0.0/16
Route Distinguisher: 65000:100

## Slide 85: Route-Target Example 1
ip vrf Customer_A
rd 65000:100
route-target export 65000:100
route-target import 65000:100
route-target import 65000:300
!
ip vrf Customer_B
rd 65000:200
route-target export 65000:200
route-target import 65000:200
route-target import 65000:300
!
ip vrf Shared
rd 65000:300
route-target export 65000:300
route-target import 65000:300
65000:100
export
65000:100
import
65000:300
Customer A
65000:200
export
65000:200
import
65000:300
Customer B
65000:300
export
import
65000:300
Shared

## Slide 86: Route-Target Example 2
ip vrf Customer_A
rd 65000:100
route-target export 65000:100
route-target export 65000:1234
route-target import 65000:100
route-target import 65000:300
!
ip vrf Customer_B
rd 65000:200
route-target export 65000:200
route-target export 65000:1234
route-target import 65000:200
route-target import 65000:300
!
ip vrf Shared
rd 65000:300
route-target export 65000:300
route-target import 65000:1234
65000:100
export
65000:100
import
65000:300
Customer A
65000:200
export
65000:200
import
65000:300
Customer B
65000:300
export
import
65000:1234
Shared
65000:1234
65000:1234

## Slide 87: MPLS-VPN Scaling BGP updates filtering
  Each VRF has an import and export policy configured
  Policies use route-target attribute (extended community)
  PE receives MP-iBGP updates for VPN-IPv4 routes
  If route-target is equal to any of the import values configured in the PE, the update is accepted
  Otherwise it is silently discarded
PE
MP-iBGP sessions
VRFs for VPNs yellow green
VPN-IPv4 update: RD:Net1, Next-hop=PE-X SOO=Site1, RT=Green, Label=XYZ
VPN-IPv4 update: RD:Net1, Next-hop=PE-X SOO=Site1, RT=Red, Label=XYZ
Import RT=yellow
Import RT=green

## Slide 88: MPLS VPN Connection Model
The routes the PE receives from CE routers are installed in the appropriate VRF
The routes the PE receives through the backbone IGP are installed in the global routing table
By using separate VRFs, addresses need NOT to be unique among VPNs
PE
CE
CE
Site-2
Site-1
VPN Backbone IGP
EBGP,OSPF, RIPv2,Static

## Slide 89: MPLS VPN Connection Model
PE-1
VPN Backbone IGP
PE-2
P
P
P
P
  PE routers receive IPv4 updates (EBGP, RIPv2, Static…)
  PE routers translate into VPN-IPv4
    Assign a SOO and RT based on configuration
    Re-write Next-Hop attribute
    Assign a label based on VRF and/or interface
    Send MP-iBGP update to all PE neighbors
BGP,RIPv2 update for Net1,Next-Hop=CE-1
VPN-IPv4 update: RD:Net1, Next-hop=PE-1 SOO=Site1, RT=Green, Label=(intCE1)
CE-1
Site-2
VPN-IPv4 update is translated into IPv4 address (Net1) put into VRF green since RT=Green and advertised to CE-2
Site-1
CE-2

## Slide 90: MPLS VPN Connection Model
  Receiving PEs translate to IPv4
    Insert the route into the VRF identified by the RT attribute (based on PE configuration)
  The label associated to the VPN-IPv4 address will be set on packet forwarded towards the destination
PE-1
VPN Backbone IGP
PE-2
P
P
P
P
BGP,OSPF, RIPv2 update for Net1 Next-Hop=CE-1
VPN-IPv4 update: RD:Net1, Next-hop=PE-1 SOO=Site1, RT=Green, Label=(intCE1)
CE-1
Site-2
VPN-IPv4 update is translated into IPv4 address (Net1) put into VRF green since RT=Green and advertised to CE-2
Site-1
CE-2

## Slide 91: MPLS Forwarding Penultimate Hop Popping
PE2
PE1
CE1
CE2
P1
P2
IGP Label(PE2) VPN Label
IP
packet
PE1 receives IP packet
Lookup is done on site VRF
BGP route with Next-Hop and Label is found
BGP next-hop (PE2) is reachable through IGP route with associated label
IGP Label(PE2) VPN Label
IP
packet
P routers switch the packets based on the IGP label (label on top of the stack)
VPN Label
IP
packet
Penultimate Hop Popping
P2 is the penultimate hop for the BGP next-hop
P2 remove the top label
This has been requested through LDP by PE2
IP
packet
PE2 receives the packets with the label corresponding to the outgoing interface (VRF)
One single lookup
Label is popped and packet sent to IP neighbor
IP
packet
CE3

## Slide 92: Packet Forwarding Example 1
T1 T7
T2 T8
T3 T9
T4 T7
T5 TB
T6 TB
T7 T8
VPN_A
VPN_A
VPN_B
10.3.0.0
10.1.0.0
11.5.0.0
P
P
P
P
PE
CE
CE
CE
Data
<RD_A,11.6> , iBGP next hop PE1
<RD_A,10.1> , iBGP next hop PE4
<RD_A,10.4> , iBGP next hop PE4
<RD_A,10.2> , iBGP next hop PE2
<RD_B,10.2> , iBGP NH= PE2 , T2 T8
Ingress PE receives normal IP Packets from CE router
PE router does “IP Longest Match” from VPN_B FIB , find iBGP next hop PE2 and impose a stack of labels: exterior Label T2 + Interior Label T8
Data
T8T2
VPN_A
VPN_B
VPN_B
10.1.0.0
10.2.0.0
11.6.0.0
CE
PE1
PE2
CE
CE
VPN_A
10.2.0.0
CE
<RD_B,10.1> , iBGP next hop PE1
<RD_B,10.2> , iBGP next hop PE2
<RD_B,10.3> , iBGP next hop PE3

## Slide 93: Packet Forwarding Example 1 (cont.)
VPN_A
VPN_A
VPN_B
10.3.0.0
10.1.0.0
11.5.0.0
P
P
P
P
PE
CE
CE
CE
T7
T8
T9
Ta
Tb
Tu
Tw
Tx
Ty
Tz
T8, TA
T2
Data
T8
Data
T2
Data
TB
out
in /
All Subsequent P routers do switch the packet Solely on Interior Label
Egress PE router, removes Interior Label
Egress PE uses Exterior Label to select which VPN/CE to forward the packet to.
Exterior Label is removed and packet routed to CE router
VPN_A
VPN_B
VPN_B
10.1.0.0
10.2.0.0
11.6.0.0
CE
PE1
PE2
CE
CE
VPN_A
10.2.0.0
CE
T2
Data
Data
TAT2

## Slide 94: Packet Forwarding Example 2
In VPN 12, host 130.130.10.1 sends a packet with destination 130.130.11.3
Customer sites are attached to Provider Edge (PE) routers A & B.
130.130.10.1
130.130.11.3
12
12
A
B

## Slide 95: Packet Forwarding Example 2 (cont.)
VPN-ID
VPN Site Address
Provider Edge Router Address
VPN Site Label
PE Label
12
130.130.10.0/24
172.68.1.11/32
26
42
12
130.130.11.0/24
172.68.1.2/32
989
101
...
...
...
...
...
2. PE router A selects the correct VPN forwarding table based on the links’ VPN ID (12).
12
1. Packet arrives on VPN 12
link on PE router A.
A

## Slide 96: Packet Forwarding Example 2 (cont.)
130.130.11.3
Rest of IP packet
VPN-ID
VPN Site Address
Provider Edge Router Address
VPN Site Label
PE Label
12
130.130.10.0/24
172.68.1.11/32
26
42
12
130.130.11.0/24
172.68.1.2/32
989
101
...
...
...
...
...
12
A
3. PE router A matches the incoming packet’s destination address with VPN 12’s forwarding table.
989
101
4. PE router A adds two labels to the packet: one identifying the destination PE, and one identifying the destination VPN site.

## Slide 97: Packet Forwarding Example 2 (cont.)
A
B
5. Packet is label-switched from PE router A to PE B based on the top label, using normal MPLS.
The network core knows nothing about VPNs and sites: it only knows how to get packets from A to B using MPLS.

## Slide 98: Packet Forwarding Example 2 (cont.)
B
12
6. PE router B identifies the correct site in VPN 12 from the inner label.
130.130.11.3
7. PE router B removes the labels and forwards the IP packet to the correct VPN 12 site.

## Slide 99: MPLS VPN - Configuration
VPN knowledge is on PE routers
PE router have to be configured for
  VRF and Route Distinguisher
  VRF import/export policies (based on Route-target)
  Routing protocol used with CEs
  MP-BGP between PE routers
  BGP for Internet routers
    With other PE routers
    With CE routers

## Slide 100: MPLS VPN - Configuration VRF and Route Distinguisher
RD is configured on PE routers (for each VRF)
VRFs are associated to RDs in each PE
Common (good) practice is to use the same RD for the same VPN in all PEs
  But not mandatory
VRF configuration command
    ip vrf <vrf-symbolic-name> rd <route-distinguisher-value> route-target import <community> route-target export <community>

## Slide 101: CLI - VRF configuration
Site-1
Site-2
Site-3
Site-4
VRF for site-1 (100:1)
Site-1 routes Site-2 routes
VRF for site-4 (100:4)
Site-3 routes Site-4 routes
VRF for site-2 (100:2)
Site-1 routes Site-2 routes Site-3 routes
VRF for site-3 (100:3)
Site-2 routes Site-3 routes Site-4 routes
PE1
PE2
P
P
Multihop MP-iBGP
Site-1
Site-3
Site-4
Site-2
VPN-A
VPN-C
VPN-B
ip vrf site1
rd 100:1
route-target export 100:1
route-target import 100:1
ip vrf site2
rd 100:2
route-target export 100:2
route-target import 100:2
route-target import 100:1
route-target export 100:1
ip vrf site3
rd 100:3
route-target export 100:2
route-target import 100:2
route-target import 100:3
route-target export 100:3
ip vrf site-4
rd 100:4
route-target export 100:3
route-target import 100:3

## Slide 102: MPLS VPN - Configuration PE/CE routing protocols
Site-1
Site-2
Site-3
Site-4
PE1
PE2
P
P
Multihop MP-iBGP
Site-1
Site-3
Site-4
Site-2
VPN-A
VPN-C
VPN-B
VRF for site-1 (100:1)
Site-1 routes Site-2 routes
VRF for site-4 (100:4)
Site-3 routes Site-4 routes
VRF for site-2 (100:2)
Site-1 routes Site-2 routes Site-3 routes
VRF for site-3 (100:3)
Site-2 routes Site-3 routes Site-4 routes
ip vrf site3
rd 100:3
route-target export 100:23
route-target import 100:23
route-target import 100:34
route-target export 100:34
ip vrf site-4
rd 100:4
route-target export 100:34
route-target import 100:34
!
interface Serial4/6
ip vrf forwarding site3
ip address 192.168.73.7 255.255.255.0
encapsulation ppp
!
interface Serial4/7
ip vrf forwarding site4
ip address 192.168.74.7 255.255.255.0
encapsulation ppp
ip vrf site1
rd 100:1
route-target export 100:12
route-target import 100:12
ip vrf site2
rd 100:2
route-target export 100:12
route-target import 100:12
route-target import 100:23
route-target export 100:23
!
interface Serial3/6
ip vrf forwarding site1
ip address 192.168.61.6 255.255.255.0
encapsulation ppp
!
interface Serial3/7
ip vrf forwarding site2
ip address 192.168.62.6 255.255.255.0
encapsulation ppp

## Slide 103: MPLS VPN - Configuration PE/CE routing protocols
Site-1
Site-2
Site-3
Site-4
PE1
PE2
P
P
Multihop MP-iBGP
Site-1
Site-3
Site-4
Site-2
VPN-A
VPN-C
VPN-B
VRF for site-1 (100:1)
Site-1 routes Site-2 routes
VRF for site-4 (100:3)
Site-3 routes Site-4 routes
VRF for site-2 (100:2)
Site-1 routes Site-2 routes Site-3 routes
VRF for site-3 (100:2)
Site-2 routes Site-3 routes Site-4 routes
router bgp 100
no bgp default ipv4-unicast
neighbor 6.6.6.6 remote-as 100
neighbor 6.6.6.6 update-source Loop0
!
address-family ipv4 vrf site4
neighbor 192.168.74.4 remote-as 65504
neighbor 192.168.74.4 activate
exit-address-family
!
address-family ipv4 vrf site3
neighbor 192.168.73.3 remote-as 65503
neighbor 192.168.73.3 activate
exit-address-family
!
address-family vpnv4
neighbor 6.6.6.6 activate
neighbor 6.6.6.6 next-hop-self
exit-address-family
router bgp 100
no bgp default ipv4-unicast
neighbor 7.7.7.7 remote-as 100
neighbor 7.7.7.7 update-source Loop0
!
address-family ipv4 vrf site2
neighbor 192.168.62.2 remote-as 65502
neighbor 192.168.62.2 activate
exit-address-family
!
address-family ipv4 vrf site1
neighbor 192.168.61.1 remote-as 65501
neighbor 192.168.61.1 activate
exit-address-family
!
address-family vpnv4
neighbor 7.7.7.7 activate
neighbor 7.7.7.7 next-hop-self
exit-address-family