## Slide 1: CS 540 Computer Networks II
Sandy Wang
chwang_98@yahoo.com
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2
11. QoS
Notes: In this chapter, we look at the underlying technology and protocol architecture
of LANs. Chapters 12 and 13 are devoted to a discussion of specific
LAN systems.

## Slide 3: Topics
  Overview
  LAN Switching
  IPv4
  IPv6
  Routing Protocols -- RIP, RIPng, OSPF
  Routing Protocols -- ISIS, BGP
  MPLS
  Midterm Exam
  Transport Layer -- TCP/UDP
  Access Control List (ACL)
  Congestion Control & Quality of Service (QoS)
  Application Layer Protocols
  Application Layer Protocols continue
  Others – Multicast, SDN
  Final Exam

## Slide 4: Reference Books
Cisco CCNA Routing and Switching ICND2 200-101 Official Cert Guide, Academic Edition by Wendel Odom -- July 10, 2013. ISBN-13: 978-1587144882
The TCP/IP Guide: A Comprehensive, Illustrated Internet Protocols Reference by Charles M. Kozierok – October 1, 2005. ISBN-13: 978-1593270476
Data and Computer Communications (10th Edition) (William Stallings Books on Computer and Data Communications) by Williams Stallings – September 23, 2013. ISBN-13: 978-0133506488
http://class.svuca.edu/~sandy/class/CS540/

## Slide 5: Motivation
Internet is designed to give best-effort service
  i.e. all packets are treated the same
However, not all packets are the same
  HTTP – delay sensitive
  Voice/Video streaming – delay and jitter sensitive
  Online Games – delay and jitter sensitive
  BitTorrent – totally insensitive
    Delay, jitter, bandwidth do not matter
    File transfer will finish eventually
Should the network give better quality to some packets?

## Slide 6: Three Relevant Factors
Application performance
  How much bandwidth do you need?
  What about delay and jitter?
Bandwidth required to provide performance
  How to meet performance goals…
  While still offering general service to all applications
Complexity/cost of required mechanisms
  How to modify the network to meet perf. goals?
  Political concerns, e.g. network neutrality
  Security

## Slide 7: QoS: Quality of Service
Idea: build some unfairness into the network
  Some traffic is high priority, gets better service
  Some traffic is low priority, gets reduced service
Thus, “important” traffic receives “better” service
  What traffic is important?
  What do we mean by “better” service?
    Is the gain guaranteed and strictly defined?
    Is the gain relative and fungible?

## Slide 8: Benefits of QoS
QoS features provide improved and more predictable network service by offering the following:
Dedicated bandwidth
Improved loss characteristics
Congestion management and Avoidance
Traffic Shaping
Prioritization of traffic

## Slide 9: What makes up QoS?
Quality of Service is managing:
Loss -- packets that never get there
Delay -- packets that take too long to get there
Jitter -- variations in the arrival times of packets

## Slide 10
Queues in a router

## Slide 11: Components of QoS - Loss
Loss refers to the percentage of packets that fail to reach their destination.
Loss can result from errors in the network, corrupted frames and congested networks. With modern switched and optically based networks corrupted frames and packet losses due to network noise, interference and collisions are becoming rare.
Many of the packets lost in a healthy network are actually deliberately dropped by networking devices as a means of avoiding congestion.
For many TCP/IP based traffic flows, such as those associated with file and print services, small numbers of lost packets are of little concern.
For UDP traffic associated with real-time applications such as streaming media and voice, retransmission is not feasible and losses are less tolerable. As a guide, a highly available network should suffer less than 1% loss and for voice traffic the loss should approach 0%.

## Slide 12: Components of QoS - Delay
Delay or Latency refers to the time it takes for a packet to travel from the source to the destination.
Delay is comprised of fixed and variable delays.
Fixed delays comprise such events as serialization and encoding/decoding. (Eg a bit takes a fixed 100ns to exit a 10Mb Ethernet interface)
Variable delays are often the result of congestion and include the time packets spend in network buffers waiting their turn to access the media.
Delay is a more significant problem for network traffic that is bi-directional in nature as the delays tend to be additive.

## Slide 13: Components of QoS - Jitter
Delay variation or Jitter is the difference in the delay times of consecutive packets.
Jitter results in degraded audio performance. Jerky motion, loss of video quality or total loss of video depending on the encoding scheme used.
Hardware such as IP Phones use a jitter buffer to smooth out arrival times. However there are limits on a buffers ability to do this. In general, traffic that requires low latency will also require that variation in latency is also kept to a minimum. This is because any buffering used to reduce jitter will directly add to the total delay in the network.
Design rule - voice networks cannot cope with more than 30 ms of jitter.

## Slide 14: Quality of Service Requirements for Data
Use the proven relative priority model to divide traffic into no more than four classes, such as:
Gold (Mission-Critical) Transactional, software
Silver (Guaranteed-Bandwidth) Streaming video, messaging, intranet
Bronze (Best-Effort and Default class) Internet browsing, E-Mail
Less-than-Best-Effort (Optional; higher-drop preferences) FTP, backups, applications (Napster, KaZaa)

## Slide 15: Quality of Service Requirements for Voice
Voice traffic should be given:
Loss should be no more than 1%.
One-way latency should be no more than 150-200 ms.
Average jitter should be no more than 30 ms.
21-106 kbps of guaranteed priority bandwidth is required per call (depending on the sampling rate, codec and Layer 2 overhead).
150 bps (+ Layer 2 overhead) per phone of guaranteed bandwidth is required for Voice Control traffic.

## Slide 16: Quality of Service Requirements for Video
Requirements vary:
Video conferencing requirements are similar to voice.
Streaming media is often buffered for several seconds so latency requirements can be relaxed.
Allow for video’s bursty nature…

## Slide 17: Principles for QOS Guarantees
Consider a phone application at 1Mbps and an FTP application sharing a 1.5 Mbps link.
  bursts of FTP can congest the router and cause audio packets to be dropped.
  want to give priority to audio over FTP
PRINCIPLE 1: Marking of packets is needed for router to distinguish between different classes; and new router policy to treat packets accordingly

## Slide 18: Principles for QOS Guarantees
Applications misbehave (audio sends packets at a rate higher than 1Mbps assumed above);
PRINCIPLE 2: provide protection (isolation) for one class from other classes
Require Policing Mechanisms to ensure sources adhere to bandwidth requirements; Marking and Policing need to be done at the edges:

## Slide 19: Principles for QOS Guarantees
Alternative to Marking and Policing: allocate a set portion of bandwidth to each application flow; can lead to inefficient use of bandwidth if one of the flows does not use its allocation
PRINCIPLE 3: While providing isolation, it is desirable to use resources as efficiently as possible

## Slide 20: Principles for QOS Guarantees
Cannot support traffic beyond link capacity
  Two phone calls each requests 1 Mbps
PRINCIPLE 4: Need a Call Admission Process; application flow declares its needs, network may block call if it cannot satisfy the needs

## Slide 21: Building blocks
Classification
Scheduling
  Active Buffer Management
Traffic Shaping & Policing
  Leaky Bucket
  Token Bucket
Resource Utiliztion
Admission Control
  QoS Routing

## Slide 22: Quality of Service Mechanisms
QoS Service Models:
Best Effort The default if no explicit QoS is configured
Integrated Services Model – IntServ RSVP – A pre-negotiated QoS path is established end-to-end. Not well established as the application software must do the negotiating.
Differentiated Services Model – DiffServ Each hop (router) prioritises traffic according to configuration. Sometimes referred to as a per-hop-behaviour.
DiffServ is the focus of this course

## Slide 23: QoS at Internet Scale
Priority queues at the edge of the network help
  … but what about QoS across the entire Internet?
  Differentiated Service (DiffServ)
    Class-based traffic management mechanism
    Coarse grain control
    Relative performance improvements / lower overhead
  Integrated Service (IntServ)
    Flow-based traffic management mechanism
    Fine grained control
    Guaranteed performance / high overhead

## Slide 24: Differentiated Services (DiffServ)
Goal: offer different levels of service to packets
  Organized around domains (ASs)
  Involves edge and core routers (sometimes hosts too)
Edge routers
  Sort packets into classes (based on many factors)
  Set bits (DiffServ Code Point) in packet headers
  Police/shape traffic
Core Routers
  Handle per-hop packet behavior based on DSCP

## Slide 25: DiffServ at a High-Level
AS-1
AS-2
Ingress/Egress routers assign class to each packet
  Must analyze each packet, high overhead
Core routers use classes to do priority queuing
Classes may switch between AS boundaries
Ingress/
Egress Routers
Core
Routers

## Slide 26: Establishing Differentiated Services
There is a need to “tag” traffic with a QoS level so that a specific per-hop treatment can be applied:
Layer 2 – CoS – Class of Service field.
    3 bits 0-7 value
    Field is present in ISL and 802.1Q/P encapsulations
Layer 3 – ToS – Type of Service field.
    3 bits 0-7 value Only relevant to IP
    Often referred to as “IP Precedence”
Layer 3 – DSCP – Differentiated Services Code Point
    Supersedes ToS
    6 bits (first 3 bits are ToS) 0-63 value
0 is the lowest priority

## Slide 27: Establishing Differentiated Services
It may seem confusing to have three options for marking traffic:
The way to proceed is often determined by the QoS capabilities of hosts, switches and routers within the network.
In many instances it may be necessary to use different marking techniques at different points within a network.
For example, it is common to use the DSCP to mark the QoS requirements of packets through the routed layers of the network and mark the frames using the CoS to allow layer 2 devices such as switches to provide for the QoS requirements of packet at the data link layer.

## Slide 28: How do we Classify Packets?
It depends.
  Based on ports
    i.e. 80 (HTTP) takes precedence over 21 (FTP)
  Based on application
    i.e. HTTP takes precedence over BitTorrent
  Based on location
    i.e. home users get normal service…
    While hospitals/policy/fire department get priority service
  Based on who pays more $$$
    $100 for “premium” Internet vs. $25 “value” Internet

## Slide 29: IP Header, Revisited
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
DiffServ Code Point
Used to label the class of the packet

## Slide 30: Classification and Conditioning
Packet is marked in the Type of Service (TOS) in IPv4, and Traffic Class in IPv6
6 bits used for Differentiated Service Code Point (DSCP) and determine PHB that the packet will receive
2 bits are currently unused
D: Delay
T: Throughput
R: Reliability
C: Cheapest
(low cost)

## Slide 31: DSCP values
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
7 | 63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 CS7
6 | 55 | 54 | 53 | 52 | 51 | 50 | 49 | 48 CS6
5 | 47 | 46 EF | 45 | 44 | 43 | 42 | 41 | 40 CS5
4 | 39 | 38 AF43 | 37 | 36 AF42 | 35 | 34 AF41 | 33 | 32 CS4
3 | 31 | 30 AF33 | 29 | 28 AF32 | 27 | 26 AF31 | 25 | 24 CS3
2 | 23 | 22 AF23 | 21 | 20 AF22 | 19 | 18 AF21 | 17 | 16 CS2
1 | 15 | 14 AF13 | 13 | 12 AF12 | 11 | 10 AF11 | 9 | 8 CS1
0 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 Default
First 3 bits
Last 3 bits

## Slide 32: Forwarding (PHB)
PHBs being developed:
Expedited Forwarding: packet departure rate of a class equals or exceeds specified rate
  logical link with a minimum guaranteed rate
    Premium service
  DSCP = 101110 (46)
Assured Forwarding: 4 classes of traffic
  Each guaranteed minimum amount of bandwidth
  Each with three drop preference partitions
    Gold, silver, bronze

## Slide 34: Forwarding (PHB)
Per Hop Behavior (PHB) result in a different observable (measurable) forwarding performance behavior
PHB does not specify what mechanisms to use to ensure required PHB performance behavior
Examples:
  Class A gets x% of outgoing link bandwidth over time intervals of a specified length
  Class A packets leave first before packets from class B

## Slide 35: DiffServ Routers
Classifier
Meter
Policer
Marker
DiffServ Edge Router
Extract
DSCP
Local
conditions
PHB
PHB
PHB
PHB
Select PHB
Packet
treatment
DiffServ Core Router
Notes: DiffServ edge router utilises these functions in order to perform its task: - Classification (based on for example application, user or load) - Marking (of the DiffServ packets) - Metering (for policing or marking purposes) - Policing (handling of non-conformant traffic)
DiffServ core router will treat an IP packet based on 1) DS codepoint 2) Local conditions
DS codepoint is actually an index to a table that contains so called Per Hop Behaviors (PHB).
Per Hop Behavior is the set of rules how the packet (or actually the aggregate flow that the packet belongs to) is treated.
The local conditions can be, for example, the occupancy level(s) of the buffer(s) of the router.
Based on these two pieces of information, the edge router treats the packet.
For example, the packet may be discarded or accepted for buffering.

## Slide 36: Scheduling and Buffer management
Scheduling: choosing the next packet for transmission
Packet dropping:
  not drop-tail
  not only when buffer is full
    Active Queue Management

## Slide 37: Scheduling
Scheduling is used to give different queueing priorities according to the packet or frames DSCP or CoS value.
First In First Out – FIFO (No QoS treatment)
Priority Queuing
Weighted Fair Queuing - WFQ

## Slide 38
FIFO queue

## Slide 39
Priority queuing
*
*
*
Q1
Qn

## Slide 40
Weighted fair queuing

## Slide 41: Weighted Random Early Deletion - W-RED
55
Stated requirement
  “Avoid congestion in the first place”
  “Statistically give some traffic better service than others”
Congestion avoidance, rather than congestion management
Notes: 55

## Slide 42: Behavior of a TCP Sender
56
Sends as much as credit (TCP window) allows
Starts credit small (initial cwnd = 1)
  Avoid overloading network queues
Increases credit exponentially (slow start) per RTT
  To gauge network capability via packet loss signal
Notes: 56

## Slide 43
ACK packets
Data packets
R
S
ACK packets
Data packets
R
S
ACK packets
Data packets
R
S

## Slide 44: Behavior of a TCP Receiver
57
When in receipt of “next message,” schedules an ACK for this data
When in receipt of something else, acknowledges all received in-sequence data immediately
  i.e. send duplicate ACK in response to out of sequence data received
Notes: 57

## Slide 45
ACK packets
Data packets
R
S
ACK packets
Data packets
R
S
Dropped Packet
Duplicate ACKs

## Slide 46: Sender Response to ACK
58
If ACK advances sender’s window
  Update window and send new data
If not then it’s a duplicate ACK
  Presume it indicates a lost packet
  Send first unacknowledged data immediately
  Halve current sending window
  shift to congestion avoidance mode
  Increase linearly to gauge network throughput
Notes: 58

## Slide 47: Implications for Routers
59
Dropping a data packet within a data sequence is an efficient way of indicating to the sender to slow down
  Dropping a data packet prior to queue exhaustion increases the probability of successive packets in the same flow sequence being delivered, allowing the receiver to generate duplicate ACKs, in turn allowing the sender to adjust cwnd and reducing sending rate using fast retransmit response
  Allowing the queue to fill causes the queue to tail drop, which in turn causes sender timeout, which in turn causes window collapse, followed by a flow restart with a single transmitted segment
Notes: 59

## Slide 48: Congestion Avoidance
Prioritising traffic in a congested network is fine but it would be better to avoid the congestion altogether.
Congestion leads to dropped packets. By default packets are dropped indiscriminately once a router’s buffers are full. This is known as “tail drop”.
Dropping packets causes TCP to reduce its window-size thus reducing the data rate and lessening congestion – good!
Tail drop causes many TCP sessions to do this simultaneously – bad!
    This means that bandwidth may not be fully utilised and it results in a traffic flow that resembles a “saw tooth”.
    Tail drop can result in bursty traffic flows that cause other problems such as jitter.

## Slide 49: RED Algorithm
60
Attempt to maintain mean queue depth
Drop traffic at a rate proportional to mean queue depth and time since last discard
Probability
of packet
drop
1
0
Onset of
RED
Queue
exhaustion
tail
drop
Average queue depth
RED
discard
Notes: 60

## Slide 50: Random Early Detection (RED)
Basic premise:
  router should signal congestion when the queue first starts building up (by dropping a packet)
  but router should give flows time to reduce their sending rates before dropping more packets
  Note: when RED is coupled with ECN, the router can simply mark a packet instead of dropping it
Therefore, packet drops should be:
  early: don’t wait for queue to overflow
  random: don’t drop all packets in burst, but space them

## Slide 51: RED
FIFO scheduling
Buffer management:
  Probabilistically discard packets
  Probability is computed as a function of average queue length (why average?)
Discard Probability
Average
Queue Length
min_th
max_th
0
1
queue_len

## Slide 52: RED (cont’d)
Enqueue
Discard
Discard/Enqueue
probabilistically
0
1
min_th
max_th
queue_len
Discard Probability

## Slide 53: Weighted RED
Alter RED-drop profile according to QoS indicator
  precedence and/or drop preference
Discard Probability
Weighted Queue Length
High priority traffic
Low priority traffic
1
0
Notes: 61

## Slide 54: Outcomes of RED
62
Increase overall efficiency of the network
  ensure that packet loss occurs prior to tail drop
  allowing senders to back off without need to resort to retransmit time-outs and window collapse
  ensure that network load signaling continues under load stress conditions
Notes: 62

## Slide 55: Outcomes of W-RED
63
High precedence and short duration TCP flows will operate without major impact
  RED’s statistical selection is biased towards large packet trains for selection of deletion
Low precedence long held TCP flows will back off transfer rate
  by how much depends on RED profile
W-RED provides differentiation of TCP-based traffic profiles
  but without deterministic level of differentiation
Notes: 63

## Slide 56: Pitfalls of RED
64
No effect on UDP
Packet drop uses random selection
  Depends on host behavior for effectiveness
  Not deterministic outcome
Specifically dependent on
  bulk of traffic being TCP
  TCP using RTT-epoch packet train clustering
    ACK spacing will reduce RED effectiveness
  TCP responding to RED drop - but not all TCPs are created equal
Notes: 64

## Slide 57: Weighted RED
65
Appropriate when
  Any given flow has low probability of having data in queue
Stochastic model
Reduces turbulent inputs
Traffic classification based on IP precedence
  Different min_threshold values per IP precedence value
Notes: 65

## Slide 58: RED Summary
Basic idea is sound, but does not always work well
    Basically, dropping packets, early or late is a bad thing
High network utilization with low delays when flows are long lived
Average queue length small, but capable of absorbing large bursts
Many refinements to basic algorithm make it more adaptive
    requires less tuning
Does not work well for short lived flows (like Web traffic)
    Dropping packets in an already short lived flow is devastating
Better to mark ECN instead of dropping packets
    ECN not widely supported

## Slide 59
To control the amount and the rate of traffic.
Traffic Shaping is to control the traffic when it leaves the network.
Traffic Policing is to control the traffic when it enters the network.
Two techniques can shape or police the traffic: leaky bucket and token bucket.
Traffic Shaping and Policing

## Slide 60
Bursty Traffic Policing VS. Shaping:
Traffic Policing propagates bursts. When the traffic rate reaches the configured maximum rate, excess traffic is dropped (or remarked). The result is an output rate that appears as a saw-tooth with crests and troughs.
Traffic Shaping In contrast to policing, retains excess packets in a QUEUE and then schedules the excess for later transmission over increments of time. The result of traffic shaping is a smoothed packet output rate.
Shaping implies the existence of a queue and of sufficient memory to buffer delayed packets, while policing does not buffer excess packets.

## Slide 61
Bursty Traffic Policing VS. Shaping:

## Slide 62: The Leaky Bucket Algorithm
The Leaky Bucket Algorithm
  used to control rate in a network.
  It is implemented as a single-server queue
    with constant service time.
  If the bucket (buffer) overflows then packets are discarded.
Leaky Bucket (parameters r and B):
  Every r time units: send a packet.
  For an arriving packet
    If queue not full (less than B) then enqueue
Note that the output is a “perfect” constant rate.

## Slide 63: The Leaky Bucket Algorithm

## Slide 64
Leaky bucket
7
8
9
10
2 Mbps

## Slide 65: Token Bucket Algorithm
Highlights:
  The bucket holds tokens.
  To transmit a packet, we “use” one token.
Allows the output rate to vary,
  depending on the size of the burst.
  In contrast to the Leaky Bucket
Granularity
  Packets (or bits)
Token Bucket (r, MaxTokens):
  Generate a token every r time units
    If number of tokens more than MaxToken, reset to MaxTokens.
  For an arriving packet: enqueue
  While buffer not empty and there are tokens:
    send a packet and discard a token

## Slide 66: The Token Bucket Algorithm
5-34

## Slide 67
Token Bucket
Since the Leaky Bucket is not fair for idle host for long times then gets bursty data, it still transmits the average rate (ignoring its long idle time)! Hence, we have Token Bucket (TB).

## Slide 68
The bucket gets tokens at a certain rate (data unit per sec, du/s).
A token is permission for the source to send a certain number of du’s into the network.
To send a packet, remove from the bucket a number of tokens equal in representation to the packet size in du’s.
If not enough tokens are in the bucket to send a packet, the packet either:
  queued waiting until the bucket has enough tokens (in the case of a shaper), OR
  discard/marked-down (in the case of a policer).
If the bucket fills to its specified capacity (max burst size) , newly arriving tokens are discarded.
A token bucket permits burstiness, but bounds (shape/police) it.

## Slide 69
The token bucket algorithm provides users with three actions/categories for each in-bound (incoming) packet, in case of Traffic Policing configured :
  a conform action– Config. to transmit packet,
  an exceed action– Config. to transmit packet but with lower priority, and
  an optional violate – Drop the packet.

## Slide 70: Leaky Bucket vs Token Bucket
Leaky Bucket
Discard:
  Packets
Rate:
  fixed rate (perfect)
Arriving Burst:
  Waits in bucket
Token Bucket
Discard:
  Tokens
  Packet management separate
Rate:
  Average rate
  Bursts allowed
Arriving Burst:
  Can be sent immediately

## Slide 71: Intserv: QoS guarantee scenario
Resource reservation
  call setup, signaling (RSVP)
  traffic, QoS declaration
  per-element admission control
  QoS-sensitive scheduling (e.g., WFQ)
request/
reply

## Slide 72: From Relative to Absolute Service
Priority mechanisms can only deliver absolute assurances if total load is regulated
Service Level Agreements (SLAs) specify:
  Amount user (organization, etc.) can send
  Level of service delivered to that traffic
DiffServ offers low (but unspecified) delay and no drops
  Acceptance of proposed SLAs managed by “Bandwidth Broker”
  Only over long time scales

## Slide 73: Inter-Domain Premium DiffServ
Goal of IntServ: end-to-end bandwidth guarantees
Mechanism: end-to-end bandwidth reservations
  Like the telephone network, circuit reservations
  End hosts ask for reserved capacity from the network
AS-1
AS-2
Please reserve 1 Mbps
?
?
?
?
?
?
?

## Slide 74: High-Level IntServ Design
Reservations are made by endpoints
  Applications know their own requirements
  Applications run on end-hosts
  Network does not need to guess about requirements
Guarantees are end-to-end on a per-flow basis
Soft-state
  State in routers constantly refreshed by endpoints

## Slide 75: Requirements for IntServ
Fixed, stable paths
  Only routers on the path know about the reservation
  Current Internet cannot guarantee this
Routers maintain per-flow state
  Very high overhead (even with soft-state)
State is used to reserve bandwidth
  Guarantees QoS for reserved flows
  … but some flows may not be admitted

## Slide 76: RSVP Reservation Protocol
Performs signaling to set up reservation state
  Initiated by the receiver
Each reservation is a simplex data flow sent to a unicast or multicast address
  <Destination IP, protocol # (TCP, UDP), port #>
Multiple senders/receivers can be in the same session

## Slide 77: RSVP Example
PATH
PATH
RESV
Soft-state: PATH and RESV need to be periodically refreshed

## Slide 78: IntServ Summary
The good:
  Reservations are guaranteed and precise
    Reserved bandwidth is not shared with a class
    Tight allocations for each flow
  Soft-state slightly reduces overhead on routers
The bad:
  IntServ is a whole Internet upgrade
  Heavyweight mechanisms, per flow state
  Security: end-hosts can DoS by reserving lots of bandwidth

## Slide 79: Call Admission
Arriving session must :
Declare its QOS requirement
  R-spec: defines the QOS being requested
Characterize traffic it will send into network
  T-spec: defines traffic characteristics
Signaling protocol: needed to carry R-spec and T-spec to routers (where reservation is required)
  RSVP

## Slide 80: RSVP request (T-Spec)
A token bucket specification
  bucket size, b
  token rate, r
  the packet is transmitted onward only if the number of tokens in the bucket is at least as large as the packet
peak rate, p
  p > r
maximum packet size, M
minimum policed unit, m
  All packets less than m bytes are considered to be m bytes
  Reduces the overhead to process each packet
  Bound the bandwidth overhead of link-level headers

## Slide 81: RSVP request (R-spec)
An indication of the QoS control service requested
  Controlled-load service and Guaranteed service
For Controlled-load service
  Simply a Tspec
For Guaranteed service
  A Rate (R) term, the bandwidth required
    R  r, extra bandwidth will reduce queuing delays
  A Slack (S) term
    The difference between the desired delay and the delay that would be achieved if rate R were used
    With a zero slack term, each router along the path must reserve R bandwidth
    A nonzero slack term offers the individual routers greater flexibility in making their local reservation
    Number decreased by routers on the path.

## Slide 82: Comparison of Intserv & Diffserv Architectures
 | Intserv | Diffserv
Granularity of service differentiation | Individual Flow | Aggregate of flows
State in routers (e.g. scheduling, buffer management) | Per Flow | Per Aggregate
Traffic Classification Basis | Several Header Fields | DS
Type of Service Differentiation | Deterministic of statistical quarantees | Absolute or relative assurance
Admission Control | Required | Required for absolute differentiation
Signaling Protocol | RSVP | Not required for relative schemes

## Slide 83: Comparison of Intserv & Diffserv Architectures
 | Intserve | Diffserv
Coordination for service differentiation | End-to-End | Local (Per-Hop)
Scope of Service Differentiation | A Unicast or Multicast path | Anywhere in a network or in specific paths
Scalability | Limited by the number of flows | Limited by the number of classes of services
Network Accounting | Based on flow characteristics and QoS requirement | Based on class usage
Network Management | Similar to Circuit Switching Networks | Similar to existing IP networks
Inter-domain deployment | Multilateral agreements | Bilateral Agreement

## Slide 84: Advantages of DiffServ
Giving priority does improve performance
  … at the expense of reduced perf. for lower classes
Relatively lightweight solution
  Some overhead on ingress/egress routers
  No per flow state, low overhead on core routers
Easy to deploy
  No hard reservations
  No advanced setup of flows
  No end-to-end negotiation

## Slide 85: Disadvantages of DiffServ
No performance guarantees
  All gains are relative, not absolute
  Classes are very coarse
    i.e. all packets of a specific class get better performance
    No per flow or per destination QoS
  What if some ASs do not support DiffServ?
  Impossible to predict end-to-end behavior
Security
  Any host can tag traffic as high priority
  E.g. Win 2K tagged all traffic as high priority by default