## Slide 1: CS 540 Computer Networks II
Sandy Wang
chwang_98@yahoo.com
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2: Introduction to Network Security
Guest Lecture
Debabrata Dash

## Slide 3: Outline
Security Vulnerabilities
DoS and DDoS
Firewalls
Intrusion Detection Systems

## Slide 4: Security Vulnerabilities
Attacks on Different Layers
  IP Attacks
  ICMP Attacks
  Routing Attacks
  TCP Attacks
  Application Layer Attacks

## Slide 5: Why?
TCP/IP was designed for connectivity
  Assumed to have lots of trust
Host implementation vulnerabilities
  Software “had/have/will have” bugs
  Some elements in the specification were left to the implementers

## Slide 6: Security Flaws in IP
The IP addresses are filled in by the originating host
  Address spoofing
Using source address for authentication
  r-utilities (rlogin, rsh, rhosts etc..)
Internet
2.1.1.1
C
1.1.1.1
1.1.1.2
A
B
1.1.1.3
S
Can A claim it is B to the server S?
  ARP Spoofing
Can C claim it is B to the server S?
  Source Routing

## Slide 7: Security Flaws in IP
IP fragmentation attack
  End hosts need to keep the fragments till all the fragments arrive
Traffic amplification attack
  IP allows broadcast destination
  Problems?

## Slide 8: Ping Flood
Attacking System
Internet
Broadcast Enabled Network
Victim System

## Slide 9: ICMP Attacks
No authentication
ICMP redirect message
  Can cause the host to switch gateways
  Benefit of doing this?
    Man in the middle attack, sniffing
ICMP destination unreachable
  Can cause the host to drop connection
ICMP echo request/reply
Many more…
  http://www.sans.org/rr/whitepapers/threats/477.php

## Slide 10: Routing Attacks
Distance Vector Routing
  Announce 0 distance to all other nodes
    Blackhole traffic
    Eavesdrop
Link State Routing
  Can drop links randomly
  Can claim direct link to any other routers
BGP
  ASes can announce arbitrary prefix
  ASes can alter path

## Slide 11: TCP Attacks
Issues?
  Server needs to keep waiting for ACK y+1
  Server recognizes Client based on IP address/port and y+1
Client
Server
SYN x
SYN y | ACK x+1
ACK y+1

## Slide 12: TCP Layer Attacks
TCP SYN Flooding
  Exploit state allocated at server after initial SYN packet
  Send a SYN and don’t reply with ACK
  Server will wait for 511 seconds for ACK
  Finite queue size for incomplete connections (1024)
  Once the queue is full it doesn’t accept requests

## Slide 13: TCP Layer Attacks
TCP Session Hijack
  When is a TCP packet valid?
    Address/Port/Sequence Number in window
  How to get sequence number?
    Sniff traffic
    Guess it
      Many earlier systems had predictable ISN
  Inject arbitrary data to the connection

## Slide 14: TCP Layer Attacks
TCP Session Poisoning
  Send RST packet
    Will tear down connection
  Do you have to guess the exact sequence number?
    Anywhere in window is fine
    For 64k window it takes 64k packets to reset
    About 15 seconds for a T1

## Slide 15: Application Layer Attacks
Applications don’t authenticate properly
Authentication information in clear
  FTP, Telnet, POP
DNS insecurity
  DNS poisoning
  DNS zone transfer

## Slide 16: An Example
Shimomura (S)
Trusted (T)
Mitnick
Finger
Finger @S
showmount –e
Send 20 SYN packets to S
Attack when no one is around
What other systems it trusts?
Determine ISN behavior
Showmount -e
SYN

## Slide 17: An Example
Shimomura (S)
Trusted(T)
Mitnick
Finger @S
showmount –e
Send 20 SYN packets to S
SYN flood T
Attack when no one is around
What other systems it trusts?
Determine ISN behavior
T won’t respond to packets
Syn flood
X

## Slide 18: An Example
Shimomura (S)
trusted (T)
Mitnick (M)
Finger @S
showmount –e
Send 20 SYN packets to S
SYN flood T
Send SYN to S spoofing as T
Send ACK to S with a guessed number
Attack when no one is around
What other systems it trusts?
T won’t respond to packets
S assumes that it has a session with T
X
SYN
SYN|ACK
ACK

## Slide 19: An Example
Shimomura (S)
Trusted (T)
Mitnick
Finger @S
showmount –e
Send 20 SYN packets to S
SYN flood T
Send SYN to S spoofing as T
Send ACK to S with a guessed number
Send “echo + + > ~/.rhosts”
Attack when no one is around
What other systems it trusts?
Determine ISN behavior
T won’t respond to packets
S assumes that it has a session with T
Give permission to anyone from anywhere
X
++ > rhosts

## Slide 20: Outline
Security Vulnerabilities
DoS and D-DoS
Firewalls
Intrusion Detection Systems

## Slide 21: Denial of Service
Objective  make a service unusable, usually by overloading the server or network
Consume host resources
  TCP SYN floods
  ICMP ECHO (ping) floods
Consume bandwidth
  UDP floods
  ICMP floods

## Slide 22: Denial of Service
Crashing the victim
  Ping-of-Death
  TCP options (unused, or used incorrectly)
Forcing more computation
  Taking long path in processing of packets

## Slide 23: Simple DoS
Attacker
Victim
Victim
Victim
The Attacker usually spoofed source address to hide origin
Easy to block

## Slide 24: Coordinated DoS
Attacker
Victim
Victim
Victim
Attacker
Attacker
The first attacker attacks a different victim to cover up the real attack
The Attacker usually spoofed source address to hide origin
Harder to deal with

## Slide 25: Distributed DoS - DDoS
Attacker
Handler
Handler
Agent
Agent
Agent
Agent
Agent
Victim

## Slide 26: Distributed DoS
The handlers are usually very high volume servers
  Easy to hide the attack packets
The agents are usually home users with DSL/Cable
  Already infected and the agent installed
Very difficult to track down the attacker

## Slide 27: Outline
Security Vulnerabilities
DoS and D-DoS
Firewalls
Intrusion Detection Systems

## Slide 28: Firewalls
Lots of vulnerabilities on hosts in network
Users don’t keep systems up to date
  Lots of patches
  Lots of exploits in wild (no patch for them)
Solution?
  Limit access to the network
  Put firewalls across the perimeter of the network

## Slide 29: Firewalls (contd…)
Firewall inspects traffic through it
Allows traffic specified in the policy
Drops everything else
Two Types
  Packet Filters, Proxies
Internet
Internal Network
Firewall

## Slide 30: Packet Filters
Packet filter selectively passes packets from one network interface to another
Usually done within a router between external and internal networks
  screening router
Can be done by a dedicated network element
  packet filtering bridge
  harder to detect and attack than screening routers

## Slide 31: Packet Filters Contd.
Data Available
  IP source and destination addresses
  Transport protocol (TCP, UDP, or ICMP)
  TCP/UDP source and destination ports
  ICMP message type
  Packet options (Fragment Size etc.)
Actions Available
  Allow the packet to go through
  Drop the packet (Notify Sender/Drop Silently)
  Alter the packet (NAT?)
  Log information about the packet

## Slide 32: Packet Filters Contd.
Example filters
  Block all packets from outside except for SMTP servers
  Block all traffic to a list of domains
  Block all connections from a specified domain

## Slide 33: Typical Firewall Configuration
Internal hosts can access DMZ and Internet
External hosts can access DMZ only, not Intranet
DMZ hosts can access Internet only
Advantages?
  If a service gets compromised in DMZ it cannot affect internal hosts
Internet
Intranet
DMZ
X
X

## Slide 34: Example Firewall Rules
Stateless packet filtering firewall
Rule  (Condition, Action)
Rules are processed in top-down order
  If a condition satisfied – action is taken

## Slide 35: Sample Firewall Rule
Dst Port
Alow
Allow
Yes
Any
> 1023
22
TCP
22
TCP
> 1023
Ext
Int
Out
SSH-2
Int
Ext
In
SSH-1
Dst Addr
Proto
Ack Set?
Action
Src Port
Src Addr
Dir
Rule
Allow SSH from external hosts to internal hosts
  Two rules
    Inbound and outbound
  How to know a packet is for SSH?
    Inbound: src-port>1023, dst-port=22
    Outbound: src-port=22, dst-port>1023
    Protocol=TCP
  Ack Set?
SYN
SYN/ACK
ACK
Client
Server

## Slide 36: Default Firewall Rules
Egress Filtering
  Outbound traffic from external address  Drop
  Benefits?
Ingress Filtering
  Inbound Traffic from internal address  Drop
  Benefits?
Default Deny
  Why?
Any
Dst Port
Any
Deny
Any
Any
Int
Any
Int
In
Ingress
Deny
Any
Any
Ext
Any
Ext
Out
Egress
Any
Deny
Any
Any
Any
Any
Any
Any
Default
Dst Addr
Proto
Ack Set?
Action
Src Port
Src Addr
Dir
Rule

## Slide 37: Packet Filters
Advantages
  Transparent to application/user
  Simple packet filters can be efficient
Disadvantages
  Usually fail open
  Very hard to configure the rules
  Doesn’t have enough information to take actions
    Does port 22 always mean SSH?
    Who is the user accessing the SSH?

## Slide 38: Alternatives
Stateful packet filters
  Keep the connection states
  Easier to specify rules
  More popular
  Problems?
    State explosion
    State for UDP/ICMP?

## Slide 39: Alternatives
Proxy Firewalls
  Two connections instead of one
  Either at transport level
    SOCKS proxy
  Or at application level
    HTTP proxy
Requires applications (or dynamically linked libraries) to be modified to use the proxy

## Slide 40: Proxy Firewall
Data Available
  Application level information
  User information
Advantages?
  Better policy enforcement
  Better logging
  Fail closed
Disadvantages?
  Doesn’t perform as well
  One proxy for each application
  Client modification

## Slide 41: Outline
Security Vulnerabilities
DoS and DDoS
Firewalls
Intrusion Detection Systems

## Slide 42: Intrusion Detection Systems
Firewalls allow traffic only to legitimate hosts and services
Traffic to the legitimate hosts/services can have attacks
Solution?
  Intrusion Detection Systems
  Monitor data and behavior
  Report when identify attacks

## Slide 43: Types of IDS
Host-based
Network-based
Signature-based
Anomaly-based

## Slide 44: Signature-based IDS
Characteristics
  Uses known pattern matching to signify attack
Advantages?
  Widely available
  Fairly fast
  Easy to implement
  Easy to update
Disadvantages?
  Cannot detect attacks for which it has no signature

## Slide 45: Anomaly-based IDS
Characteristics
  Uses statistical model or machine learning engine to characterize normal usage behaviors
  Recognizes departures from normal as potential intrusions
Advantages?
  Can detect attempts to exploit new and unforeseen vulnerabilities
  Can recognize authorized usage that falls outside the normal pattern
Disadvantages?
  Generally slower, more resource intensive compared to signature-based IDS
  Greater complexity, difficult to configure
  Higher percentages of false alerts

## Slide 46: Network-based IDS
Characteristics
  NIDS examine raw packets in the network passively and triggers alerts
Advantages?
  Easy deployment
  Unobtrusive
  Difficult to evade if done at low level of network operation
Disadvantages?
  Fail Open
  Different hosts process packets differently
  NIDS needs to create traffic seen at the end host
  Need to have the complete network topology and complete host behavior

## Slide 47: Host-based IDS
Characteristics
  Runs on single host
  Can analyze audit-trails, logs, integrity of files and directories, etc.
Advantages
  More accurate than NIDS
  Less volume of traffic so less overhead
Disadvantages
  Deployment is expensive
  What happens when host get compromised?

## Slide 48: Summary
TCP/IP security vulnerabilities
  Spoofing
  Flooding attacks
  TCP session poisoning
DOS and D-DOS
Firewalls
  Packet Filters
  Proxy
IDS
  Signature and Anomaly IDS
  NIDS and HIDS

## Slide 49: Password Cracking: Dictionary Attack & Brute Force
Pattern | Calculation | Result | Time to Guess (2.6x1018/month)
Personal Info: interests, relatives |  | 20 | Manual 5 minutes
Social Engineering |  | 1 | Manual 2 minutes
American Dictionary |  | 80,000 | < 1 second
4 chars: lower case alpha | 264 | 5x105 | 
8 chars: lower case alpha | 268 | 2x1011 | 
8 chars: alpha | 528 | 5x1013 | 
8 chars: alphanumeric | 628 | 2x1014 | 3.4 min.
8 chars alphanumeric +10 | 728 | 7x1014 | 12 min.
8 chars: all keyboard | 958 | 7x1015 | 2 hours
12 chars: alphanumeric | 6212 | 3x1021 | 96 years
12 chars: alphanumeric + 10 | 7212 | 2x1022 | 500 years
12 chars: all keyboard | 9512 | 5x1023 | 
16 chars: alphanumeric | 6216 | 5x1028 | 
Notes: Calculation = <number of possible characters> to the <password length> power
Result is maximum number of guesses needed to find the right password.
This is taken from NIST, and assumes many computers are used in parallel to crack a password. Think criminal effort potentially using bots.