## Slide 1: CS 540 Computer Networks II
Sandy Wang
chwang_98@yahoo.com
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2
7. MPLS
Notes: In this chapter, we look at the underlying technology and protocol architecture
of LANs. Chapters 12 and 13 are devoted to a discussion of specific
LAN systems.

## Slide 3: Topics
  Overview
  LAN Switching
  IPv4
  IPv6
  Routing Protocols -- RIP, RIPng, OSPF
  Routing Protocols -- ISIS, BGP
  MPLS
  Midterm Exam
  Transport Layer -- TCP/UDP
  Congestion Control & Quality of Service (QoS)
  Access Control List (ACL)
  Application Layer Protocols
  Application Layer Protocols continue
  Others – Multicast, SDN
  Final Exam

## Slide 4: Reference Books
Cisco CCNA Routing and Switching ICND2 200-101 Official Cert Guide, Academic Edition by Wendel Odom -- July 10, 2013. ISBN-13: 978-1587144882
The TCP/IP Guide: A Comprehensive, Illustrated Internet Protocols Reference by Charles M. Kozierok – October 1, 2005. ISBN-13: 978-1593270476
Data and Computer Communications (10th Edition) (William Stallings Books on Computer and Data Communications) by Williams Stallings – September 23, 2013. ISBN-13: 978-0133506488
http://class.svuca.edu/~sandy/class/CS540/

## Slide 5: Virtual Private LAN Service (VPLS)
VPLS defines an architecture allows MPLS networks offer Layer 2 multipoint Ethernet Services
SP emulates an IEEE Ethernet bridge network (virtual)
Virtual Bridges linked with MPLS Pseudo Wires
  Data Plane used is same as EoMPLS (point-to-point)
PE
PE
CE
CE
VPLS is an Architecture
CE

## Slide 6: Virtual Private LAN Service
End-to-end architecture that allows MPLS networks to provide Multipoint Ethernet services
It is “Virtual” because multiple instances of this service share the same physical infrastructure
It is “Private” because each instance of the service is independent and isolated from one another
It is “LAN Service” because it emulates Layer 2 multipoint connectivity between subscribers

## Slide 7: Why Provide A Layer 2 Service?
Customer have full operational control over their routing neighbours
Privacy of addressing space - they do not have to be shared with the carrier network
Customer has a choice of using any routing protocol including non IP based (IPX, AppleTalk)
Customers could use an Ethernet switch instead of a router as the CPE
A single connection could reach all other edge points emulating an Ethernet LAN (VPLS)

## Slide 8: VPLS Components
N-PE
MPLS Core
CE router
CE router
CE switch
CE router
CE router
CE switch
CE switch
CE router
Attachment circuits
Port or VLAN mode
Mesh of LSP between N-PEs
N-PE
N-PE
Pseudo Wires within LSP
Virtual Switch Interface (VSI) terminates PW and provides Ethernet bridge function
Targeted LDP between PEs to exchange VC labels for Pseudo Wires
Attachment CE
can be a switch or router

## Slide 9: Virtual Switch Interface
Flooding / Forwarding
  MAC table instances per customer (port/vlan) for each PE
  VFI will participate in learning and forwarding process
  Associate ports to MAC, flood unknowns to all other ports
Address Learning / Aging
  LDP enhanced with additional MAC List TLV (label withdrawal)
  MAC timers refreshed with incoming frames
Loop Prevention
  Create full-mesh of Pseudo Wire VCs (EoMPLS)
  Unidirectional LSP carries VCs between pair of N-PE Per
  A VPLS use “split horizon” concepts to prevent loops

## Slide 10: Pseudo Wire Reference Model (RFC 3916)
A Pseudo Wire (PW) is a connection between two provider edge devices connecting two attachment circuits (ACs)
In an MPLS core a Pseudo Wire uses two MPLS labels
  Tunnel Label (LSP) identifying remote PE router
  VC Label identifying Pseudo Wire circuit within tunnel
Emulated Service
IP/MPLS
PE1
Attachment Circuit
Pseudo Wire PDUs
Customer Site
Customer Site
Customer Site
Customer Site
PSN Tunnel (LSP in MPLS)
Packet Switched Network (PSN) IP or MPLS
Pseudo Wire
PE2
CE
PW1
PW2
CE
CE
CE
Notes: A PWES is either: - an Ethernet link or a VLAN link between two ports, or - an ATM VC or VP, or - a Frame Relay VC, or - a TDM circuit, or - an MPLS LSP
Note that the PSN tunnel may be MPLS, L2TP, GRE and so on .. UTI is another mechanism to transport the PDUs between ingress and egress PE – in this case the PW is created using a UTI tunnel.

## Slide 11: PW Encapsulation over MPLS (RFC 4448)
Ethernet Pseudo Wires use 3 layers of encapsulation
  Tunnel Encapsulation (zero, one or more MPLS Labels)
  To get PDU from ingress to egress PE;
  Could be an MPLS label (LDP, TE), GRE tunnel, L2TP tunnel
  Pseudo Wire Demultiplexer (PW Label)
  To identify individual circuits within a tunnel;
  Obtained from Directed LDP session
  Control Word (Optional)
    The following is supported when carrying Ethernet
      Provides the ability to sequence individual frames
      Avoidance of equal-cost multiple-path load-balancing
      Operations and Management (OAM) mechanisms
Control word format varies depending on transported PDU
Tunnel Label
PW
Label
Control Word
Layer 2
PDU
Notes: Cisco implementation allows only 1 key per GRE tunnel – GRE code would need to be enhanced to provide multiple keys per GRE tunnel to allow for demultiplexer field implementation.

## Slide 12
CE4
P2
P1
PE2
CE2
CE1
CE5
PE3
VPN B
VPN B
PE1
P3
P4
PE4
CE3
CE6
CE7
CE8
CE9
A
B
C
D
E
L
K
J
N
G
M
H
F
VPN B
VPN A
VPN A
VPN A

## Slide 13: Network point of view from VPN-B
CE3
CE8
CE6
CE9
F

## Slide 14
CE4
PE2
CE2
CE1
CE5
PE3
PE1
CE7
A
B
C
D
E
L
K
J
N
G
M
H
VPN A
VPN A
VPN A
if1
if2

## Slide 15: Ethernet PW Tunnel Encapsulation
Tunnel Encapsulation
  One or more MPLS labels associated with the tunnel
  Defines the LSP from ingress to egress PE router
  Can be derived from LDP+IGP, RSVP-TE, BGP IPv4+Label
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
EXP
TTL (set to 2)
VC Label (VC)
1
Tunnel Label (LDP,RSVP,BGP)
Layer-2 PDU
0 0 0 0
Reserved
Sequence Number
EXP
TTL
0
PW Demux
Tunnel Encaps
Control Word

## Slide 16: Ethernet PW Demultiplexer
VC Label
  Inner label used by receiving PE to determine the following
    Egress interface for L2PDU forwarding (Port based)
    Egress VLAN used on the CE facing interface (VLAN Based)
EXP can be set to the values received in the L2 frame
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
EXP
TTL (set to 2)
VC Label (VC)
1
Tunnel Label (LDP,RSVP,BGP)
Layer-2 PDU
0 0 0 0
Reserved
Sequence Number
EXP
TTL
0
PW Demux
Tunnel Encaps
Control Word
Notes: If using LDP, liberal retention mode should be used but conservative label retention must be implemented

## Slide 17: Ethernet PW Control Word
Control Word is Optional (as per RFC)
  0 0 0 0 First nibble is 0x0 to prevent aliasing with IP Packets over MPLS (MAC addresses that start with 0x4 or 0x6)
  Reserved Should be all zeros, ignored on receive
  Seq number provides sequencing capability to detect out of order packets - currently not in Cisco’s implementation – processing is optional
EXP
TTL (set to 2)
VC Label (VC)
1
Tunnel Label (LDP,RSVP,BGP)
Layer-2 PDU
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
PW Demux
Tunnel Encaps
Control Word
0 0 0 0
Reserved
Sequence Number
EXP
TTL
0

## Slide 18: PW Operation and Encapsulation
P2
P1
IP/MPLS
Customer Site
Customer Site
Directed LDP Session between PE1 and PE2
PE2
CE
CE
LSP
“PW1”
Lo0:
Label 24
for Lo0:
Label Pop
for Lo0:
Label 38
for Lo0:
Label 72
for PW1
PE1
LDP Session
LDP Session
LDP Session
24
72
L2 PDU
This process happens in both directions
  (Example shows process for PE2  PE1 traffic)
38
72
L2 PDU
72
L2 PDU
Notes: A PWES is either: - an Ethernet link or a VLAN link between two ports, or - an ATM VC or VP, or - a Frame Relay VC, or - a TDM circuit, or - an MPLS LSP
Note that the PSN tunnel may be MPLS, L2TP, GRE and so on .. UTI is another mechanism to transport the PDUs between ingress and egress PE – in this case the PW is created using a UTI tunnel.

## Slide 19: VPLS Flooding & Forwarding
Flooding (Broadcast, Multicast, Unknown Unicast)
Dynamic learning of MAC addresses on PHY and VCs
Forwarding
  Physical Port
  Virtual Circuit
Data
SA
DA?
Unknown DA?
Pseudo Wire in LSP
Notes: Frame Forwarding Requirements
- MAC address to VC-LSP association is required
- Dynamically learn MAC addresses on PHY ports and VCs
- Forward

## Slide 20: MAC Address Learning and Forwarding
Broadcast, Multicast, and Unknown Unicast are learned via the received label associations
Two LSPs associated with a VC (Tx & Rx)
If inbound or outbound LSP is down
  Then the entire Pseudo Wire is considered down
PE1
PE2
Send me frames using Label 170
Send me frames using Label 102
CE
CE
E0/0
E0/1
MAC 2 E0/1
MAC Address Adj
MAC 1 102
MAC 2 170
MAC Address Adj
MAC 1 E0/0
Use VC
Label 102
MAC1
Use VC
Label 170
MAC2
PE2
170
MAC2
MAC1
Data
PE2
102
MAC1
MAC2
Data
Directed LDP
Notes: Assume a packet from A1 is bound for A2. When it leaves CE1, say it has a source MAC address of M1 and a destination MAC of M2. If PE1 does not know where M2 is, it will multicast the packet to PE2 and PE3. When PE2 receives the packet, it will have an inner label of 201. PE2 can conclude that the source MAC address M1 is behind PE1, since it distributed the label 201 to PE1. It can therefore associate MAC address M1 with VC Label 102.

## Slide 21: VPLS Topology – PE View
MPLS
Each PE has a P2MP view of all other PEs it sees it self as a root bridge with split horizon loop protection
Full mesh topology obviates STP in the SP network
Customer STP is transparent to the SP / Customer BPDUs are forwarded transparently
PEs
CEs
PE view
Full Mesh LDP
Ethernet PW to each peer

## Slide 22: VPLS Topology – CE View
MPLS
PEs
CEs
PE view
Full Mesh LDP
Ethernet PW to each peer
CE routers/switches see a logical Bridge/LAN
VPLS emulates a LAN – but not exactly…
  This raises a few issues which are discussed later
MPLS VPLS Core
MPLS
CEs

## Slide 23: Direct Attachment VPLS (Flat Architecture)
CE
N-PE
MPLS Core
N-PE
CE
Ethernet (VLAN/Port
Ethernet (VLAN Port)
Full Mesh PWs + LDP
MAC2
MAC1
Data
PE
VC
MAC2
MAC1
Data
MAC2
MAC1
Data
802.1q Customer
Pseudo Wire SP Core

## Slide 24
CE4
PE2
CE2
CE1
CE5
PE3
PE1
CE7
A
B
C
D
E
L
K
J
N
G
M
H
VPN A
VPN A
VPN A
if1
if2
MAC | Intf
A | if1

## Slide 25
CE4
P2
P1
PE2
CE2
CE1
CE5
PE3
VPN B
VPN B
PE1
P3
P4
PE4
CE3
CE6
CE7
CE8
CE9
A
B
C
D
E
L
K
J
N
G
M
H
F
VPN B
VPN A
VPN A
VPN A
410
235
300
200

## Slide 26
CE4
PE2
CE2
CE1
CE5
PE3
PE1
CE7
A
B
C
D
E
L
K
J
N
G
M
H
VPN A
VPN A
VPN A
if1
if2
MAC | Intf
A | If1
B | If1
C | If2
D | If2
E | If2
F | 200,410
H | 200,410
J | 200,410
K | 200,410
L | 200,410
M | 300, 235
N | 300, 235