## Slide 1: CS 540 Computer Networks II
Sandy Wang
chwang_98@yahoo.com
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2
5. Routing Protocols – RIP & OSPF
Notes: In this chapter, we look at the underlying technology and protocol architecture
of LANs. Chapters 12 and 13 are devoted to a discussion of specific
LAN systems.

## Slide 3: Topics
  Overview
  LAN Switching
  IPv4
  IPv6
  Tunnels ---------------- 6/15, 6/16
  RIP, RIPng, OSPF ---------------- 6/22, 6/23
  ISIS, BGP ------------------ 6/29, 6/30
  Midterm Exam ------------------- 7/6, 7/7
  MPLS
  Transport Layer -- TCP/UDP
  Congestion Control & Quality of Service (QoS)
  Access Control List (ACL)
  Application Layer Protocols
  Others – Multicast, SDN
  Final Exam

## Slide 4: Reference Books
Cisco CCNA Routing and Switching ICND2 200-101 Official Cert Guide, Academic Edition by Wendel Odom -- July 10, 2013. ISBN-13: 978-1587144882
The TCP/IP Guide: A Comprehensive, Illustrated Internet Protocols Reference by Charles M. Kozierok – October 1, 2005. ISBN-13: 978-1593270476
Data and Computer Communications (10th Edition) (William Stallings Books on Computer and Data Communications) by Williams Stallings – September 23, 2013. ISBN-13: 978-0133506488
http://class.svuca.edu/~sandy/class/CS540/

## Slide 5: Topics:
RIP
OSPF

## Slide 6: Introduction

## Slide 7
A
B
C
D
E
 | A | B | C | D | E
A | 0 | 1 | 1 | 1 | ∞
B | 1 | 0 | ∞ | ∞ | 1
C | 1 | ∞ | 0 | 1 | ∞
D | 1 | ∞ | 1 | 0 | 1
E | ∞ | 1 | ∞ | 1 | 0
Notes: A

## Slide 8
A
B
C
D
E
C: Routing Table
D: Routing Table
E: Routing Table
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | ∞ | ?
A: Routing Table
B: Routing Table
 | Cost | Nexthop
A | 1 | A
B | 0 | --
C | ∞ | ?
D | ∞ | ?
E | 1 | E
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 0 | --
D | 1 | D
E | ∞ | ?
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 1 | C
D | 0 | --
E | 1 | E
 | Cost | Nexthop
A | ∞ | ?
B | 1 | B
C | ∞ | ?
D | 1 | D
E | 0 | --
Notes: A

## Slide 9
A
B
C
D
E
C  A
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | ∞ | ?
A: Routing Table
B  A
 | Cost | Nexthop
A | 1 | A
B | 0 | --
C | ∞ | ?
D | ∞ | ?
E | 1 | E
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 0 | --
D | 1 | D
E | ∞ | ?
D  A
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 1 | C
D | 0 | --
E | 1 | E
Notes: A

## Slide 10
A
B
C
D
E
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | ∞ | ?
A: Routing Table
B  A
 | Cost | Nexthop
A | 1 | A
B | 0 | --
C | ∞ | ?
D | ∞ | ?
E | 1 | E
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | 2 | B
A: Routing Table
Notes: A

## Slide 11
A
B
C
D
E
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | 2 | B
A: Routing Table
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | 2 | B
A: Routing Table
C  A
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 0 | --
D | 1 | D
E | ∞ | ?
Notes: A

## Slide 12
A
B
C
D
E
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | 2 | B, D
A: Routing Table
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | 2 | B
A: Routing Table
D  A
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 1 | C
D | 0 | --
E | 1 | E
Notes: A

## Slide 13
A
B
C
D
E
E  B
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | ∞ | ?
A  B
B: Routing Table
 | Cost | Nexthop
A | 1 | A
B | 0 | --
C | 2 | A
D | 2 | A, E
E | 1 | E
 | Cost | Nexthop
A | ∞ | ?
B | 1 | B
C | ∞ | ?
D | 1 | D
E | 0 | --
B: Routing Table
 | Cost | Nexthop
A | 1 | A
B | 0 | --
C | ∞ | ?
D | ∞ | ?
E | 1 | E
Notes: A

## Slide 14
A
B
C
D
E
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | ∞ | ?
A  C
C: Routing Table
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 0 | --
D | 1 | D
E | ∞ | ?
C: Routing Table
 | Cost | Nexthop
A | 1 | A
B | 2 | A
C | 0 | --
D | 1 | D
E | 2 | D
D  C
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 1 | C
D | 0 | --
E | 1 | E
Notes: A

## Slide 15
A
B
C
D
E
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | ∞ | ?
A  D
D: Routing Table
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 1 | C
D | 0 | --
E | 1 | E
D: Routing Table
 | Cost | Nexthop
A | 1 | A
B | 2 | A, E
C | 1 | C
D | 0 | --
E | 1 | E
C  D
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 0 | --
D | 1 | D
E | ∞ | ?
E  D
 | Cost | Nexthop
A | ∞ | ?
B | 1 | B
C | ∞ | ?
D | 1 | D
E | 0 | --
Notes: A

## Slide 16
A
B
C
D
E
E: Routing Table
 | Cost | Nexthop
A | ∞ | ?
B | 1 | B
C | ∞ | ?
D | 1 | D
E | 0 | --
E: Routing Table
 | Cost | Nexthop
A | 2 | B, D
B | 1 | B
C | 2 | D
D | 1 | D
E | 0 | --
B  E
 | Cost | Nexthop
A | 1 | A
B | 0 | --
C | ∞ | ?
D | ∞ | ?
E | 1 | E
D  E
 | Cost | Nexthop
A | 1 | A
B | ∞ | ?
C | 1 | C
D | ∞ | ?
E | 1 | E
Notes: A

## Slide 17
A
B
C
D
E
 | Cost | Nexthop
A | 0 | --
B | 1 | B
C | 1 | C
D | 1 | D
E | 2 | B, D
A: Routing Table
E: Routing Table
 | Cost | Nexthop
A | 2 | B, D
B | 1 | B
C | 2 | D
D | 1 | D
E | 0 | --
D: Routing Table
 | Cost | Nexthop
A | 1 | A
B | 2 | A, E
C | 1 | C
D | 0 | --
E | 1 | E
C: Routing Table
 | Cost | Nexthop
A | 1 | A
B | 2 | A
C | 0 | --
D | 1 | D
E | 2 | D
 | Cost | Nexthop
A | 1 | A
B | 0 | --
C | 2 | A
D | 2 | A, E
E | 1 | E
B: Routing Table
Notes: A

## Slide 18
A
B
C
D
E
F
F: Routing Table
 | Cost | Nexthop
A | ∞ | ?
B | ∞ | ?
C | ∞ | ?
D | ∞ | ?
E | 1 | E
F | 0 | --
E  F
 | Cost | Nexthop
A | ∞ | ?
B | 1 | B
C | ∞ | ?
D | 1 | D
E | 0 | --
F | 1 | F
F: Routing Table
 | Cost | Nexthop
A | ∞ | ?
B | 2 | E
C | ∞ | ?
D | 2 | E
E | 1 | E
F | 0 | --
1st Update
Notes: A

## Slide 19
A
B
C
D
E
11.0.0.1
11.0.0.2
F
F: Routing Table
 | Cost | Nexthop
A | 3 | E
B | 2 | E
C | 3 | E
D | 2 | E
E | 1 | E
F | 0 | --
E  F
 | Cost | Nexthop
A | 2 | B, D
B | 1 | B
C | 2 | D
D | 1 | D
E | 0 | --
F | 1 | F
2nd Update
F: Routing Table
 | Cost | Nexthop
A | ∞ | ?
B | 2 | E
C | ∞ | ?
D | 2 | E
E | 1 | E
F | 0 | --
Notes: A

## Slide 20
F: Routing Table
Dst | Cost | Nexthop
11.0.0.0/16 | 3 | 17.0.0.5
12.0.0.0/16 | 2 | 17.0.0.5
13.0.0.0/16 | 3 | 17.0.0.5
14.0.0.0/16 | 3 | 17.0.0.5
15.0.0.0/16 | 3 | 17.0.0.5
16.0.0.0/16 | 2 | 17.0.0.5
17.0.0.0/16 | 1 | connected
A
B
C
D
E
11.0.0.0/16
F
.2
12.0.0.0/16
13.0.0.0/16
.1
14.0.0.0/16
15.0.0.0/16
16.0.0.0/16
17.0.0.0/16
.5
.6
.4
.3
Notes: A

## Slide 21: Characteristics of Distance Vector Routing
Periodic Updates: Updates to the routing tables are sent at the end of a certain time period. A typical value is 90 seconds.
Triggered Updates: If a metric changes on a link, a router immediately sends out an update without waiting for the end of the update period.
Full Routing Table Update: Most distance vector routing protocol send their neighbors the entire routing table (not only entries which change).
Route invalidation timers: Routing table entries are invalid if they are not refreshed. A typical value is to invalidate an entry if no update is received after 3-6 update periods.

## Slide 22: The Count-to-Infinity Problem
A
B
C
1
1

## Slide 23: Count-to-Infinity
The reason for the count-to-infinity problem is that each node only has a “next-hop-view”
For example, in the first step, A did not realize that its route (with cost 2) to C went through node B
How can the Count-to-Infinity problem be solved?

## Slide 24: Count-to-Infinity
The reason for the count-to-infinity problem is that each node only has a “next-hop-view”
For example, in the first step, A did not realize that its route (with cost 2) to C went through node B
How can the Count-to-Infinity problem be solved?
Solution: Never advertise the cost to a neighbor if this neighbor is the next hop on the current path (Split Horizon)
      Example: A would not send the first routing update to B, since B is the next hop on A’s current route to C
      Split Horizon does not solve count-to-infinity in all cases!

## Slide 25: Split Horizon and Poison Reverse
  One drawback of Split Horizon
    Normally, the DV protocol uses a timer and if there is no news about a route, the node deletes the route from its table
    In the previous e.g., node A cannot guess that this is due to split horizon or because B has not received any news about X recently
  Poison Reverse
    Node B can still advertise the value for X, but is the source of information is A, it can replace the distance with infinity as a warning

## Slide 26
Three-node instability
Update loop until infinity
If the instability is btw three nodes, stability cannot be guaranteed

## Slide 27: RIP - Routing Information Protocol
A simple intradomain protocol
Straightforward implementation of Distance Vector Routing
Each router advertises its distance vector every 30 seconds (or whenever its routing table changes) to all of its neighbors
RIP always uses 1 as link metric
Maximum hop count is 15, with “16” equal to “”
Routes are timeout (set to 16) after 3 minutes if they are not updated

## Slide 28: RIP - History
Late 1960s : Distance Vector protocols were used in the ARPANET
Mid-1970s: XNS (Xerox Network system) routing protocol is the precursor of RIP in IP (and Novell’s IPX RIP and Apple’s routing protocol)
1982 Release of routed for BSD Unix
1988 RIPv1 (RFC 1058) - classful routing
1993 RIPv2 (RFC 1388) - adds subnet masks with each route entry - allows classless routing
1998 Current version of RIPv2 (RFC 2453)

## Slide 29: RIP Packet Format
MAC Hdr
IP Hdr
RIP Hdr
RIP type-specific Data
MAC Header
    Src – MAC of sending interface
    Dst – 0100:5E00:0009
    Type – 0x0800
IP Header
  Src – IP addr of sending interface
  Dst – 224.0.0.9
  Protocol – UDP 17
UDP Header
  Port 520
UDP Hdr
MAC Header
  Dst – 3333:0000:0009
  Type – 0x86DD
IPv6 Header
  Src – IPv6 addr of sending interface
  Dst – FF02::9
  Protocol – UDP 17
UDP Header
  Port 521
Notes: 01:00:5E:00:00:00 - 01:00:5E:7F:FF:FF 0x0800 IPv4 Multicast (RFC 1112), insert the low 23 Bits of the multicast IPv4 Address into the Ethernet Address (RFC 7042 2.1.1.)
33:33:xx:xx:xx:xx 0x86DD IPv6 Multicast (RFC 2464), insert the low 32 Bits of the multicast IPv6 Address into the Ethernet Address (RFC 7042 2.3.1.)
224.0.0.5 The Open Shortest Path First (OSPF) All OSPF Routers address is used to send Hello packets to all OSPF routers on a network segment.
224.0.0.6 The OSPF All Designated Routers ""(DR)"" address is used to send OSPF routin`g information to designated routers on a network segment.

## Slide 30: RIPv1 Packet Format
One RIP message can have up to 25 route entries
1: request 2: response
2: for IP
0…0: request full rou-ting table
Address of destination
Cost (measured in hops)
1: RIPv1

## Slide 31: RIPv2
RIPv2 is an extends RIPv1:
  Subnet masks are carried in the route information
  Authentication of routing messages
  Route information carries next-hop address
  Exploites IP multicasting
Extensions of RIPv2 are carried in unused fields of RIPv1 messages

## Slide 32: RIPv2 Packet Format
One RIP message can have up to 25 route entries
1: request 2: response
2: for IP
0…0: request full rou-ting table
Address of destination
Cost (measured in hops)
2: RIPv2

## Slide 33: RIPv2 Packet Format
Used to carry information from other routing protocols (e.g., autonomous system number)
Identifies a better next-hop address on the same subnet than the advertising router, if one exists (otherwise 0….0)
2: RIPv2
Subnet mask for IP address

## Slide 34: RIP Messages
This is the operation of RIP in routed. Dedicated port for RIP is UDP port 520.
Two types of messages:
  Request messages
    used to ask neighboring nodes for an update
  Response messages
    contains an update

## Slide 37: Routing with RIP
Initialization: Send a request packet (command = 1, address family=0..0) on all interfaces:
    RIPv1 uses broadcast if possible,
    RIPv2 uses multicast address 224.0.0.9, if possible
requesting routing tables from neighboring routers
Request received: Routers that receive above request send their entire routing table
Response received: Update the routing table
Regular routing updates: Every 30 seconds, send all or part of the routing tables to every neighbor in an response message
Triggered Updates: Whenever the metric for a route change, send entire routing table.

## Slide 38: RIP Security
Issue: Sending bogus routing updates to a router
RIPv1: No protection
RIPv2: Simple authentication scheme
2: plaintext password

## Slide 39: RIP Problems
RIP takes a long time to stabilize
  Even for a small network, it takes several minutes until the routing tables have settled after a change
RIP has all the problems of distance vector algorithms, e.g., count-to-Infinity
        RIP uses split horizon to avoid count-to-infinity
The maximum path in RIP is 15 hops

## Slide 40: Distance Vector vs. Link State Routing
With distance vector routing, each node has information only about the next hop:
    Node A: to reach F go to B
    Node B: to reach F go to D
    Node D: to reach F go to E
    Node E: go directly to F
Distance vector routing makes poor routing decisions if directions are not completely correct (e.g., because a node is down).
If parts of the directions incorrect, the routing may be incorrect until the routing algorithms has re-converged.
A
B
C
D
E
F

## Slide 41: Distance Vector vs. Link State Routing
In link state routing, each node has a complete map of the topology
If a node fails, each node can calculate the new route
Difficulty: All nodes need to have a consistent view of the network
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F

## Slide 42: Link State Routing: Properties
Each node requires complete topology information
Link state information must be flooded to all nodes
Guaranteed to converge

## Slide 43: Link State Routing: Basic princples
  1. Each router establishes a relationship (“adjacency”) with its neighbors
  2.Each router generates link state advertisements (LSAs) which are distributed to all routers
      LSA = (link id, state of the link, cost, neighbors of the link)
  3. Each router maintains a database of all received LSAs (topological database or link state database), which describes the network has a graph with weighted edges
  4. Each router uses its link state database to run a shortest path algorithm (Dijikstra’s algorithm) to produce the shortest path to each network

## Slide 44: Operation of a Link State Routing protocol
Received LSAs
IP Routing Table
Dijkstra’s
Algorithm
Link State Database
LSAs are flooded to other interfaces

## Slide 45: Dijkstra’s Shortest Path Algorithm for a Graph
Input: Graph (N,E) with N the set of nodes and E  N  N the set of edges
dvw link cost (dvw = infinity if (v,w)  E, dvv = 0)
s source node.
Output: Dn cost of the least-cost path from node s to node n
M = {s};
for each n  M
Dn = dsn;
while (M  all nodes) do
Find w  M for which Dw = min{Dj ; j  M};
Add w to M;
for each n  M
Dn = minw [ Dn, Dw + dwn ];
Update route;
enddo

## Slide 46: Introduction to OSPF Concepts
Introducing OSPF and Link State Concepts
Advantages of OSPF
Brief History
Terminology
Link State Concepts
Introducing the OSPF Routing Protocol
Metric based on Cost (Bandwidth)
Hello Protocol
Steps to OSPF Operation
DR/BDR
OSPF Network Types

## Slide 47: Brief History
1987 – Initial development of OSPF began by IETF OSPF working group
1989 – OSPFv1 published in RFC 1131. OSPFv1 was experimental and was never deployed.
1991 – OSPFv2 introduced in RFC 1247 by John Moy. It is classless by design.
1998 – OSPFv2 specification updated in RFC 2328 which remains the current RFC for OSPF
1999 – OSPFv3 for IPv6 published in RFC 2740
2008 – OSPFv3 updated in RFC 5340

## Slide 48: Features of OSPF
Classless
Efficient – no periodic updates. Use the SPF algorithm to choose the best path
Fast convergence
Scalable – Hierarchical
Secure – Support MD5 authentication

## Slide 49: Terminology
Link: Interface on a router
Link state: Description of an interface and of its relationship to its neighboring routers, including:
  IP address/mask of the interface,
  The type of network it is connected to
  The routers connected to that network
  The metric (cost) of that link
The collection of all the link-states would form a link-state database.

## Slide 50: Terminology
Router ID – Used to identify the routers in the OSPF network
  IP address configured with the OSPF router-id command (extra)
  Highest loopback address (configuration coming)
  Highest active IP address (any IP address)
Loopback address has the advantage of never going down, thus diminishing the possibility of having to re-establish adjacencies. (more in a moment)

## Slide 51: Terminology
Or “OSPF Routing Domain”
Single Area OSPF uses only one area, usually Area 0

## Slide 52: Link State
1 – Flooding of link-state information
The first thing that happens is that each node, router, on the network announces its own piece of link-state information to other all other routers on the network. This includes who their neighboring routers are and the cost of the link between them.
Example: “Hi, I’m RouterA, and I can reach RouterB via a T1 link and I can reach RouterC via an Ethernet link.”
Each router sends these announcements to all of the routers in the network.
1 – Flooding of link-state information

## Slide 53: Link State
2. Building a Topological Database
Each router collects all of this link-state information from other routers and puts it into a topological database.
3. Shortest-Path First (SPF), Dijkstra’s Algorithm
Using this information, the routers can recreate a topology graph of the network.
Believe it or not, this is actually a very simple algorithm and I highly suggest you look at it some time, or even better, take a class on algorithms. (Radia Perlman’s book, Interconnections, has a very nice example of how to build this graph – she is one of the contributors to the SPF and Spanning-Tree algorithms.)
1 – Flooding of link-state information
2 – Building a Topological Database
3 – SPF Algorithm

## Slide 54: Link State
4. Shortest Path First Tree
This algorithm creates an SPF tree, with the router making itself the root of the tree and the other routers and links to those routers, the various branches.
5. Routing Table
Using this information, the router creates a routing table.
1 – Flooding of link-state information
2 – Building a Topological Database
3 – SPF Algorithm
4 – SPF Tree
5 – Routing Table

## Slide 55: Link State Concepts
1 – Flooding of link-state information
2 – Building a Topological Database
3 – SPF Algorithm
4 – SPF Tree
5 – Routing Table
How does the SPF algorithm create an SPF Tree?
Let’s take a look!
This is extra Information.

## Slide 56: Extra: Simplified Link State Example
In order to keep it simple, we will take some liberties with the actual process and algorithm, but you will get the basic idea!
You are RouterA and you have exchanged “Hellos” with:
  RouterB on your network 11.0.0.0/8 with a cost of 15,
  RouterC on your network 12.0.0.0/8 with a cost of 2
  RouterD on your network 13.0.0.0/8 with a cost of 5
  Have a “leaf” network 10.0.0.0/8 with a cost of 2
This is your link-state information, which you will flood to all other routers.
All other routers will also flood their link state information. (OSPF: only within the area)
“Leaf” 10.0.0.0/8
11.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2

## Slide 57: Extra: Simplified Link State Example
RouterB:
Connected to RouterA on network 11.0.0.0/8, cost of 15
Connected to RouterE on network 15.0.0.0/8, cost of 2
Has a “leaf” network 14.0.0.0/8, cost of 15
RouterC:
Connected to RouterA on network 12.0.0.0/8, cost of 2
Connected to RouterD on network 16.0.0.0/8, cost of 2
Has a “leaf” network 17.0.0.0/8, cost of 2
RouterD:
Connected to RouterA on network 13.0.0.0/8, cost of 5
Connected to RouterC on network 16.0.0.0/8, cost of 2
Connected to RouterE on network 18.0.0.0/8, cost of 2
Has a “leaf” network 19.0.0.0/8, cost of 2
RouterE:
Connected to RouterB on network 15.0.0.0/8, cost of 2
Connected to RouterD on network 18.0.0.0/8, cost of 10
Has a “leaf” network 20.0.0.0/8, cost of 2
All other routers flood their own link state information to all other routers.
RouterA gets all of this information and stores it in its LSD (Link State Database).
Using the link state information from each router, RouterC runs Dijkstra algorithm to create a SPT. (next)
RouterA’s Topological Data Base (Link State Database)

## Slide 58: Link State information from RouterB
We now get the following link-state information from RouterB:
Connected to RouterA on network 11.0.0.0/8, cost of 15
Connected to RouterE on network 15.0.0.0/8, cost of 2
Have a “leaf” network 14.0.0.0/8, cost of 15
Now, RouterA attaches the two graphs…
+
=
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
11.0.0.0/8
12.0.0.0/8
13.0.0.0/8
14.0.0.0/8
15.0.0.0/8
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
2
2
2
Notes: A

## Slide 59: Link State information from RouterC
We now get the following link-state information from RouterC:
Connected to RouterA on network 12.0.0.0/8, cost of 2
Connected to RouterD on network 16.0.0.0/8, cost of 2
Have a “leaf” network 17.0.0.0/8, cost of 2
12.0.0.0/8
16.0.0.0/8
17.0.0.0/8
2
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
+
16.0.0.0/8
17.0.0.0/8
2
=
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
Now, RouterA attaches the two graphs…
Notes: A

## Slide 60: Link State information from RouterD
We now get the following link-state information from RouterD:
Connected to RouterA on network 13.0.0.0/8, cost of 5
Connected to RouterC on network 16.0.0.0/8, cost of 2
Connected to RouterE on network 18.0.0.0/8, cost of 2
Have a “leaf” network 19.0.0.0/8, cost of 2
13.0.0.0/8
16.0.0.0/8
18.0.0.0/8
19.0.0.0/8
18.0.0.0/8
19.0.0.0/8
2
2
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
+
=
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
18.0.0.0/8
19.0.0.0/8
2
Now, RouterA attaches the two graphs…
10.0.0.0/8
10.0.0.0/8
Notes: A

## Slide 61: Link State information from RouterE
We now get the following link-state information from RouterE:
Connected to RouterB on network 15.0.0.0/8, cost of 2
Connected to RouterD on network 18.0.0.0/8, cost of 10
Have a “leaf” network 20.0.0.0/8, cost of 2
15.0.0.0/8
18.0.0.0/8
2
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
18.0.0.0/8
19.0.0.0/8
2
10.0.0.0/8
+
20.0.0.0/8
2
20.0.0.0/8
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
19.0.0.0/8
2
10.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
2
Now, RouterA attaches the two graphs…
Notes: A

## Slide 62: Topology
Using the topological information we listed, RouterA has now built a complete topology of the network.
The next step is for the link-state algorithm to find the best path to each node and leaf network.
2
2
2
2
2
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
17.0.0.0/8
16.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
19.0.0.0/8
10.0.0.0/8
Notes: A

## Slide 63: Extra: Simplified Link State Example
RouterB:
Connected to RouterA on network 11.0.0.0/8, cost of 15
Connected to RouterE on network 15.0.0.0/8, cost of 2
Has a “leaf” network 14.0.0.0/8, cost of 15
RouterC:
Connected to RouterA on network 12.0.0.0/8, cost of 2
Connected to RouterD on network 16.0.0.0/8, cost of 2
Has a “leaf” network 17.0.0.0/8, cost of 2
RouterD:
Connected to RouterA on network 13.0.0.0/8, cost of 5
Connected to RouterC on network 16.0.0.0/8, cost of 2
Connected to RouterE on network 18.0.0.0/8, cost of 2
Has a “leaf” network 19.0.0.0/8, cost of 2
RouterE:
Connected to RouterB on network 15.0.0.0/8, cost of 2
Connected to RouterD on network 18.0.0.0/8, cost of 10
Has a “leaf” network 20.0.0.0/8, cost of 2
RouterA’s Topological Data Base (Link State Database)

## Slide 64: Choosing the Best Path
Using the link-state algorithm RouterA can now proceed to find the shortest path to each leaf network.
2
2
2
2
2
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
17.0.0.0/8
16.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
19.0.0.0/8
10.0.0.0/8
Notes: A

## Slide 65: Choosing the Best Path
Now RouterA knows the best path to each network, creating an SPT (Shortest Path Tree).
2
2
2
2
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
17.0.0.0/8
16.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
19.0.0.0/8
10.0.0.0/8
Notes: A

## Slide 66: SPT Results Get Put into the Routing Table
RouterA’s Routing Table
10.0.0.0/8 connected e0
11.0.0.0/8 connected s0
12.0.0.0/8 connected s1
13.0.0.0/8 connected s2
14.0.0.0/8 17 s0
15.0.0.0/8 17 s1
16.0.0.0/8 4 s1
17.0.0.0/8 4 s1
18.0.0.0/8 14 s1
19.0.0.0/8 6 s1
20.0.0.0/8 16 s1
2
2
2
2
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
17.0.0.0/8
16.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
19.0.0.0/8
10.0.0.0/8
s0
s1
s2
e0

## Slide 67: Introduction to OSPF Concepts
Introducing OSPF and Link State Concepts
Advantages of OSPF
Brief History
Terminology
Link State Concepts
Introducing the OSPF Routing Protocol
Metric based on Cost (Bandwidth)
Hello Protocol
Steps to OSPF Operation
DR/BDR
OSPF Network Types

## Slide 68: OSPF’s Metric is Cost (Bandwidth)
RFC 2328, OSPF version 2, J. Moy
“A cost is associated with the output side of each router interface. This cost is configurable by the system administrator. The lower the cost, the more likely the interface is to be used to forward data traffic.”
RFC 2328 does not specify any values for cost.
Bay and some other vendors use a default cost of 1 on all interfaces, essentially making the OSPF cost reflect hop counts.

## Slide 69: OSPF’s Metric is Cost (Bandwidth)
Cisco: Cost = Bandwidth
Cisco uses a default cost of 108/bandwidth
Default bandwidth of the interface (bandwidth command)
108 (100,000,000) as the reference bandwidth: This is used so that the faster links (higher bandwidth) have lower costs.
  Routing metrics, lower the cost the better the route.
  I.e. RIP: 3 hops is better than 10 hops
  Extra: The reference bandwidth can be modified to accommodate networks with links faster than 100,000,000 bps (100 Mbps). See ospf auto-cost reference-bandwidth command.
Cost of a route is the cumulative costs of the outgoing interfaces from this router to the network.

## Slide 70: OSPF’s Metric is Cost (Bandwidth)
Cisco default interface costs:
56-kbps serial link = 1785
64-kbps serial link = 1562 128-kbps serial link = 781
T1 (1.544-Mbps serial link) = 64
E1 (2.048-Mbps serial link) = 48
4-Mbps Token Ring = 25
Ethernet = 10
16-Mbps Token Ring = 6
Fast Ethernet = 1
Problem: Gigabit Ethernet and faster = 1
Notes:
Cisco routers default to T1 (1.544 Mbps) on all serial interfaces and require manual modification with the bandwidth command.
ospf auto-cost reference-bandwidth reference-bandwidth can be used to modify the reference-bandwidth for higher speed interfaces
Cost = 100,000,000/Bandwidth

## Slide 71: OSPF’s Metric is Cost (Bandwidth)
Few final notes
For serial links, if it is not a T1 line, use the bandwidth command to configure the interface to the right bandwidth
Both sides of the link should have the same bandwidth value
If you use the command ospf auto-cost reference-bandwidth reference-bandwidth, configure all of the routers to use the same value.

## Slide 72: OSPF Areas
Group of contiguous nodes/networks
Per area topology DB
  Invisible outside the area
  Reduces routing traffic
Backbone Area is contiguous
  All others areas must connect to the backbone
Virtual Links
Area 1
Area 4
Area 0
Backbone Area
Area 2
Area 3
Notes: 27
Router ID: A 32-bit number assigned to each router running the OSPF protocol. This number uniquely identifies the router within an Autonomous System. Router use this number to identify themselves when generating updates.
Neighboring routers: Two routers that have interfaces to a common network. On multi-access networks, neighbors are dynamically discovered by OSPFs Hello Protocol.
Adjacency: A relationship formed between selected neighboring routers for the purpose of exchanging routing information. Not every pair of neighboring routers become adjacent.
Link state advertisement: Describes the local state of the router or network. This includes the state of the router’s interfaces and adjacencies. Each link state advertisement is flooded throughout the routing domain. The collected link state advertisements of all routers and networks forms the protocol’s topological database.
Hello protocol: The part of the OSPF protocol used to establish and maintain neighboring relationships. On multi-access networks the Hello Protocol can also dynamically discover neighboring routers.
Designated router: Each multi-access network that has at least two attached routers has a Designated Router. The Designated Router generates a link state advertisement for the multi-access network and has other special responsibilities in the running of the protocol. The Designated Router is elected by the Hello Protocol.

## Slide 73: Router Classification
Internal Router (IR)
Area Border Router (ABR)
Backbone Router (BR)
Autonomous System Border Router (ASBR)
Area 1
IR/BR
Area 0
Area 2
Area 3
IR
ABR/BR
To another AS
ASBR
Notes: 32

## Slide 74: OSPF Route Types
Intra-Area Route
  All routes within an area
Inter-Area Route
  Routes announced from area to another by an ABR
External Route
  Routes imported into OSPF from another protocol or Static routes
Area 0
Area 2
Area 3
ABR
To Another AS
ASBR

## Slide 75: Topology/Links-State DB
A router has a separate DB for each area it belongs
All routers within an area have an identical DB
SPF calculation is done separately for each area
LSA flooding is limited to the particular area
Notes: 30

## Slide 76: OSPF Packet Types

## Slide 77: OSPF Packet Format
MAC Hdr
IP Hdr
OSPF Hdr
OSPF type-specific Data
MAC Header
  Src – MAC addr of sending interface
  Dst – 0100:5E00:0005 or 0100:5E00:0006
  Type – 0x0800
IP Header
  Src – IP addr of sending interface
  Dst – 224.0.0.5 or 224.0.0.6
  Protocol – 89
OSPF Header
  Version
  Type
  Router ID
  Area ID
Notes: 01:00:5E:00:00:00 - 01:00:5E:7F:FF:FF 0x0800 IPv4 Multicast (RFC 1112), insert the low 23 Bits of the multicast IPv4 Address into the Ethernet Address (RFC 7042 2.1.1.)
33:33:xx:xx:xx:xx 0x86DD IPv6 Multicast (RFC 2464), insert the low 32 Bits of the multicast IPv6 Address into the Ethernet Address (RFC 7042 2.3.1.)
224.0.0.5 The Open Shortest Path First (OSPF) All OSPF Routers address is used to send Hello packets to all OSPF routers on a network segment.
224.0.0.6 The OSPF All Designated Routers ""(DR)"" address is used to send OSPF routin`g information to designated routers on a network segment.

## Slide 78: OSPF Packet Format
2: current version is OSPF V2
Message types:
1: Hello (tests reachability)
2: Database description
3: Link Status request
4: Link state update
5: Link state acknowledgement
ID of the Area from which the packet originated
0: no authentication
1: Cleartext password
2: MD5 checksum
(added to end packet)
Authentication passwd = 1: 64 cleartext password
Authentication passwd = 2: 0x0000 (16 bits)
KeyID (8 bits)
Length of MD5 checksum (8 bits) Nondecreasing sequence number (32 bits)
Standard IP checksum taken over entire packet
Prevents replay attacks

## Slide 79: OSPF Hello Protocol
Hello subprotocol is intended to perform the following tasks within OSPF:
Dynamic neighbor discovery
Detect unreachable neighbors
Ensure two-way communications between neighbors
Ensure correctness of basic interface parameters between neighbors
Provide necessary information for the election of the Designated and Backup Designated routers on a LAN segment (coming)

## Slide 80: OSPF Hello Protocol
OSPF routers send Hellos on OSPF enabled interfaces:
  Default every 10 seconds on multi-access and point-to-point segments
  Default every 30 seconds on NBMA segments (Frame Relay, X.25, ATM)
  Most cases OSPF Hello packets are sent as multicast to ALLSPFRouters (224.0.0.5)
HelloInterval - Cisco default = 10 seconds or 30 seconds and can be changed with the command ip ospf hello-interval.
RouterDeadInterval - The period in seconds that the router will wait to hear a Hello from a neighbor before declaring the neighbor down.
  Cisco uses a default of four-times the HelloInterval (4 x 10 sec. = 40 seconds, 120 secconds for NBMA) and can be changed with the command ip ospf dead-interval.
Note: For routers to become adjacent, the Hello, DeadInterval and network types must be identical between routers or Hello packets get dropped!

## Slide 81: Network Types – more later
show ip ospf interface
Unless you are configuring an NBMA network like Frame Relay, this won’t be an issue.
Many administrators prefer to use point-to-point or point-to-multipoint for NMBA to avoid the DR/BDR and full-mesh issues.

## Slide 82: OSPF packet types
OSPF Type-2 (DBD)
OSPF Type-3 (LSR)
OSPF Type-4 (LSU)
OSPF Type-5 (LSAck)

## Slide 83: Steps to OSPF Operation

## Slide 84: Steps to OSPF Operation with States
1. Establishing router adjacencies (Routers are adjacent)
  Down State – No Hello received
  Init State – Hello received, but not with this router’s Router ID
    “Hi, my name is Carlos.” “Hi, my name is Maria.”
  Two-way State – Hello received, and with this router’s Router ID
    “Hi, Maria, my name is Carlos.” “Hi, Carlos, my name is Maria.”
2. Electing DR and BDR – Multi-access (broadcast) segments only
  ExStart State with DR and BDR
  Two-way State with all other routers
3. Discovering Routes
  ExStart State
  Exchange State
  Loading State
  Full State (Routers are “fully adjacent”)
4. Calculating the Routing Table
5. Maintaining the LSDB and Routing Table

## Slide 85: 1. Establishing Adjacencies
Initially, an OSPF router interface is in the down state.
An OSPF interface can transition back to this state if it has not received a Hello packet from a neighbor within the RouterDeadInterval time (40 seconds unless NBMA, 120 seconds).
In the down state, the OSPF process has not exchanged information with any neighbor.
OSPF is waiting to enter the init state.
An OSPF router tries to form an adjacency with at least one neighbor for each IP network it’s connected to.

## Slide 86: 1. Establishing Adjacencies
The process of establishing adjacencies is asymmetric, meaning the states between two adjacent routers may be different as they both transition to full state.
RTB perspective and assuming routers are configured correctly.
Trying to start a relationship and wanting to enter the init state or really the two-way-state
RTB begins multicasts OSPF Hello packets (224.0.0.5, AllSPFRouters), advertising its own Router ID.
  224.0.0.5: All OSPF routers should be able to transmit and listen to this address.

## Slide 87: 1. Establishing Adjacencies
Router ID = Highest loopback address else highest active IP address.
Loopback address has the advantage of never going down, thus diminishing the possibility of having to re-establish adjacencies. (more in a moment)
  Use private ip addresses for loopbacks, so you do not inadvertently advertise a route to a real network that does not exist on your router.
For routers to become adjacent, the Hello, DeadInterval and network types must be identical between routers or Hello packets get dropped!

## Slide 88: 1. Establishing Adjacencies
Hello 10.6.0.1
Hello 10.5.0.1
Hello 10.6.0.1 10.5.0.1
Hello 10.5.0.1 10.6.0.1
Down
Init
Down
Init
2-way
2-way
Down State - Init State – Two Way State
Down State - OSPF routers send Type 1 Hello packets at regular intervals (10 sec.) to establish neighbors.
When a router (sends or) receives its first Hello packet, it enters the init state, indicating that the Hello packet was received but did not contain the Router ID of the receiving router in the list of neighbors, so two-way communications is not yet ensured.
As soon as the router sends a Hello packet to the neighbor with its RouterID and the neighbor sends a Hello packet packet back with that Router ID, the router’s interface will transition to the two-way state.
Now, the router is ready to take the relationship to the next level.

## Slide 89: 1. Establishing Adjacencies
Hello 10.6.0.1
Hello 10.5.0.1
Hello 10.6.0.1 10.5.0.1
Hello 10.5.0.1 10.6.0.1
Down
Init
Down
Init
2-way
2-way
From Init state to the Two-way state
RTB receives Hello packets from RTA and RTC (its neighbors), and sees its own Router ID (10.6.0.1) in the Neighbor ID field.
RTB declares takes the relationship to a new level, and declares a two-way state between itself and RTA, and itself and RTC.
As soon as the router sends a Hello packet to the neighbor with its RouterID and the neighbor sends a Hello packet packet back with that Router ID, the router’s interface will transition to the two-way state.
Now, the router is ready to take the relationship to the next level.

## Slide 90: 1. Establishing Adjacencies
Two-way state
RTB now decides who to establish a “full adjacency” with depending upon the type of network that the particular interfaces resides on.
Note: The term adjacency is used to both describe routers reaching 2-way state and when they reach full-state. Not to go overboard on this, but technically OSPF routers are adjacent when the FSM reaches full-state and IS-IS is considered adjacent when the FSM reaches 2-way state.
Two-way state to ExStart state
If the interface is on a point-to-point link, the routers becomes adjacent with its sole link partner (aka “soul mates”), and take the relationship to the next level by entering the ExStart state. (coming soon)
Remaining in the two-way state
If the interface is on a multi-access link (Ethernet, Frame Relay, …) RTB must enter an election process to see who it will establish a full adjacency with, and remains in the two-way state. (Next!)

## Slide 91: Steps to OSPF Operation with States
1. Establishing router adjacencies (Routers are adjacent)
  Down State – No Hello received
  Init State – Hello received, but not with this router’s Router ID
    “Hi, my name is Carlos.” “Hi, my name is Maria.”
  Two-way State – Hello received, and with this router’s Router ID
    “Hi, Maria, my name is Carlos.” “Hi, Carlos, my name is Maria.”
2. Electing DR and BDR – Multi-access (broadcast) segments only
  ExStart State with DR and BDR
  Two-way State with all other routers
3. Discovering Routes
  ExStart State
  Exchange State
  Loading State
  Full State (Routers are “fully adjacent”)
4. Calculating the Routing Table
5. Maintaining the LSDB and Routing Table

## Slide 92: Electing the DR and BDR
Without a DR, the formation of an adjacency between every attached router would create many unnecessary LSA (Link State Advertisements), n(n-1)/2 adjacencies.
Flooding on the network itself would be chaotic.
DR - Designated Router
BDR – Backup Designated Router
DR’s serve as collection points for Link State Advertisements (LSAs) on multi-access networks
A BDR back ups the DR.
If the IP network is multi-access, the OSPF routers will elect one DR and one BDR
On multi-access, broadcast links (Ethernet), a DR and BDR (if there is more than one router) need to be elected.

## Slide 93: Electing the DR and BDR
Router with the highest Router ID is elected the DR, next is BDR.
But like other elections, this one can be rigged.
The router’s priority field can be set to either ensure that it becomes the DR or prevent it from being the DR.
Rtr(config-if)# ip ospf priority <0-255>
  Higher priority becomes DR/BDR
  Default = 1
  0 = Ineligible to become DR/BDR
The router can be assigned a priority between 0 and 255, with 0 preventing this router from becoming the DR (or BDR) and 255 ensuring at least a tie. (The highest Router ID would break the tie.)

## Slide 94: Electing the DR and BDR
All other routers, “DROther”, establish adjacencies with only the DR and BDR.
DRother routers multicast LSAs to only the DR and BDR
  (224.0.0.6 - all DR routers)
DR sends LSA to all adjacent neighbors (DROthers)
  (224.0.0.5 - all OSPF routers)
Backup Designated Router - BDR
Listens, but doesn’t act.
If LSA is sent, BDR sets a timer.
If timer expires before it sees the reply from the DR, it becomes the DR and takes over the update process.
The process for a new BDR begins.

## Slide 95: Electing the DR and BDR
A new router enters the network:
Once a DR is established, a new router that enters the network with a higher priority or Router ID it will NOT become the DR or BDR. (Bug in early IOS 12.0)
Regardless of the priority or Router ID, that router will become a DROther.
If DR fails, BDR takes over as DR and selection process for new BDR begins.

## Slide 96: Clarifications
Hello packets are still exchanged between all routers on a multi-access segment (DR, BDR, DROthers,….) to maintain neighbor adjacencies.
OSPF LSA packets (coming) are packets which are sent from the BDR/DROthers to the DR, and then from the DR to the BDR/DROthers. (The reason for a DR/BDR.)
Normal routing of IP packets still takes the lowest cost route, which might be between two DROthers.

## Slide 97: Steps to OSPF Operation with States - Extra
1. Establishing router adjacencies
  Down State – No Hello received
  Init State – Hello received, but not with this router’s Router ID
    “Hi, my name is Carlos.” “Hi, my name is Maria.”
  Two-way State – Hello received, and with this router’s Router ID
    “Hi, Maria, my name is Carlos.” “Hi, Carlos, my name is Maria.”
2. Electing DR and BDR – Multi-access (broadcast) segments only
  ExStart State with DR and BDR
  Two-way State with all other routers
3. Discovering Routes
  ExStart State
  Exchange State
  Loading State
  Full State
4. Calculating the Routing Table
5. Maintaining the LSDB and Routing Table

## Slide 98: Steps to OSPF Operation with States Discovering Routes and Reaching Full State

## Slide 99: ExStart State – the explanation
ExStart State
This state starts the LSDB (Link State Data Base) synchronization process.
This will prepare for initial database exchange.
Routers are now ready to exchange routing information.
  Between routers on a point-to-point network
  On a multi-access network between the DRothers and the DR and BDR.
Formally, routers in ExStart state are characterized as adjacent, but have not yet become “fully adjacent” as they have not exchanged data base information.
But who goes first in the exchange?
ExStart is established by exchanging OSPF Type-2 DBD (Database Description) packets
Purpose of ExStart is to establish a “master/slave relationship” between the two routers decided by the higher router id.
Once the roles are established they enter the Exchange state.

## Slide 100: OSPF Database Description Packet Format
Interface MTU
Options
00000I M MS
DD Sequence #
LSA Headers
I – Initial bit M – More bit MS – 1: master, 0: slave
Sequence #: Set by master in the 1st DD packet, and incremented in subsequent packets

## Slide 101: Exchange State – the explanation
Routers exchange one or more Type-2 DBDs (Database Description) packets, which is a summary of the link-state database
  send LSAcks to verify
Routers compare these DBDs with information in its own database.
When a DBD packet is received the router looks through the LSA (Link State Advertisement) headers and identifies LSAs that are not in the router’s LSDB or are a different version from its LSDB version (older or newer).
If the LSA is not in its LSDB or the LSA is a more recent version, the router adds an entry to its Link State Request list.
This process ends when both routers stop have sent and received acknowledgements for all their DBD packets – that is they have successfully sent all their DBD packets to each other.

## Slide 102: Exchange State – the explanation
Exchange State
If a router has entries in its Link State Request list, meaning that it needs additional information from the other router for routes that are not in its LSDB or has more recent versions, then it enters the loading state.
If there are no entries in its Link State Request list, than the router’s interface can transition directly to full state.
Complete routing information is exchanged in the loading state, discussed next.

## Slide 103: Loading State - the explanation
Loading State
If a router has entries in its Link State Request list, meaning that it needs additional information from the other router for routes that are not in its LSDB or has more recent versions, then it enters the loading state.
The router needing additional information sends LSR (Link State Request) packets using LSA information from its LSR list.

## Slide 104: Loading State - the explanation
Loading State
The other routers replies by sending the requested LSAs in the Link State Update (LSU) packet.
The receiving router sends LSAck to acknowledge receipt.
When all LSAs on the neighbors Link State Request list have been received, the “neighbor FSM” transitions this interface to Full state.

## Slide 105: Link State Requests (LSR)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Version # | 3 | Packet length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Router ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Area ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Checksum | AuType |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Authentication |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Authentication |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LS type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Link State ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Advertising Router |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ... |
(LSRs)
LSR

## Slide 106: Link State Advertisement (Update)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Version # | 4 | Packet length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Router ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Area ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Checksum | AuType |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Authentication |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Authentication |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| # LSAs |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+- +-+
| LSAs |
+- +-+
| ... |
LSAs
LSAs: Types 1, 2, 3, 4, or 5
# LSAs included in this msg

## Slide 107: OSPF Link State ACK Packet Format
LSA Headers

## Slide 108: OSPF Link State Advertisement Header Format
LS Age
Options
Type
Link State ID
Advertising Router
LS Sequence Number
LS Checksum
Length
LS Age -- #seconds elapsed since the LSA was created

## Slide 109: OSPF LS Types
Value | Link Type | Description
1 | Router –LSA | Link to a Router
2 | Network-LSA | Link to a network
3 | Summary –LSA | Summary information about a network
4 | ASBR Summary-LSA | Summary information about a link to an ASBR
5 | AS-Extenal LSA | External link outside the AS
6 | Multicast-OSPF-LSA | Deprecated
7 | Not-so-stubby area LSA | 
8 | External attribute LSA for BGP | 
9 | link-local "opaque" LSA | Carry application-specification info such as traffic engineering or MPLS throughput the OSPF domain
10 | area-local "opaque" LSA | 
11 | AS "opaque" LSA | 

## Slide 110: OSPF LS Types -- Continue
Value | LSA Type | Originated By | Advertised To
1 | Router LSA | Every Router | Within the area originated
2 | Network LSA | Designated Router | Within the area originated
3 | Network Summary LSA | ABR | Flooded into a singe area
4 | ASBR Summary LSA | ABR | Flooded into a single area
5 | AS External LSA | ASBR | All non-stub areas
7 | NSSA External LSA | ASBR | Within the NSSA originated

## Slide 111: OSPF Router LSA
LS Age
Options
Type
Link State ID
Advertising Router
LS Sequence Number
LS Checksum
Length
#Links
00000VEB
0x00
Link ID
Link Data
Metric
Link Type
#TOS
TOS Metric
TOS
0x00
…..
Link ID
Link Data
Originating router’s router ID
V: Virtual Link Endpoint
E: External, originating router is ASBR
B: Border, originating router is ABR
Cost of the ink

## Slide 112: Router LSA Link Types
Link Type | Connection | Link ID | Link Data
1 | Point-to-point | Neighboring Router’s Router ID | IP addr of the originating router’s intf to the network
2 | Connection to a transit network | IP addr of the DR’s intf | IP addr of the originating router’s intf to the network
3 | Connection to a stub network | IP network or subnet addr | Network’s IP addr or subnet mask
4 | Virtual Link | Neighboring Router’s Router ID | Ifindex value for the originating router’s intf

## Slide 113: OSPF Network LSA
LS Age
Options
Type
Link State ID
Advertising Router
LS Sequence Number
LS Checksum
Length
#Links
00000VEB
0x00
Network Mask
Attached Router
…..
Attached Router
IP addr of the DR’s intf to the network
Router IDs of all routers on the network
Advertise the multi-access network and al routers attached to the network

## Slide 114: OSPF Network and ASBR Summary LSA
LS Age
Options
Type
Link State ID
Advertising Router
LS Sequence Number
LS Checksum
Length
#Links
00000VEB
0x00
Network Mask
…..
TOS Metric
TOS
0x00
Metric
0x00
TOS Metric
TOS
0x00
Metric
0x00
IP addr of the network (Type 3)
Router ID of the ASBR (Type 4)
Network Summary LSA (Type 3) – Advertise networks external to an area
ASBR Summary LSA (Type 4) – Advertise ASBRs external to an area
Cost of the route to this destination

## Slide 115: OSPF AS External LSA
LS Age
Options
Type
Link State ID
Advertising Router
LS Sequence Number
LS Checksum
Length
#Links
00000VEB
0x00
Network Mask
…..
Metric
E0000000
IP addr of the destination
AS External LSA (Type 5) – Advertise destinations external to the Autonomous System
Cost of the route to this destination
Forwarding Address
External Route Tag

## Slide 116: OSPF NSSA External LSA (Type 7)
LS Age
Options
Type
Link State ID
Advertising Router
LS Sequence Number
LS Checksum
Length
#Links
00000VEB
0x00
Network Mask
…..
Metric
E0000000
IP addr of the destination
Flooded only within the NSSA in which it was originated
Forwarding Address –
  next hop address for internal route
  NSSA ASBR’s Router ID for non-internal route
Cost of the route to this destination
Forwarding Address
External Route Tag

## Slide 117: Full State - the explanation
Full State
Full state - after all LSRs have been updated.
At this point the routers should have identical LSDBs (link-state databases).
Flooding LSAs
Once this interface transitions to or from Full state the router originates a new version of a Router LSA (coming) and floods it to its neighbors, distributing the new topological information – out all OSPF enabled interfaces.
Broadcast networks:
  DR: If the LSA was received on this interface, send it out this interface so DROthers receive it (224.0.0.5 - all OSPF routers)
  BDR/DROther: If the LSA was received on this interface, do not send out this interface (received from DR).
Calculating Routing Table
The router still must calculate its routing table – Next!

## Slide 118: Couple of notes on link state flooding…
OSPF is a link state routing protocol and does not send periodic updates like RIP.
OSPF only floods link state state advertisements when there is a change in topology (this includes when a routers are first booted).
OSPF uses hop-by-hop flooding of LSAs; an LSA received on one interface are flooded out other OSPF enabled interfaces.
If a link state entry in the LSDB (Link State DataBase) reaches an age of 60 minutes (MaxAge) without being updated, it is removed and SPF is recalculated.
Every 30 minutes (LSRefreshTime), OSPF routers flood only their link states to all other routers (in the area).
  This is known as a “paranoid update”
  These do not trigger SPF recalculations.
Special note: When a link goes down and a router wants to send a LSA to tell other routers to remove this link state, it sends this link state with a value of 60 minutes (MAXAGE).

## Slide 119
Backbone
Area #0
External Links
1.A
1.C
1.B
1.D
3.D
3.A
3.C
3.B
1.A
1.B
1.C
1.D
3.A
3.B
3.C
3.D
2.A
2.B
2.C
2.A
2.C
2.B
ASBR
Notes: 54