## Slide 1: CS 540 Computer Networks II
Sandy Wang
chwang_98@yahoo.com
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2
6. Routing Protocols – BGP
Notes: In this chapter, we look at the underlying technology and protocol architecture
of LANs. Chapters 12 and 13 are devoted to a discussion of specific
LAN systems.

## Slide 3: Topics
  Overview
  LAN Switching
  IPv4
  IPv6
  Tunnels
  Routing Protocols -- RIP, RIPng
  Routing Protocols -- OSPF
  IS-IS
  Midterm Exam
  BGP
  MPLS
  Transport Layer -- TCP/UDP
  Congestion Control & Quality of Service (QoS)
  Access Control List (ACL)
  Final Exam

## Slide 4: Reference Books
Cisco CCNA Routing and Switching ICND2 200-101 Official Cert Guide, Academic Edition by Wendel Odom -- July 10, 2013. ISBN-13: 978-1587144882
The TCP/IP Guide: A Comprehensive, Illustrated Internet Protocols Reference by Charles M. Kozierok – October 1, 2005. ISBN-13: 978-1593270476
Data and Computer Communications (10th Edition) (William Stallings Books on Computer and Data Communications) by Williams Stallings – September 23, 2013. ISBN-13: 978-0133506488
http://class.svuca.edu/~sandy/class/CS540/

## Slide 5: Interior and Exterior Gateway Protocols
Note: IGRP and EIGRP are Cisco proprietary protocols. They are meant as an alternative between the limited RIP routing protocol and the more complicated and resource intensive OSPF and IS-IS routing protocols. IGRP was discontinued with IOS 12.2 in 2005.
The dates shown are when the RFC or other document was finalized. The protocol may have been implemented earlier than this date.
 | Interior Gateway Protocols |  |  |  | Exterior Gateway Protocols
 | Distance Vector Routing Protocols |  | Link State Routing Protocols |  | Path Vector
Classful | RIPv1 (1982/1988) | IGRP (1985) |  |  | EGP (1982)
Classless | RIPv2 (1994) | EIGRP (1992) | OSPFv2 (1991) | IS-IS (1990) | BGPv4 (1995)
IPv6 | RIPng (1997) | EIGRP for IPv6 (not yet released) | OSPFv3 (1999) | IS-IS for IPv6 (2000) | BGPv4 for IPv6 (1999)

## Slide 6: BGP -- Border Gateway Protocol
An inter-Autonomous Routing Protocol
RFC 1105, 1989 -- A Border Gateway Protocol (BGP)
RFC 1163, 1990 -- A Border Gateway Protocol (BGP)
RFC 1267, 1991 -- A Border Gateway Protocol 3 (BGP-3)
RFC 1771, 1995 – A Border Gateway Protocol 4 (BGP-4)
Latest RFC 4271 -- A Border Gateway Protocol 4 (BGP-4)
Use TCP as the transport protocol (Use port 179)
  Eliminates the need to implement explicit update fragmentation, retransmission, acknowledgement, and sequencing.

## Slide 7: BGP Basics
BGP is a path vector routing protocol.
BGP is a distance vector routing protocol, in that it relies on downstream neighbors to pass along routes from their routing table.
BGP uses a list of AS numbers through which a packet must pass to reach a destination.

## Slide 8: Overview of autonomous systems
An AS is a group of routers that share similar routing policies and operate within a single administrative domain.
An AS can be a collection of routers running a single IGP, or it can be a collection of routers running different protocols all belonging to one organization.
In either case, the outside world views the entire Autonomous System as a single entity.

## Slide 9: Autonomous System Number
A unique ASN is allocated to each AS for use in BGP routing. AS numbers are important because the ASN uniquely identifies each network on the Internet.
Internet Assigned Numbers Authority (IANA)
IANA allocates AS numbers to Regional Internet Registries (RIRs). Each AS has an identifying number that is assigned by an Internet registry or a service provider.
This number is between 1 and 65,535.
AS numbers within the range of 64,512 through 65,535 are reserved for private use.
Because of the finite number of available AS numbers, an organization must present justification of its need before it will be assigned an AS number.
Extend to 32-bit in RFC 6793 -- BGP Support for Four-Octet Autonomous System (AS) Number Space

## Slide 10: Overview of autonomous systems
Today, the Internet Assigned Numbers Authority (IANA) is enforcing a policy whereby organizations that connect to a single provider and share the provider's routing policies use an AS number from the private pool, 64,512 to 65,535.

## Slide 11: Single-homed autonomous systems
If an AS has only one exit point to outside networks, it is considered a single-homed system.
Single-homed autonomous systems are often referred to as stub networks or stubs.
Stubs can rely on a default route to handle all traffic destined for non-local networks.
BGP is not normally needed in this situation.
Static Route

## Slide 12: Multihomed nontransit autonomous systems
Multihomed nontransit autonomous systems do not really need to run BGP4 with their providers.
It is usually recommended and often required by ISPs.
As it will be seen later in this module, BGP4 offers numerous advantages, including increased control of route propagation and filtering.
Or same ISP

## Slide 13: Multihomed nontransit autonomous systems
Incoming route advertisements influence your outgoing traffic, and outgoing advertisements influence your incoming traffic.
If the provider advertises routes into your AS via BGP, your internal routers have more accurate information about external destinations.
  BGP also provides tools for setting routing policies for external destinations.
If your internal routes are advertised to the provider via BGP, you have influence over which routes are advertised at which exit point.
  BGP also provides tools for your influencing (to some degree) the choices the provider makes when sending traffic into your AS.

## Slide 14: Multi-homed Transit Autonomous Systems
When BGP is running inside an AS, it is referred to as Internal BGP (IBGP).
When BGP runs between autonomous systems, it is called External BGP (EBGP).
If the role of a BGP router is to route IBGP traffic, it is called a transit router.
Routers that sit on the boundary of an AS and that use EBGP to exchange information with the ISP are called border or edge routers.
Edge Router

## Slide 15: IBGP vs EBGP
When BGP is running inside an AS, it is referred to as Internal BGP (IBGP).
  If a BGP router’s role is to route IBGP traffic, it is called a transit router.
When BGP runs between autonomous systems, it is called External BGP (EBGP).
  Routers that sit on the boundary of an AS and use EBGP to exchange information with the ISP are called border routers.
EBGP
IBGP
…

## Slide 16
Routers A and B are running EBGP (BGP), and Routers B and C are running IBGP.
Note that the EBGP (BGP) peers are directly connected and that the IBGP peers are not. (They can be.)
As long as there is an IGP running that allows the two neighbors to reach one another, IBGP peers do not have to be directly connected.

## Slide 17
All BGP speakers within an AS must establish a peer relationship with each other, that is, the BGP speakers within an AS must be fully meshed logically. (later)
BGP4 provides two techniques that alleviate the requirement for a logical full mesh: confederations and route reflectors. (later)
AS 200 is a transit AS for AS 100 and AS 300---that is, AS 200 is used to transfer packets between AS 100 and AS 300.

## Slide 18: EBGP vs IBGP
EBGP peers must be directly connected, but there are certain exceptions to this requirement.
In contrast, IBGP peers merely require TCP/IP connectivity within the same AS.
  As long as RTY can communicate with RTW using TCP, both routers can establish an IBGP session.
  If needed, an IGP such as OSPF can provide IBGP peers with routes to each other.

## Slide 19: EBGP
EBGP neighbors must be directly connected in order to establish an EBGP session.
However, EBGP multihop is a Cisco IOS option allows RTW and RTU to be logically connected in an EBGP session, despite the fact that RTV does not support BGP.
The EBGP multihop option is configured on each peer with the following command:
Router(config-router)#neighbor IP-address ebgp-multihop [hops]
EBGP Multihop
EBGP Multihop
I do not speak BGP. But RTW and RTU can use EBGP multihop to speak BGP.

## Slide 20: EBGP
EBGP Multihop
EBGP Multihop

## Slide 21: BGP Packet Format
MAC Hdr
IP Hdr
Data
TCP Port 179
TCP Hdr
BGP Hdr
Notes: 01:00:5E:00:00:00 - 01:00:5E:7F:FF:FF 0x0800 IPv4 Multicast (RFC 1112), insert the low 23 Bits of the multicast IPv4 Address into the Ethernet Address (RFC 7042 2.1.1.)
33:33:xx:xx:xx:xx 0x86DD IPv6 Multicast (RFC 2464), insert the low 32 Bits of the multicast IPv6 Address into the Ethernet Address (RFC 7042 2.3.1.)
224.0.0.5 The Open Shortest Path First (OSPF) All OSPF Routers address is used to send Hello packets to all OSPF routers on a network segment.
224.0.0.6 The OSPF All Designated Routers ""(DR)"" address is used to send OSPF routin`g information to designated routers on a network segment.

## Slide 22: BGP Message Types
Before establishing a BGP peer connection the two neighbors must perform the standard TCP three-way handshake and open a TCP connection to port 179.
After the TCP session is established, BGP peers exchanges several messages to open and confirm connection parameters and to send BGP routing information.
All BGP messages are unicast to the one neighbor over the TCP connection.
There are four BGP message types:
  Type 1: OPEN
  Type 2: KEEPALIVE
  Type 3: UPDATE
  Type 4: NOTIFICATION

## Slide 23: BGP messages
BGP header format
  Marker: 16-octet that is used to detect loss of synchronization and to authenticate messages when authentication is supported.
  Length: indicates the total length of the message in octets, including the BGP header.
  Type: indicates the type of the message.
Marker
Length
Type
0
16
24
31
Notes: An Interesting Idea is behind the use of the Marker field in the BGP messages header. Since BGP uses TCP to provide reliable transport for routing information, so technically BGP is an Application. When TCP deliver data to the application layer it does not know what is the format of data it is carrying in its payload (text, Image, …etc) TCP only identifies data by connection (IP Address + Port Number) for TCP data is a stream of bytes with no boundaries between them, its up to the application to distinguish between different data formats.
So to mark the beginning of each message BGP uses the Marker field, a 16 bytes long field that contains a value both side agree to use to identify the beginning of a message. A value of all ones is used in the initial message and sometime its value is also used to carry authentication data, although the BGP message contains a length field a miscount of bytes might occur which could cause a synchronization error so the marker field is also used so both sender and receiver can remain synchronized.
Upon identifying the beginning of the BGP message the Type field is used to identify the Type of the message (OPEN, UPDATE, NOTIFICATION, and KEEPALIVE).

## Slide 24: OPEN message
Marker
Length
Type=OPEN
Version
My autonomous system
Hold time
BGP identifier
Optional parameter length
Optional parameters
0
8
16
24
31
Version: the protocol version number of the message.
My autonomous system: The AS number of the sending router.
Hold time: the number of seconds between the transmission of successive KEEPALIVE messages.
BPG identifier: the sending BGP router.
Optional parameter: a list of optional parameters, encoded in TLV structure.

## Slide 25: KEEPALIVE message
If the hold time is zero, then KEEPALIVE messages will not be sent.
Marker
Length
Type=KEEPALIVE
0
8
16
24
31

## Slide 26: Type 2: BGP Keepalive Message
This message type is sent periodically between peers to maintain connections and verify paths held by the router sending the keepalive.
If a router accepts the parameters specified in its neighbor’s Open message, it responds with a Keepalive.
Subsequent Keepalives are sent every 60 seconds by Cisco default or equal to one-third the agreed-upon hold time (180 seconds).
If the periodic timer is set to a value of zero (0), no keepalives are sent.

## Slide 27: NOTIFICATION message
Error code: the type of error condition.
Error subcode: specific information about the nature of the error.
Data: the reason for the notification.
Marker
Length
Type=NOTIFICATION
Error code
Data
Error subcode
0
8
16
24
31

## Slide 28: BGP Notification Message Error Code
Type Code | Name | Sub-Code and Description
1 | Message Header Error | 1: Connection not synchronized 2: Bad message length 3: Bad message type
2 | Open Message Error | 1: Unsupported Version number 2: Bad peer AS 3: Bad BGP Identifier 4: Unsupported optional parameter 5: Authentication failure 6: Unacceptable hold time
3 | Update Message Error | 1: Malformed attribute list 2: Unrecognized well-known attribute 3: Mission well-known attribute 4: Attribute flags error 5: Attribute length error 6: Invalid ORIGIN attribute 7: AS Routing loop 8: Invalid NEXT_HOP attribute 9: Optional attribute error 10: Invalid network field 11: Malformed AS_PATH
4 | Hold Time Expired | 
5 | Finite State Machine Error | 
6 | Cease | 

## Slide 29: UPDATE message
Unfeasible routes length: the total length of the withdrawn routes field in octets.
Withdrawn routes: a list of IP address prefixes for the routes that need to be withdrawn from BGP routing tables.
Total path attribute length: the total length of the Path Attributes field in octets.
Path attributes: a variable length sequence of path attributes.
NLRI: a list of IP prefixes.
Unfeasible routes length (2 octets)
Withdrawn routes (variable)
Total path attribute length (2 octets)
Path attributes (variable)
Network layer reachability information (variable)
Length (1 octet)
Prefix (variable)
Length (1 octet)
Prefix (variable)
……
Attribute type
Attribute length
Attribute value
Attribute type
Attribute length
Attribute value
……
BGP header
Length (1 octet)
Prefix (variable)
Length (1 octet)
Prefix (variable)
……

## Slide 30: Type 3: BGP Update Message
Network-Layer Reachability Information (NLRI)
This is one or more (Length, Prefix) tuples that advertise IP address prefixes and their lengths.
192.168.160.0/19
  Prefix = 192.168.160.0
  Prefix Length = 19
Path Attributes
This is described later, providing the information that allows BGP to choose a shortest path, detect routing loops, and determine routing policy.
Withdrawn Routes
These are (Length, Prefix) tuples describing destination that have become unreachable and are being withdrawn from service.

## Slide 31: BGP Attribute Categories
Well-Known Mandatory : Must be recognized and included in all BGP Update messages
Well-Known Discretionary: Must be recognized but may or may not be included in a specific Update message
Optional Transitive: Not required to be supported. Accept the attribute and pass on to peers
Optional Non-transitive: Not required to be supported. Quietly ignore and not advertise to other peers.

## Slide 32: Update message (cont.)
Attribute flag (1 octet):
  O bit: attribute is optional (O=1), or required (O=0).
  T bit: an optional attribute is transitive (T=1), or non-transitive (T=1). Set to 1 for Well-known attributes
  P bit: the information in the optional transitive attribute is partial (P=1), or complete (P=0). Set to 0 for well-known attributes and for optional non-transitive attributes
  E bit: the attribute length is two octets (E=1), or one octet (E=0).
Attribute type
Attribute length
Attribute value
O
T
P
E
0
Attribute type code

## Slide 33: BGP Attributes
Type Code | Name | Value Code | Description | 
1 | Origin | 0 | IGP | Well-Known Mandatory
 |  | 1 | EGP | 
 |  | 2 | Incomplete | 
2 | AS_PATH | 1 | AS_SET | Well-Known Mandatory
 |  | 2 | AS_SEQUENCE | 
 |  | 3 | AS_CONFED_SET | 
 |  | 4 | AS_CONFED_SEQUENCE | 
3 | NEXT_HOP | 0 | Next-Hop IP Address | Well-Known Mandatory
4 | MULTI_EXIT_DISC | 0 | 4-octet MET | Optional Non-transitive
5 | LOCAL_PREF | 0 | 4-octet LOCAL_PREF | Well-Known Discretionary
6 | ATOMIC_AGGREGATE | 0 | None | Well-Known Discretionary
7 | AGGREGATOR | 0 | AS Number and IP Address of aggregator | Well-Known Discretionary
8 | COMMUNITY | 0 | 4-octet community identifier | Optional Transitive
9 | ORIGINATOR_ID | 0 | 4-octet router ID of originator | Optional Non-transitive
10 | CLUSTER_LIST | 0 | Variable-length list of cluster IDs | Optional Non-transitive

## Slide 34: Update message (cont.)
Attribute type code:
  ORIGIN (type code 1): defines the origin of the NLRI.
  AS_PATH (type code 2): lists the sequence of Ass that the route have traversed to reach the destination.
  NEXT_HOP (type code 3): defines the IP address of the border router that should be used as the next hop to the destination listed in the NLRI.
  MULTI_NEXT_DISC (type code 4): discriminates among multiple entry/exit points to a neighboring AS and gives a hint to the neighboring AS about the preferred path.
  LOCAL_PREF( type code 5): informs other BGP routers within the same AS of its degree of preference for an advertised route.
  ATOMIC_AGGREGATE (type code 6): informs other BGP routers that it selected a less specific route without selecting a more specific one that is included in it.
  AGGREGATOR (type code 7): specifies the last AS number that formed the aggregate route followed by the IP address of the BGP router that formed the aggregate route.

## Slide 35: The ORIGIN Attribute
IGP – The router was learned from a protocol internal to the originating AS.
EGP – The route was learned from the Exterior Gateway Protocol
Incomplete – The router was learned by some other means. Routes learns through redistribution has the incomplete origin attribute, because there is no way to determine the original source of the route.

## Slide 36: The AS-Path Attribute
Sequence of ASs a route has traversed – Prepended only when the route is advertised between EBGP peers
Loop detection
Apply policy
AS 100
AS 300
AS 200
AS 500
AS 400
170.10.0.0/16
180.10.0.0/16
150.10.0.0/16
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200
150.10.0.0/16 300 400
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200

## Slide 37: The AS-Path Attribute
AS 100
AS 300
AS 200
AS 500
AS 400
180.10.0.0/16
180.10.0.0/16 100
180.10.0.0/16 200 100
180.10.0.0/16 300 200 100
180.10.0.0/16 100
180.10.0.0/16 400 100
180.10.0.0/16 100 100 100
180.10.0.0/16 400 100 100 100

## Slide 38: The Next Hop Attribute
150.10.0.0/16 150.10.1.1
160.10.0.0/16 150.10.1.1
150.10.1.2
150.10.1.1
160.10.0.0/16
150.10.0.0/16
AS 100
AS 300
AS 200
A
B
20

## Slide 39: Next Hop (continued)
Advertising to different AS – the NEXT_HOP is the IP address of the advertising router’s interface
Advertising to the same AS and the route is in the same AS – NEXT_HOP is the IP address of the originating router
Advertising to the same AS and the route is in a different AS – NEXT_HOP is the IP address of the external peer from which the route was learned

## Slide 40: The Next Hop Attribute
172.16.83.1
172.16.83.2
172.16.5.0/24
AS 200
A
B
20
C
172.16.101.1
172.16.101.2
iBGP
172.16.5.0/24
NEXT_HOP = 172.16.83.2

## Slide 41: The Next Hop Attribute
172.16.83.1
172.16.83.2
AS 200
A
B
20
C
172.16.101.1
172.16.101.2
iBGP
207.135.64.0/19
NEXT_HOP = 192.168.5.1
AS 300
D
192.168.5.1
207.135.64.0/19
NEXT_HOP = 192.168.5.1
eBGP

## Slide 42: The Local Preference Attribute
AS 400
AS 200
160.10.0.0/16
AS 100
AS 300
160.10.0.0/16 500
> 160.10.0.0/16 800
500
800
E
B
C
A
D

## Slide 43: The Local Preference Attribute
Local to an AS – non-transitive
  Only between iBGP peers
  Local preference set to 100 when heard from neighbouring AS
Used to influence BGP path selection
  Determines best path for outbound traffic
Path with highest local preference wins

## Slide 44: The Multi-Exit Discriminator (MED) Attribute
AS 201
AS 200
192.68.1.0/24
C
A
B
192.68.1.0/24 1000
192.68.1.0/24 2000
D
eBGP
iBGP
192.68.1.0/24 0

## Slide 45: The Multi-Exit Discriminator Attribute
Inter-AS Metric: Optional non-transitive
  Carried in eBGP updates to inform another AS of the preferred ingress point
  Lowest MED value is preferred
Used only to influence traffic between two directly connected AS
  Not passed beyond the receiving AS
  Metric reset to 0 on announcement to next AS
Comparable if paths are from same AS

## Slide 46: The ATOMIC_AGGREGATE and AGGREGATOR Attributes
The ATOMIC_AGGREGATE is a well-know discretionary attribute. Used to alert downstream routers that a loss of path information has occurred.
Receiving router must attach the ATOMIC_AGGREGATE attribute
The AGGREGATOR attribute is optional transitive. Provide information about where the aggregation was performed by including the AS number and the Router ID that originated the aggregate route.

## Slide 47: Route Aggregation
AS 3113
206.25.128.0/19
AS 237
206.25.160.0/19
AS 225
206.25.192.0/19
AS 810
206.25.224.0/19
206.25.128.0/17
(3113)
206.25.224.0/19
(810)
206.25.192.0/19
(237,225)
206.25.160.0/19
(237)
206.25.192.0/19
(225)
128 10000000
192 11000000
160 10100000
224 11100000
206.25.192.0/19
(3113,237,225)
206.25.160.0/19
(3113,237)
206.25.224.0/19
(3113,810)

## Slide 48: ATOMIC_AGGREGATE and AGGREGATOR
AS 3113
206.25.128.0/19
AS 237
206.25.160.0/19
AS 225
206.25.192.0/19
AS 810
206.25.224.0/19
206.25.128.0/17
(3113)
ATOMIC_AGGREGATE
AGGREGATOR = 3113, 206.25.254.252
206.25.224.0/19
(810)
206.25.192.0/19
(237,225)
206.25.160.0/19
(237)
206.25.192.0/19
(225)
RID= 206.25.254.252
128 10000000
192 11000000
160 10100000
224 11100000

## Slide 49: AS_SET and AS_SEQUENCE
AS_SEQUENCE: Ordered list of AS numbers
AS_SET: Unordered list of the AS numbers
  When a BGP router aggregates routes learned from other AS, it can include all those AS numbers in the AS_PATH as an AS_SET

## Slide 50: Inter-AS Routing Loops
AS 3113
206.25.128.0/19
AS 6571
AS 810
206.25.224.0/19
206.25.128.0/17
(3113)
206.25.224.0/19
(810)
206.25.192.0/19
(237,225)
206.25.160.0/19
(237)
192 11000000
160 10100000
224 11100000
206.25.128.0/17
(6571,3113)
206.25.225.0/24 e3
206.25.128.0/17 e2
e1
e2
e3
1
2
3
206.25.225.1
206.25.192.0/19 e1
206.25.160.0/17 e1
206.25.224.0/19 e2
e1
e2
e3
e1
e2
206.25.128.0/17 e1

## Slide 51: AS_SET and AS_SEQUENCE
AS 3113
206.25.128.0/19
AS 237
206.25.160.0/19
AS 225
206.25.192.0/19
AS 810
206.25.224.0/19
206.25.128.0/17
AS_SEQUENCE = (3113)
AS_SET = (237,810,225)
206.25.224.0/19
(810)
206.25.192.0/19
(237,225)
206.25.160.0/19
(237)
206.25.192.0/19
(225)
192 11000000
160 10100000
224 11100000

## Slide 52: The COMMUNITY Attribute
Optional transitive attribute to simplify policy enforcement
Originally Cisco-specific. Standardized in RFC 1997.
Identify a destination as a member of a community
Represented as two 16bit integers AA:NN (AA is the AS Number)
Well-known Communities:
  INTERNET : no value. Can be advertised freely
  NO_EXPORT (0xFFFFFF01) : cannot be advertised outside the confederation
  NO_ADVERTISE (0xFFFFFF02) : cannot be advertised at all
  LOCAL_AS (0xFFFFFF03) : Cannot be advertised to EBGP peers

## Slide 53: Community
160.10.0.0/16 300:1
AS 200
160.10.0.0/16 300:1
170.10.0.0/16 300:1
170.10.0.0/16 300:1
AS 400
D
C
E
B
170.10.0.0/16
AS 100
A
160.10.0.0/16
ISP 1
200.10.0.0/16 300:9
X
ISP 2
200.10.0.0/16
AS 300

## Slide 54: The ORIGINATOR_ID and CLUSTER_LIST Attributes
Optional non-transitive attributes used by route reflectors to prevent routing loops
ORIGINATOR_ID: Router ID of the originator of the route in the local AS
CLUSTER_LIST: A sequence of route reflector cluster IDs through which the route has traversed.

## Slide 55: BGP Routing
BGP is so flexible because it is a fairly simple protocol.
Routes are exchanged between BGP peers via UPDATE messages.
BGP routers receive the UPDATE messages, run some policies or filters over the updates, and then pass on the routes to other BGP peers.

## Slide 56: BGP Route Selection Algorithm
Summary of the BGP Path Selection Process
BGP selects only one path as the best path.
When the path is selected, BGP puts the selected path in its routing table and propagates the path to its neighbors.
BGP uses the following criteria, in the order presented, to select a path for a destination:
If the path specifies a next hop that is inaccessible, drop the update
2. Prefer the path with the largest weight.
3. If the weights are the same, prefer the path with the largest local preference.
4. If the local preferences are the same, prefer the path that was originated by BGP running on this router.
5. If no route was originated, prefer the route that has the shortest AS_path.
6. If all paths have the same AS_path length, prefer the path with the lowest origin type (where IGP is lower than EGP, and EGP is lower than Incomplete).
7. If the origin codes are the same, prefer the path with the lowest MED attribute.
8. If the paths have the same MED, prefer the external path over the internal path.
9. If the paths are still the same, prefer the path through the closest IGP neighbor.
10. Prefer the path with the lowest IP address, as specified by the BGP router ID.

## Slide 57: Internal vs. External BGP
R3
R4
R1
R2
E-BGP
BGP can be used by R3 and R4 to learn routes
How do R1 and R2 learn routes?
AS1
AS2

## Slide 58: Internal BGP (I-BGP)
Same messages as E-BGP
Different rules about re-advertising prefixes:
  Prefix learned from E-BGP can be advertised to I-BGP neighbor and vice-versa, but
  Prefix learned from one I-BGP neighbor cannot be advertised to another I-BGP neighbor
  Reason: no AS PATH within the same AS and thus danger of looping.

## Slide 59: Internal BGP (I-BGP)
R3
R4
R1
R2
E-BGP
I-BGP
R3 can tell R1 and R2 prefixes from R4
R3 can tell R4 prefixes from R1 and R2
R3 cannot tell R2 prefixes from R1
R2 can only find these prefixes through a direct connection to R1
Result: I-BGP routers must be fully connected (via TCP)!
  contrast with E-BGP sessions that map to physical links
AS1
AS2

## Slide 60: Reasons For Fully Meshed iBGP
To prevent BGP routing loops within an AS
To ensure that all routers along the path of a BGP route know how to forward packets to the destination

## Slide 61: Route Flap Dampening
Route flap
  Going up and down of path or change in attribute
    BGP WITHDRAW followed by UPDATE = 1 flap
    eBGP neighbour going down/up is NOT a flap
  Ripples through the entire Internet
  Wastes CPU
Route Dampening is to To limit the propagation of flapping routes. Advertise stable routes only
Described in RFC2439

## Slide 62: Route Dampening
Route Dampening Parameters:
  History state: After a single route flap, the route is assigned a penalty, and the dampening state of the route is set to History. Each time the route flaps, the penalty increases.
  Suppress limit: If the penalty exceeds the suppress limit, the route is Dampened. When the route is in Damp state, the router is not considered for best path selection and is not advertised to BGP peers.
  Half life: The penalty of a route is decreased based on the half-life period. The default half-life period is 15 minutes. The penalty on the route is reduced every 5 seconds.
  Reuse limit: When the penalty falls below the reuse limit, the route is unsuppressed. When the penalty falls below half of reuse limit, the history of the route is cleared.
  Maximum suppress limit: It is the maximum amount of time a route can be suppressed for.
  Cisco Default: Penalty = 1000 per flap. Suppress limit = 2000, half-life period = 15 minutes, reuse-limit = 750 and maximum suppress-limit = 60 minutes.

## Slide 63: Operation
Add penalty (1000) for each flap
  Change in attribute gets penalty of 500
Exponentially decay penalty
  half life determines decay rate
Penalty above suppress-limit
  do not advertise route to BGP peers
Penalty decayed below reuse-limit
  re-advertise route to BGP peers
  penalty reset to zero when it is half of reuse-limit

## Slide 64: Operation
Reuse limit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
0
1000
2000
3000
4000
Time
Penalty
Suppress limit
Network
Announced
Network
Re-announced
Network
Not Announced

## Slide 65: Route Reflector
All iBGP peers must be fully meshed which requires n(n-1)/2 iBGP connections in the AS.
A router is configured as a route reflector (RR)
Other iBGP routers (clients) peer with the RR only
Rules to Advertise
  Routes learned from a non-client iBGP peer – Advertise to clients only
  Routes learned from a client – Advertise to all non-clients and clients, except the originating client
  Routes learned from an eBGP peer – Advertise to all clients and non-clients

## Slide 66: Router Reflector
AS 9184
Router Reflector Cluster
Router Reflector
Client
Client
Client
Client
Client

## Slide 67: Router Reflection Cluster Peering Relationships
AS 9184
Router Reflector Cluster
Router Reflector
Non-Client
Client
Client
EBGP
Client
AS 2153
AS 829
EBGP
iBGP
iBGP
iBGP
iBGP

## Slide 68: Route Reflector
AS 100
A
B
C
Clients
Reflectors
Reflector receives path from clients and non-clients
Selects best path
If best path is from client, reflect to other clients and non-clients
If best path is from non-client, reflect to clients only
If a route is received from an EBGP peer, reflect to all clients and non-clients
Described in RFC2796

## Slide 69: Route Reflectors: Loop Avoidance
Originator_ID attribute
  Carries the RID of the originator of the route in the local AS (created by the RR)
    An RR does not advertise a route back to the originator
    If the originator receives an update with its own RID, the update is ignored
Cluster_list attribute
  The local cluster-id is added when the update is sent by the RR
  Cluster-id is router-id (address of loopback)
    When an RR receives an update, it checks the CLUSTER_LIST. Ignores the update if it sees its own cluster ID in the list

## Slide 70: Confederations
Member Autonomous Systems: An AS subdivided into a group of sub-autonomous systems. Usually use AS number in the reserved range 64512 to 65535.
iBGP to peers in the same member AS and eBGP to peers in other member AS
Confederation ID: the AS number of the entire confederation which is represented to peers outside of the confederation as the AS number of the entire confederation.
AS_CONFED_SEQUENCE: ordered list of AS numbers within the confederation
AS_CONFED_SET: Unordered list of AS numbers within the confederation
When update sent to a peer external to the confederation, the AS_CONFED_SEQUENCE and AS_CONFED_SET is stripped, and the confederation ID is prepended. External peers see the confederation as a single AS.
Choosing a route: EBGP external to the confederation > EBGP to member AS > IBGP

## Slide 71: Confederation
AS 1836
AS 65510
AS 65520
AS 65530
AS 9184
eBGP
eBGP
eBGP
iBGP
iBGP
iBGP
iBGP
iBGP
Confederation ID

## Slide 72: Inter-AS Routing Loops
AS 3113
206.25.128.0/19
AS 6571
AS 810
206.25.224.0/19
206.25.224.0/19 0
206.25.192.0/19 0
206.25.160.0/19 0
e1
e2
e3
206.25.225.1
206.25.192.0/19 e1 1
206.25.160.0/19 e1 1
206.25.224.0/19 e2 1
e1
e2
e3
e1
e2
206.25.192.0/19 1
206.25.160.0/19 1
206.25.224.0/19 1
206.25.192.0/19 e1 2
206.25.160.0/19 e1 2
206.25.224.0/19 e2 1
206.25.192.0/19 1
206.25.160.0/19 1
206.25.224.0/19 1
206.25.224.0/19 e2 1
206.25.224.0/19 e3 0